## Slide 1: STEM CELL RESEARCH & THERAPY

## Slide 2: STEM CELLS AND BIOMATERIALS
The science of biomaterials has evolved to direct cellular differentiation
Biomaterials can now be molded into 3-D scaffolds
Natural Scaffolds
Biodegradability & biologically active nature
Enhanced tissue growth & tissue integration on transplantation
Synthetic Scaffolds
Versatility, malleability, processability

## Slide 3: NANOSCALE PLATFORMS
Generating a substrate topography that mimics the in vivo microenvironment
Scaffold generating techniques:
Electrospinning
Soft Lithography
Microfluidics

## Slide 4: Electrospinning
Obtaining nanofibers mainly as scaffolds for tissues
Nanofibers of sub-microscale diameter are generated by ejecting electrically charged polymer solutions through a needle on to a grounded collector surface

## Slide 5: Applications
Tissue engineering, biosensors, filtration, wound dressings, drug delivery, and enzyme immobilization
- Poly-L-lactic acid (PLLA): Human tendon stem cells
- Poly-ε-caprolactone (PCL): Human bone marrow stromal cells
- Polylactic acid (PLA): Differentiating human mesenchymal stem cells
- PCL-gelatin: MSCs for myocardial regeneration
- Polylactic-co-glycolic acid (PLGA): Skin scaffolds

## Slide 6: Limitations
Possibility of cells squeezing into smaller pores
Limiting growth potential
Depends on polymer properties:
Viscosity
Surface tension
Conductivity
Diaelectric constant

## Slide 7: Soft Lithography
Customizing the spatial distribution of polymer molecules placed on the substrate to aid specific outcomes
Conditioned culture method for lineage specifity
3D polyglycolic acid (PGA)

## Slide 8: Limitations
Provides a limited and narrow range of ECM signals for the cells to perceive
Distortion in the fabrication of single-layer structures
Formation of a thin film of polymer under the nanometer-sized features
Integration of large and small features in phase shift lithography

## Slide 10
Microfluidic devices make an excellent platform to study cells under various micro environmental conditions
The capillary flow maintains a constant soluble microenvironment
Microfluidics

## Slide 11
Large surface area to volume ratio similar to biological systems
Used for high-throughput screening because of the capacity to culture a limited number of cells in a controlled manner
There are some main limitations of microfluidics in long-term stem cell cultures

## Slide 15
THANK YOU FOR LISTENING
Aycan Bulucu 15290146
Ece Görkemli 15290158
Esin Yiğit 15290196
Pelin Bölükbaş 15290145