## Slide 1: BIOETHANOL
Ethanol Production from Sugar and Starch Raw Materials

## Slide 2: Bioethanol producing microorganisms
Saccharomyces cerevisiae
Kluyveromyces marxianus
Pichia stipitis
Zymomonas mobilis
Escherichia coli
Klebsiella oxytoca
Candida sheaeta
Model organism, high ethanol production, ethanol resistance
Wide range of substrates
Ability to produce ethanol from pentoses such as xylose and arabinose
advantages

## Slide 3
Saccharomyces cerevisiae
This yeast is the universal microorganism used for ethanol production from starch and sugar raw materials.
Glucose, fructose, mannose, galactose, sucrose, maltose and maltotriose are the sugars metabolized by this yeast.

## Slide 4
Ethanol production by S. cerevisiae is through the glycolytic pathway.
In its simplest form, ethanol production from glucose:
C6H12O6+2Pi+2ADP 2C2H5OH+2CO2+2ATP+2H2O

## Slide 5
According to the above equation, theoretically 0.511 grams of ethanol is produced from 1 gram of glucose. But in practice this is not the case. Because;
Not all glucose is converted to ethanol. In addition, cell material synthesis, cell continuity, glycerol, acetic acid and so on. It is also used in the formation of by-products.
But under ideal conditions, 90-95% ethanol yield can be achieved.

## Slide 6
In industrial applications, a wide range of sugars are present. But yeast primarily consumes glucose and sucrose.
The presence of these two sugars represses the uptake and metabolisation of other sugars.

## Slide 7
Yeast needs Ca, Mg, Mn, Co, Fe, Cu, K, Na, Zn minerals for growth and ethanol fermentation.
Organic nutrients and other substances that are already present in industrial raw materials, improve ethanol production

## Slide 8
S. cerevisiae is inhibited from its own product, ethanol. The increase in ethanol disrupts the flowability and permeability of the cell membrane. Therefore, it causes loss of ions and small metabolites.
Ethanol inhibition can be prevented using Ca. However, it is important to optimize Ca concentration. Because the high Ca: Mg ratio negatively affects the growth and ethanol production by causing antogonism.

## Slide 9
Acetic and lactic acids may also cause inhibition in S. cerevisiae yeast. In ethanol fermentation, these are by-products and are synthesized in small amounts.
However, as it can accumulate on a large scale in industrial applications, it adversely affects growth and ethanol production.

## Slide 10
Oxygen plays an important role in S. cerevisiae metabolism. Ethanol inhibition is reduced in micro-aerobic conditions compared to anaerobic conditions. Ventilation conditions also affect the formation of by-products. For example, glycerol synthesis can be virtually eliminated.
However, if the amount of oxygen is too high, the cell will increase its biomass rather than produce ethanol.

## Slide 11
Zymomonas mobilis
Although not commercially available today, this bacterium is also very important in ethanol production.
It can produce ethanol faster than S. cerevisiae yeast.

## Slide 12
The most important difference of Z. mobilis and S. cerevisiae in glycolysis;is the presence or absence of the key enzyme (PFK).

## Slide 13
In yeast this enzyme is strictly regulated. But Z. mobilis does not have this enzyme. Therefore, ethanol production and energy production are independent of each other.
In other words, cell growth is not required for ethanol production, ie high cell concentration is not required for high ethanol yield.
Therefore, ethanol yield is very close to theoretical yield.

## Slide 14
Other advantages of Z. mobilis
High sugar uptake and ethanol production efficiency
High ethanol tolerance
No ventilation required for optimal ethanol production

## Slide 15
Disadvantages of using Z. mobilis
Formation of by-products
acetic acid: lactic acid = 16: 1, (by pH 4.5) Z. mobilis
acetic acid: lactic acid = 8: 1, (by pH 3) S. cerevisiae
No contamination problem, important in industrial production !!!!!

## Slide 16
Pichia stipitis
Very few yeast species can produce ethanol from xylose
Only 6 of the 200 yeast species tested in the laboratory produced ethanol more than 1 g / L. These;
Pichia stipitis, P. segobiensis, Candida shehatae, C. tenuis, Brettanomyces naardenensis, Pachysolen tannophilus.
Among these yeasts, only Pichia stipitis and Candida shehatae have xylanase activity.

## Slide 17
3C5H10O5 5CO2 + 5C2H5OH
According to the equation, 1 mole xylose consists of 1.67 mole ethanol.
Theoretically, the maximum ethanol yield is 0.51 ethanol per gram of xylose.

## Slide 18: Ethanol Production from Lignocellulosic Raw Materials
Lignocellulosic raw material consists of three main components: cellulose, hemicellulose, lignin
Cellulose and hemicellulose should be converted to fermentable sugars to be converted to ethanol.
These fermentable sugars are glucose, xylose, arabinose, galactose and mannose.
The hydrolysis of cellulose and hemicellulose to these sugars is by acid or enzyme use.