## Slide 1: Pretreatment of raw material
An ideal biomass pretreatment process should provide:
High hydrolysis and high yield fermentable sugar
Minimal degradation of carbohydrate fractions
No compound that will have inhibitory effect on microorganisms used in fermentation step
Requires cheap material
Moderate conditions for cost reduction
Recycling of used chemicals
Minimal waste generation

## Slide 2
Today, there is no single pre-treatment process that provides all these points.
All these points should be taken into consideration when selecting the pre-treatment method and the type of biomass to be used must be taken into consideration.
As a matter of fact, the pretreatment process that is suitable for one biomass may not be suitable for the other one.

## Slide 3
Concentrated Sulfuric Acid Hydrolysis
Hydrolysis of Dilute Sulfuric Acid
Steam Treatment
Treatment with ammonia
Treatment with cao
Treatment with Alkaline Peroxide
Wet Oxidation
Organosolv Separation Method
Concentrated Phosphoric Acid Treatment
Ionic Liquid Treatment

## Slide 4
Use of Enzymes in Hydrolysis Process
Cellulose glucose can be hydrolyzed using an enzyme complex called “cellulase..
Cellulase is secreted by some microorganisms that break down cellulose.
This enzyme complex consists of endo-β- (14) -glucanase (Cx-cellulase) and exo-β- (14) -glucanase (cellobiohydrolase).

## Slide 5
Cx cellulase breaks bonds in amorphous portions in the cellulose molecule. Sellobiohydrolase, on the other hand, removes cellobiosis from non-reducing ends.
The activity of these two enzymes together causes the breakdown of cellulose.
Another enzyme called sellobiase [β- (14) -glucosidase] is required for hydrolysis of cellobiose to glucose.
This enzyme is secreted by fungi and by some aerobic bacteria that develop on cellulose.

## Slide 6
Cellulase enzymes sold commercially have a small amount of cellobiase enzyme. However, if high glucose yield is desired, enzymatic hydrolysis of biomass should also include cellobiase.

## Slide 7
Enzyme hydrolysis of hemicellulose is more complex.
The complete degradation of this heterogeneous biopolymer is achieved by the co-operation of several hydrolytic enzymes.
These enzymes are called “hemicellulases..
They consist of endo-enzymes that break down internal glycoside bonds and exo-enzymes that remove sugars from non-reducing ends and esterases that attack non-glycosidic ester bonds.

## Slide 8
Commercially available cellulases also exhibit “hemicellulase” activity.
Due to their complex structure, they cannot be effectively hydrolyzed by all kinds of biomass “hemicellulase” enzymes (as in corn cobs).
The most appropriate strategy for converting maize structures into fermentable sugars is to use commercial cellulases to hydrolyse the cellulose remaining after treatment with dilute acid under moderate conditions.