## Slide 1: BIOBUTANOL PRODUCTION

## Slide 2: alcohols
Short chain | 
Methanol | CH3OH
Ethanol | C2H5OH
Propanol | C3H7OH
Long chain | 
Butanol | C4H9OH
Pentanol | C5H11OH
Hexanol | C6H13OH
Heptanol | C7H15OH
Octanol | C8H17OH
Compared to diesel fuels, long chain alcohols have higher performance than short chain alcohols.

## Slide 3: What is butanol?
4-carbon long chain primary alcohol.
n-butanol, tert-butanol and isobutanol are used as additives to gasoline.
It can be produced as a renewable energy source by fermentation from biological sources.
It is distinguished from other bioalcohols (bioethanol, biomethanol, etc.) produced by its many properties.

## Slide 4: Production and use of butanol in the world
İn the world
Synthetic
Petro-butanol
from fossil fuels;
From microorganisms and biomass
China
USA
Germany
Taiwan
Brazil
oxo pathway, is obtained by Propylenehydroformylation.

## Slide 5
Hydroformylation, also known as oxo synthesis or oxo process, is an industrial process for the production of aldehydes from alkenes. This chemical reaction requires the net addition of a formyl group (CHO) and a hydrogen atom to a carbon-carbon double bond.
Aldehydes are important because they are easily converted to many secondary products. For example, the resulting aldehydes may be hydrogenated to alcohols.

## Slide 6
Biobutanol can be used as an alternative renewable energy source;
Polysaccharides in biological raw materials such as sugar (sugar beet), starch (corn), lignocellulosic wastes (wheat straw) and microalgae (Chlorella sp.),
Decomposition to monomers by enzymes secreted by anaerobic Clostridium bacteria and
It is carried out by fermentation of the bacteria to acetone, butanol and ethanol.
Industrial production is currently limited.
It is shown in the literature that this situation can be solved by using metabolism engineering.

## Slide 7: Raw materials
corn
rice
molasses
Wheat straw
Corn bran
straw
Starch rich
lignocellulosic
microorganisms
Chlorella sp.
Dunaliella sp.

## Slide 8: Advantages of biobutanol
According to ethanol and methanol;
Very good mixing with diesel fuels
Lower evaporation temperature
High density
High flash point
Low auto ignition temperature
Low moisture absorption

## Slide 9: Microorganisms for butanol production
Clostridium acetobutylicum
Clostridium cellulolyticum
Clostridium beinjerinckii
They are gram-positive, obligate anaerobic bacteria that form endospores.
They can ferment polysaccharides such as pentose, hexose, starch, cellulose, hemicellulose.
It can produce enzymes such as α-amylase, β-amylase, β-glucosidase, and glycoamylase that break down polysaccharides to their monomers.
Fermentation products are butyric acid, acetic acid, butanol, acetone, ethanol.

## Slide 10
The production of fermentative biobutanol takes place in two phases by Clostridium sp.
acidogenesis
solventogenensis
These acids are then re-assimilated to produce ethanol and butanol during the solventogenic phase.
The cells grow in the acidogenic phase in which acetic and butyric acids are produced together with ATP.

## Slide 11: metabolism
biomass
6C sugars
5C sugars
Pentose phosphate
glycolysis
pyruvate
Butyric acid
Acetic acid
butanol
Ethanol
Butanol
aceton
Ethanol
Butanol
aceton

## Slide 12: butanol production steps
Lignocellulosic materials
Micro-macroalge based
Raw material
pretreatment
Acid pretreatment
Alcali treatment
Enzymatic hydrolysis
……
fermentation
Clostridium beijerinckii
C. acetobutylicum
C. saccharobutylicum
C. Cellulovorans
Microorganisms developed by metabolism engineering
product
Butanol
Ethanol
Aceton
ABE (acetone-butanol-ethanol) Fermentation
Fermentation takes place in two stages;
Acetic and butyric acid production stage (acidogenesis)
Conversion of acids to acetone, butanol and ethanol (solventogenesis) and CO2 and H2O are products