## Slide 1: BIODIESEL
Biodiesel is a type of fuel that consists mainly of fatty acid alkyl esters (FAAE) and is generally synthesized by transesterification reactions between triglycerides (vegetable, animal, waste or microbial lipids) and alcohol.
It is an alternative to fossil diesel.
Today, biodiesel fuel properties are determined according to ASTM D6751 in America and EN 14214 in European countries.

## Slide 2
Biodiesel is biodegradable, non-toxic and has a lower emission profile compared to petroleum diesel.
The use of biodiesel provides a balance between agriculture, economic development and the environment

## Slide 3
Although biodiesel cannot completely replace petroleum-based diesel fuels today, there are many reasons supporting its production:
creating a market for the production of vegetable and animal oils,
reduce countries' dependence on oil imports,
does not contribute to global warming thanks to its renewable property and closed carbon cycle,
reduced 78% of all CO2 emissions compared to oil-based diesel ,
carbon monoxide, unburned hydrocarbon and particulate emission output is lower than normal diesel fuel.
,
,

## Slide 4
Because of these properties, when biodiesel is added at a rate of 1-2% to normal diesel fuel, it can convert the fuel into acceptable fuel as with modern ultra-low sulfur diesel fuel with poor lubrication properties.
However, many emission tests of biodiesel show that nitrogen oxides are increased (in very small amounts)

## Slide 5
Cost of biodiesel (%)
Raw material 84
Chemicals 7
Water-electricty 4
Fixed Expenses 5
Vegetable oils
Microabial oils

## Slide 6: RAW MATERIALS
Vegetable oils
Animal fats
Waste oils
Microbial oils

## Slide 7
Vegatable oils
Although vegetable oils are used as a diesel fuel source in the 1930s and 1940s in emergency situations, and biodiesel is known only as methyl esters of vegetable oils, the most important feature of alternative fuel is that it is being «economical»

## Slide 8
The use of vegetable oils as fuel dates back to centuries before today.
The inventor of the diesel engine, Rudolf Diesel, used peanut oil for the first time in a compression ignition engine.

## Slide 9
However, since petroleum products are much cheaper today, such fuels have not been able to replace them.
Although vegetable oils stand out in the development of alternative fuels, many problems are encountered especially in direct injection machines.
At the beginning of these problems;
coking and injecting too much noise,
carbon residues, oil adhesion,
thickening and gelling and lubrication problems caused by vegetable oil contamination

## Slide 10
Other major disadvantages in the use of vegetable oils, especially animal fats, are the high viscosity, which is 11-17 times higher than that of diesel fuel, and the low volatility which causes residues in the engine. The cause of these problems is the large triacylglycerol molecule and its high molecular weight.

## Slide 11
Animal fats
The high production cost due to the fact that biodiesel is made from high quality, expensive vegetable oils can be reduced by the use of non-edible oils as raw materials.

## Slide 12
In the literature, tallow oil and chicken residues are the main raw materials for the use of animal fat in biodiesel production
Animal oils, especially tallow oil, vary depending on the nutritional habits of people, and the soap industry cannot receive all of the animal fat produced.

## Slide 13
These oils consist of saturated fatty acids such as C14: 0, C16: 0 and C18: 0, which have a high cetane number and are less susceptible to oxidation than unsaturated oils.
However, it is an important disadvantage that this property tends to crystallize at high temperatures.

## Slide 14
Waste oils
Today, the rapid increase in vegetable oil prices requires finding alternative solutions in biodiesel production such as the use of waste oils such as frying oils instead of cooking oils.