## Slide 2
The use of vegetable oils as raw materials makes the price of biodiesel 1.5 times more expensive than oil-based diesel.
However, the price of waste frying oils is 2-3 times cheaper than vegetable oils. Moreover, the similar quality of biodiesel produced from waste frying oils and vegetable oils is an appropriate material for the evaluation of these oils.

## Slide 3
Vegetable oils are exposed to very high temperatures during food frying. Hydrolysis, polymerization and oxidation occur and both the chemical and physical structure of the oil are destroyed.
Due to the hydrolysis of triacylglycerol in the presence of moisture and oxidation, the amount of free fatty acid in the oil increases. The free fatty acid and water content have a negative effect on the transesterification reaction. It also prevents the separation of fatty acid esters and glycerol.

## Slide 4
The formation of dimeric and polymeric acids and glycerides in frying oils significantly increases the viscosity of the oil. Thus, as the molecular mass and iodine values ​​decrease, the saponification value and density increases. This prevents direct transesterification of the biodiesel.
It is therefore necessary to reduce the free fatty acid content with an acidic catalyst. Both waste oils and animal fats have high saturation rates. Therefore, cold flow properties of biodiesel produced from these oils should be considered.

## Slide 5
In order to replace petroleum based fuels, biodiesel must be produced on a commercial scale, cheaper than petroleum based fuels, and must meet the same standards as the fuels we use today in terms of combustion quality. Some of the studies conducted for this purpose have suggested the idea of ​​obtaining biodiesel from microbial lipids.

## Slide 6
Microorganisms compared to plants;
contain more lipids,
easier development processes,
are not affected by changing seasons and climatic conditions
They are more advantageous in biodiesel production because they can be produced in large quantities in a short time.
Microbial Lipids

## Slide 7
Bacteria
Bacteria generally do not produce triacylglycerol, but instead store polybutyl hydroxybutyrate and alkanoate.
However, many bacteria are usually not lipid producers. Only a few bacterial species can accumulate mixed lipoid structures (polyhydroxyalkanoate) in their cells. These structures are very difficult to extract because they are in the outer membrane.
Therefore, the use of bacteria with high lipid content as raw material in biodiesel production has no commercial significance.
Therefore, lipid accumulation feature is seen only in some yeast, fungi and algae.
Usage of microbial lipids in biodiesel production

## Slide 8
Fungi
Since the 1980s, fungi (unicellular yeasts and filamentous fungi) have been interesting oleaginous microorganisms.
Rhodosporidium sp., Rhodotorula sp, and Lypomyces sp. Some yeast species such as yeast have the ability to accumulate lipid up to 70% of their dry weight.
Examples of fungi with high lipid content include Mortierella sp. species belonging to the genus can be given.
Fatty yeasts and molds accumulate triacylglycerol rich in polyunsaturated fatty acids. The most common fatty acids in these cells are C18: 1, C18: 2, C16: 0, C16: 1.

## Slide 9
Microalgae and Cyanobacteria
It is sometimes used in food and chemical production.
But in recent years, their use as an energy source is in high demand.
These microorganisms may be degraded for methane production, produce photosynthetically hydrogen, or some algae may be used as oil sources in the production of liquid fuel.

## Slide 10
Easy to cultivate
Cheap growth medium
Reduce the greenhouse gas effect by CO2 fixation
Photosynthetic microorganisms
Easy to obtain, high oil content
Compared to plants, they can grow in ponds, fermentation units and even waste water (no need agricultural areas and forests)
Microalgae are extremely rich in carbohydrate, protein and especially fatty acid content

## Slide 11
The most important advantage of microalgae is that they do not need a carbon source because they can grow photosynthetically and they use carbon dioxide, which is the product of previous consumption, as an energy source and provide carbon dioxide neutralization.
Lipids deposited by microalgae are generally in the form of triacylglycerol (> 80%) and contain fatty acids rich in carbon atoms 16 and 18.
Although the average lipid content of algae cells varies from 1% to 70%, there are microalgae capable of accumulating 90% lipid when optimum conditions are achieved.

## Slide 12
Compared to the agricultural raw materials used for biodiesel production, it is thought that the separation of arable fields for biodiesel production by using microalgae as a raw material in biodiesel production is considerably reduced because they need 49 times smaller area than rapeseed area and 132 times smaller than soybean area.

## Slide 13
It has been reported that some algae and cyanobacteria species have high lipid content and under optimum conditions these photosynthetic microorganisms can produce 100 times more lipid than the plant system grown in the same area.
The researchers stated that the biodiesel produced from algae does not contain sulfur and can perform like diesel fuels with petroleum, particle, CO, hydrocarbon and SOx emissions are low, but NOx emission may be higher in some engine types.