## Slide 1: Microalgal lipids,
Chemically similar to vegetable oils
Triglycerides make up a significant portion of lipid content

## Slide 2: In which cases microalgae accumulate lipid ???
Usually 20-50% of the dry biomass weight is lipid. In some cases it is 80%.
In case of excessive photosynthesis
Heterotroph conditions
Under stress conditions
(nutrient deficiency (N, P), salt, heavy metal stress, etc.)

## Slide 3
Lipid extraction
Usually, Bligh & Dyer, 1959 method
Chloroform and methanol extraction
Soxhlet is also common

## Slide 4
Chemical Modifications to Triacylglycerols
Vegetable oils generally include free fatty acids, phospholipids, sterols, water, odorants and other compounds.
Therefore, oil cannot be used as a direct fuel. Vegetable oils have a viscosity of 10-20 times higher than a diesel fuel.

## Slide 5
The high viscosity, low volatility and polyunsaturated structure of triacylglycerols used in place of diesel fuels cause some problems during their usage.

## Slide 6
Chemical modifications to solve such problems are;
dilution,
micro-emulsification,
pyrolysis and
Transesterification