## Slide 1
METHANE PRODUCTION

## Slide 2
Animal manure, household waste and food processing wastewater have been treated in different ways for many years.
Anaerobic digestion reduces the organic matter content in the waste, undergoes organic carbon conversion, and releases biogas, mainly methane and carbon dioxide.

## Slide 3: Microbiology of methane production
Methanogenic environments
Microbiological methane production is observed in the gastrointestinal tract of non-ruminant animals, anaerobic digestion of domestic and animal wastes and in environments such as fresh water or marine sediments.

## Slide 4
At the end of the 1770s, the Italian physicist Alessandro Volta (known as the inventor of the first battery) carried out some experiments which he called «flammable air». Volta collected gas bubbles from the sediment of a shallow lake and described the combustion properties of the gas.
His early experiments led to an understanding of metanogenesis in the future.
A methanogenic archae was named in his honor. (Methanococcus voltae)

## Slide 5
The production of methane requires “anaerobic conditions», which lack inorganic terminal electron acceptors such as oxygen, nitrate, iron, sulfate.
In the case of any of the above-mentioned electron receptors in the microbial community, the electrons will flow to these receptors, reducing or completely stopping the metanogenesis.
In such a case, further reduced products are formed. For example, nitrogen gas if nitrate or hydrogen sulfide if sulphate.

## Slide 6
Metabolically diverse bacteria and archae can produce methane.
This process, in which methane and carbon dioxide are produced, consists of a series of successive interconnected reactions.
The end product of one group of microorganisms may be the substrate for another group.

## Slide 7
Methane production from complex organic compounds in biomass or waste consists of 4 main steps.
Hydrolysis
Fermentation (acidogenesis)
Asetogenesis
methanogenesis

## Slide 8
Biomass Resources for Methane Production
Municipal and animal wastes and wastewaters
Municipal solid waste
Food and vegetable waste
Agricultural by-products