## Slide 1: PACKAGING of fresh fruits and vegetables
Instructor
Assist. Prof. Dr. Eda Demirok Soncu
E-mail: edemirok@eng.ankara.edu.tr
Phone: +90312 203 3300 (3639 ext.)
Office: 2nd floor #212
Fde 216 food packagıng

## Slide 2: WHAT ARE QUALITY CHANGES ?

## Slide 3: Quality changes in fresh fruits and vegetables

## Slide 4: 1) Sensory attributes
Texture, flavor, odor, color, and visual development of fresh fruits and vegatables change in time.
For example (changes regarding texture);
    Softening of fresh produce is due to the solubilization and depolymerization of pectins by the action of pectinolytic enzymes
    Dehydration of produce can lead to a soft texture and wilt surface

## Slide 5: 1) Sensory attributes
For example (changes regarding flavor);
    Starch degradation and decarboxylation of organic acids induce modification of flavor, where the ratio between sweetness and acidity is important
For example (changes regarding color);
    Change in color is attributed to the degradation of color compounds or enzymatic browning
Decarboxylation means removal or elimination of carboxyl group (-COOH) from a molecule

## Slide 6: 2) Safety concerns (Microbial spoilage)
Spoilage microorganisms are involved in product degradation but generally do not directly affect human health
Fungi mycotoxin is an exception. Mycotoxin is toxic compound that produce by fungi
Although fruits have generally been considered safe from pathogens, some might be found sporadically in vegetables (for example Clostridium botulinum in vegetables. It is a pathogenic microorganism and responsible from food poisoning)

## Slide 7: FACTORS AFFECTING QUALITY FACTORS

## Slide 8: What are the factors that affect quality changes?
Factors that affect previously mentioned quality changes in fresh fruits and vegetables are listed below
    Respiration and ripening
    Dehydration
    Temperature effect
    Gas composition effect

## Slide 9: 1) Respiration and ripening
Once fruits and vegetables are harvested, they have to draw on their own reserves to achieve aerobic respiration and maintain their cellular integrity
During respiration, stored carbohydrates are broken down into glucose, which is oxidized into CO2, water, and energy via several enzymatic steps.
As soon as these substrates become unavailable, other carbonated resources (protein or lipids) are used, leading to the death of the harvested product

## Slide 10: 1) Respiration and ripening
Thus, the potential shelf life of fruits and vegetables is closely related to their respiration rate
The lower the respiration rate, the longer the potential shelf life
For climacteric fruits (peaches, apples, kiwis, etc…), an increase in respiration is associated with an increase in ethylene. During the biosynthesis of ethylene, the produce ripens and several biochemical and structural changes occur, such as softening due to the degradation of pectins or internal browning caused by the enzymatic oxidation of phenolic compounds

## Slide 11: 2) Dehydration
In association with aerobic respiration, moisture vapor is produced and natural dehydration occurs, caused by diffusion of moisture vapor from the high-concentration compartments in fresh product to the low concentration in the surrounding environment
Fruits and vegetables contain over 90% water. Loss of 5% or more water is visually noticeable, lowering the grade of the product and resulting in a decrease in its commercial value

## Slide 12: 2) Dehydration
Major effects of water loss are
    reduction in weight
    wilted appearance
    reduction in nutritional value as the amount of water-soluble components decreases when water is released
    loss in aroma and flavor
    enhanced sensitivity to chilling injuries

## Slide 13: 3) Temperature effect
Temperature is one of the major factors affecting shelf life of fresh produce. Chill temperatures slow down the rate of deteriorative reactions
Respiration of raw fruits and vegetables increases 2- to 3-fold for every 10°C rise in temperature
The rate of enzymatic reactions and respiration is reduced by decreasing temperature
Therefore it needs to be positively controlled during handling and marketing

## Slide 14: 4) Gas composition effect
Gas composition is an important factor to control respiration
Usually, lowering the O2 level is really effective in reducing respiration, but anoxia (a switch to anaerobic catabolism and growth of anaerobic flora that produce undesirable off-flavors and off-odors) should be avoided

## Slide 15: 4) Gas composition effect
High CO2 levels (more than 10%) might also reduce the respiration in onions, strawberries, or cucumbers and can limit the production of ethylene as observed in kiwifruit
High CO2 levels induce a bacteriostatic effect on aerobic bacteria but might lead to the development of anaerobic flora
On the other side, each fruit or vegetables has its own tolerance limit for CO2. High CO2 can lead to formation of some visual degradations (such as brown spots in lettuce or yellow color formation in mushrooms)

## Slide 16: 4) Gas composition effect
In brief, critical concentrations of O2 and CO2 exist for each fruit or vegetable
Therefore, optimal combination of O2 and CO2 should be applied to each fruit or vegetable

## Slide 17
WHICH TYPE OF PACKAGING SYSTEM SHOULD BE USED FOR FRESH FRUITS AND VEGETABLES?

## Slide 18: Packaging systems for fresh fruits and vegetables
The two packaging system given below can be used for fresh fruits and vegetables to extend their shelf life and preserve their quality
    Modified atmosphere packaging (MAP): Only gas or vapor permeation properties of the material is important
    Active modified atmosphere packaging (MAP)
    Edible packaging, which is a coating of products with waxes to increase the natural barrier properties of fruit and vegetables

## Slide 19: Active MAP
Plastic packaging material used | Plastic films for lidding Plastic trays or foams
Barrier properties of packaging material | It is essential to carefully select a film with suitable gas and vapor permeabilities. Most synthetic polymer films exhibit too low permeability to gases and vapors; therefore, films should be perforated (micro-holes) to allow sufficient gas exchange ---Packaging material should have O2 and CO2 permeability for respiration ---Packaging material should have water vapor permeability. Excess moisture, occured as a result of transpiration, should be removed to prevent condensation. On the other side, moisture intake is desirable to prevent drying ---Packaging material should have ethylene permeability for maturation

## Slide 20: Active MAP
What should be done to extend the shelf life under this packaging condition? | ---Controlled release of antimicrobial agents, which are incorporated into packaging film, can be used to control microbial growth ---Ethylene scavengers can be used to delay ripening of climacteric fruits ---Undesirable gas or vapors should be absorbed by active agents (such as oxygen scavengers, CO2 absorbers, moisture absorbers….)

## Slide 21
Schematic demonstration of active MAP

## Slide 22: Example for active MAP

## Slide 23: PACKAGING of pasteurized milk
Instructor
Assist. Prof. Dr. Eda Demirok Soncu
E-mail: edemirok@eng.ankara.edu.tr
Phone: +90312 203 3300 (3639 ext.)
Office: 2nd floor #212
Fde 216 food packagıng

## Slide 24: Attributes of pasteurized milk
Pasteurization is a heat treatment which applies for a definite time and to a specific temperature
Pasteurization is applied to milk to destroy all vegetative and pathogenic microorganisms and nearly all other bacteria without significantly altering the flavor or composition of the product
It also kills all the yeasts and molds that might be present in the product

## Slide 25: QUALITY CHANGES IN PASTEURIZED MILK

## Slide 26: Deteriorative reactions in pasteurized milk
Quality changes in pasteurized milk can be listed in one of four titles
  Light-induced oxidation
  Oxidation of milk fat (Lipid peroxidation)
  Microbial activity
  Pick-up of odor compounds at any stage of production and processing or interaction with the packaging material resulting in product flavor deterioration

## Slide 27: 1) Light-induced oxidation
This reaction results in off-flavor formation. For example;
Degradation of sulfur-containing amino acids (methionine), which develops during the first 2–3 days of storage
Light-induced oxidation of lipids is responsible from metallic off-flavor
Destruction of light-sensitive vitamins (mainly riboflavin and vitamin A) in the case of light exposure, especially at wavelengths below 500 nm

## Slide 28: 2) Oxidation of milk fat
Lipid peroxidation in considered to be the main chemical defect in pasteurized milk
Unsaturated fatty acids are attacked by free radicals, which is followed by the addition of O2 to form peroxides or hydroperoxides
Lipid peroxidation results in off-flavor development

## Slide 29: 3) Microbial activity
Microbiological changes involve growth of psychrotrophic bacteria as a result of either inadequate pasteurization or postpasteurization contamination
It leads to the formation of microbial flavor described as acidic, bitter, fruity, malty, putrid, or unclean
Additionally, some pathogenic microorganisms, which are contaminated to milk after pasteurization, can grow in pasteurized milk

## Slide 30
WHICH TYPE OF PACKAGING SYSTEM SHOULD BE USED FOR PASTEURIZED MILK?

## Slide 31: General requirements of packaging material?
Packaging material should have the common attributes given below to protect the quality of pasteurized milk
  It is able to protect the milk from light, O2, and microbial cross-contamination
  It also protects the product from loss of desirable flavor compounds or pick-up of undesirable odors
  Other requirements including recyclability or reuse, tamper evidence, nontoxicity, aesthetics, machinability, and functionality in terms of shape, size, and disposability

## Slide 32: Packaging materials used for pasteurized milk
Packaging materials used for pasteurized milk are listed as follow
    Glass
    Plastic containers
      High Density Polyethylene Bottles (HDPE)
      Poly(ethylene Terephthalate) Bottles (PET)
      Polycarbonate Bottles (PC)
      Linear Low Density Polyethylene/Low Density Polyethylene Pouches (LLDPE / LDPE)
      Paperboard Laminate Cartons

## Slide 33: Packaging materials used for pasteurized milk
GLASS | ---It is inert material --- It provides ultimate protection from O2, moisture, and microorganisms ---When it is colored appropriately (blue, amber, green, and, to a lesser degree, white), glass can protect milk from harmful UV light ---Sealing of glass bottles for milk packaging is usually achieved with aluminum foil caps ---Most glass bottles are returnable ---Major disadvantages of glass are its fragility and weight

## Slide 34: Packaging materials used for pasteurized milk
HDPE bottles | ---HDPE bottles transmit 58–79% of the incident light ---To improve this property, HDPE bottles are pigmented with TiO2 , producing an opaque bottle
PET bottles | ---They are superior to HDPE bottles in terms of their mechanical and optical properties, their lower flavor scalping potential, and substantially lower gas permeability ---Due to the almost complete transparency of PET to light, milk bottles are either labeled or, even better, sleeved using thermoshrinkable polypropylene (PP) labels ---Today most PET bottles are sealed with rigid PP screw caps

## Slide 35: Packaging materials used for pasteurized milk
PC bottles | ---PC bottles have a high temperature resistance and high impact strength and clarity ---They are currently used for multiuse baby bottles ---PC bottles are lightweight, clear, and are recyclable
LLDPE/LDPE bottles | ---Pillow-shaped pouches (also referred to as sachets) for milk are produced by feeding a linear LDPE ---A disadvantage of the pouch is that it cannot be reclosed, thus exposing the milk to odor absorption in the refrigerator ---The pouch material should be pigmented to reduce light transmission

## Slide 36: Packaging materials used for pasteurized milk
Paperboard laminate cartons | ---Paperboard laminate cartons are multilayer containers ---The paperboard is coated with LDPE on both sides ---The external LDPE coating is used to provide protection from moisture and indirectly for mechanical integrity ---The internal LDPE coating is used to prevent interaction of milk with the paperboard and to provide effective heat sealing

## Slide 37: Packaging materials used for pasteurized milk
PET bottles
PC bottles
HDPE bottles
Paperboard laminated carton bottles
LLDPE/LDPE pouches

## Slide 38: References
Robertson, G.L. (2010). Packaging and the shelf life of fruits and vegetables (Chapter 16 pages 297-310) In Food Packaging and Shelf Life: A Practical Guide. CRC Press Taylor&Francis Group
Robertson, G.L. (2010). Packaging and the shelf life of milk (Chapter 5 pages 82-99) In Food Packaging and Shelf Life: A Practical Guide. CRC Press Taylor&Francis Group