## Slide 1: BLOOD TESTS

## Slide 2: Blood count is carried out to learn the number of shaped elements (erythrocyte, leukocyte, platelet) in 1 mm3 of blood. It is a useful test for the diagnosis of diseases such as anemia, infections, leukemia.

## Slide 3
Adult males have an average of 5,400,000 / mm3 blood (4,600,000-6,200,000) and adult females have an average of 4,800,000 / mm3 blood (4,200,000-5,400,000) erythrocytes.

## Slide 4
Normal mean values for leukocytes are 5,000-10,000 / mm3 blood. Blood platelets are 200,000-300,000 / mm3.

## Slide 5
In addition to erythrocyte, leukocyte and platelet counts, hemoglobin and hemotocrit measurements are also very important tests in order to provide information about the presence of any pathological condition in the organism.
Normal mean values for hemoglobin are 16 g / 100 ml of blood in adult males; 14.4 g / 100 ml of blood in adult women.
Hematocrit is the expression of the ratio of the volume of erythrocytes to the entire volume of blood. Normal values are 42-52% (47%) in adult males and 36-46% (42%) in adult females.

## Slide 6
Hematocrit is % expression of the ratio of erythrocytes volume to whole blood volume.
Tissue oxygenation should theoretically increase with increasing hematocrit. However, increased hematocrit also increases the visible blood viscosity, which reduces the flow of blood through the microvasculature and thus reduces tissue oxygenation. A hematocrit value where these two contrasting effects balance each other represents the optimal hematocrit that maximizes tissue oxygenation.

## Slide 7
When erythrocyte, hemoglobin and hematocrit increase (polycythemia);
  life in high places,
  pick-wick syndrome,
  diuretic therapy
Conditions where erythrocyte, hemoglobin and hematocrit decrease (anemia and oligocyemia);
  Erythrocyte production disorders,
  erythrocyte destruction increased

## Slide 8
When leukocytes are increased (leukocytosis);
  acute and local inflammations
  burns
  Tuberculosis
When leukocytes are reduced (leukopenia);
  aplastic anemia,
  myelosikleroz,
  anaphylactic shock,

## Slide 9: Erythrocyte count in blood
The finger to be blood is punctured and the blood is diluted with erythrocyte dilution solution (1/100 ratio) and blood is spreaded on lamella and covered with the coverslip.
At least 16 of the squares (1/20 mm of the edge) where the erythrocyte count is made are counted, averaged and multiplied by 400.000.
Because;
Volume of square= 1/20 x 1/20 x 1/10
Dilution ratio = 1/100
1/20 x 1/20 x 1/10 x 1/100 = 1/400.000 mm3 blood
1/400.000 mm3 blood A erytrocyte
1 mm3 blood X erytrocyte
A x 1
X=--------------- X= A x 400.000
1/400.000

## Slide 10: Leukocyte count in blood
The finger to be blood is punctured and the blood is diluted with leukocyte dilution solution (1/100 ratio)and blood is spreaded on lamella and covered with the coverslip.
At least 10 of the squares (1/5 mm of the edge) where the erythrocyte count is made are counted, averaged and multiplied by 2500.
Because;
Volume of square= 1/5 x 1/5 x 1/10
Dilution ratio = 1/10
1/5 x 1/5 x 1/10 x 1/10 = 1/2.500 mm3 blood
1/2.500 mm3 blood A leukocyte
1 mm3 blood X leukocyte
A x 1 X= ----------------- X= A x 2.500 olur.
1/2.500

## Slide 11: Hemoglobin analysis by sahli method
Aim: To determine the amount of hemoglobin in erythrocytes in 100 cc blood. In Sahli method, the hemoglobin is converted to acid hematine and colorimetric quantification is performed.
Material: Steril needle
Alcohol
Sahli Hemoglobinometer Sahli pipette
0.1 N HCl

## Slide 12: Experimental Procedure:
1. 0.1 N HCl is placed in the empty hemometer tube up to 10.
2. Blood is taken from the pierced fingertip and added on acid.
3. The tube is shaken and waited for 1-10 minutes after the acid and blood are mixed together.
4. Then distilled water is added dropwise and after each drop, the tube contents are mixed. This process is continued until the standard color on the hemometer and the color on the graduated hemometer tube are the same.
5. In the end, the tube in which the blood is examined is read from the scale on it, the amount of hemoglobin in % or g.

## Slide 13: Hematocrit assay
Material: Heparinize capillary tube
Centrifuge suitable for capillary tube
Alcohol
Steril needle
Plastic hematocrit scale
The oxygen flow in animals can change by a change in theerythrocyte-to-blood volume ratio. This ratio is called hematocri

## Slide 14: Experimental Procedure:
The heparinized capillary tube is filled completely the blood on the pierced finger tip.
One end of the tube is closed and placed in the special centrifuge. It is centrifuged.
At the end of this period are moved on the plastic hematocrit scale until the lower limit of the erythrocyte volume and the upper limit of the serum volume reach the two thick lines. The number it corresponds to on the scale is determined as% hematocrit.

## Slide 15: References
Biochemistry practice book (2004)
Piety NZ, Reinhart WH, Stutz J, Shevkoplyas SS. Optimal hematocrit in an artificial microvascular network. Transfusion. 2017 Sep;57(9):2257-2266. doi: 10.1111/trf.14213. Epub 2017 Jul 5. PMID: 28681482; PMCID: PMC5583001.
Stark, H., & Schuster, S. (2012). Comparison of various approaches to calculating the optimal hematocrit in vertebrates. Journal of Applied Physiology, 113(3), 355–367. https://doi.org/10.1152/japplphysiol.00369.2012.