## Slide 1: Bellek ve Programlanabilir Mantık (Memory and Programmable Logic)
Bölüm 7
Mano & Ciletti kitabından ve Suleyman TOSUN’un slaytlarından Türkçeleştiren Kurtuluş KÜLLÜ

## Slide 2: Konular
RAM
Bellek kod çözme (Memory decoding)
Hata saptama ve düzeltme (Error detection and correction)
ROM
Programlanabilir Mantık Dizisi (Programmable Logic Array (PLA))
Programlanabilir Dizi Mantığı (Programmable Array Logic (PAL))

## Slide 3: Bellekler
Bir bellek birimi yüksek miktarda ikili (binary) bilgi depolayabilen hücrelerden oluşur.
  Giriş cihazlarından gelen bilgi bellekte depolanır
  Çıktıya giden bilgi bellekten alınır
Belleklerin iki türü
  Rasgele erişimli bellek (Random-access memory (RAM))
    Daha sonra kullanılması için ikili bilgiyi depolar
    Yazma (Write) işlemi: Veriyi belleğe depolamak
    Okuma (Read) işlemi: Bellekten veriyi dışarı aktarmak
  Salt okunur bellek (Read-only memory (ROM))
    Yalnızca okuma işlemi gerçekleştirebilir

## Slide 4: RAM vs ROM
ROM bir programlanabilir mantık cihazıdır (programmable logic device (PLD)).
  İkili bilgi donanımın içine gömülüdür.
Diğer programlanabilir cihazlar
  Programlanabilir mantık dizisi (Programmable logic array (PLA))
  Programlanabilir dizi mantığı (Programmable array logic (PAL))
  Alanda programlanabilir kapı dizileri (Field programmable gate array (FPGA))
PLD’lerde çok kapı ve bağlantı olduğu için dizi mantığındaki kapılar biraz farklı gösterilir.

## Slide 5: Rasgele Erişimli Bellek (Random-Access Memory (RAM))
Herhangi rasgele konuma veya o konumdan aktarım yapma süresi hep aynıdır
  Bu sebeple rasgele erişimli olarak adlandırılmıştır.
  Manyetik bantlarda (tapes) bu zaman verinin konumuna göre değişir.

## Slide 6: Kelime Boyutu (Word Size)
4 bit - nibble
8 bit - byte
16 bit – 2 byte
32 bit – 4 byte
Çoğu bilgisayar 8 bitin katlarını kullanır
Bir belleğin kapasitesi toplam byte sayısı olarak verilir.

## Slide 7: Bir bellek birimi
Bellek ve çevresi arasındaki iletişim aşağıdakilerle sağlanır
  Veri giriş ve çıkış hatları
  Adres seçim hatları
  Kontrol hatları

## Slide 8: Adres
Her kelime bir adrese atanır
  Adres hatlarının sayısı k ise 0 ile 2k-1 aralığında adresler vardır
İçeride bir kod çözücü (decoder) belirli bir kelime için verilen adresi çözümler.
Bellek boyutu ve adres hatları
  10 bit (k=10), 210 kelimeyi adresleyebilir
  32 bit, 232 kelimeyi

## Slide 9: Bellek Adresleme
Her biri 16 bit olan 1024(=2^10) kelimelik bir bellek

## Slide 10: Okuma ve Yazma İşlemleri
Veriyi okumak için
  İkili adresi adres hatlarına verin
  Oku (read) girdisini aktifleştirin
Veri yazmak için
  İkili adresi adres hatlarına verin
  Veri girdi hatlarına veri gönderin
  Yaz (write) girdisini aktifleştirin

## Slide 11: Bellek Türleri
Static RAM (SRAM)
  Consists of latches to store binary data
  Stored data is valid as long as power is applied
  Easier to use
  Shorter write and read cycles
Dynamic RAM (DRAM)
  Stores data in the form of electric charges on capacitors (MOS transistors).
  It must be refreshed periodically.
  Has less power consumption
  Larger storage capacity.

## Slide 12: Volatile vs Nonvolatile
SRAMs and DRAMs are volatile memories
  Since they loose data when power is turned off
Magnetic disks are nonvolatile
  They store data using magnetization.

## Slide 13: Memory Decoding
Decoders are used to select word locations.
A memory with m words and n bits per word requires mxn storage cells.
A basic cell is behaves like D latch (4 to 6 transistors)
  When read/write=1, read operation
  When read/write=0, write operation

## Slide 14: 4x4 RAM
4 words needs 2 address lines to be decoded
2k words needs k address lines

## Slide 15: Coincident decoding
A decoder with k inputs and 2k output requires 2k AND gates with k inputs per gate.
  Use two decoders to reduce this (two dimensional decoding)
  Two decoders with k/2 inputs
2x32=64 AND gates instead of 1024 AND gates (for 10 bits)
32x32 memory cell array

## Slide 16: Error Detection and Correction
Error detection
  Use parity bits
Error correction
  Use multiple parity bits
  Each parity is generated for a group of bits
  If check parity bits are correct
    No error
  If check bit/bits are not correct
    They give a pattern (called syndrome) that gives which bit is incorrect.

## Slide 17: Hamming Code
K parity bits are added to n bit data
  Bit positions are numbered from 1 to n+k (no 0)
  Parity bits are positioned as powers of 2.
  Remaining bits are data bits.
Example: data word is 11000100 (8 bit)

## Slide 18: Parity generation

## Slide 19: Parity check
C=C8C4C2C1
If C=0, no error
If C!=0, error (C gives the erroneous bit position)

## Slide 20: Single error correction, Double error detection
Add additional parity bit (P13)

## Slide 21: ROM
Only read occurs
K inputs and n outputs
Nonvolatile

## Slide 22: 32x8 bit ROM
32 words of 8 bits each.
2kxn ROM has kx2k decoder and n OR gates

## Slide 23: Combinational Circuit Implementation
Similar to design procedure of circuits with decoders and OR gates as we have seen in Chapter 4.
  We have decoders and OR gates inside of the ROM.

## Slide 24: Types of ROMs
ROM-mask programming
  Fill out the truth table, manufacturer makes the mask to produce 0’s and 1’s.
PROM (programmable ROM)
  Can be programmed in a lab by blowing the fuses (all fuses initially intact)
EPROM (Erasable PROM)
  Program it then erase under ultraviolet light.
EEPROM or E2PROM(Electrically erasable PROM)
  Can be programmed and erased electrically.

## Slide 25: Combinational PLDs

## Slide 26: Programmable Logic Array
Similar to PROMS except that decoder is replaced with AND gates.
AND gates are connected to OR gates to produce sum-of-product terms.

## Slide 27: An example PLA circuit
F1=AB’+AC+A’BC’
F2=(AC+BC)’

## Slide 28: Fuse Map
- means not connected, 1 means connected, 0 means complement is connected.
T means true (for XOR)
C means complement (for XOR)

## Slide 29: Programmable Array Logic (PAL)
Fixed OR array and programmable AND array.
Figure shows 4 input 4 output PAL

## Slide 30: Sequential Programmable Devices
Needs flip-flops
Types