## Slide 1: Digital Systems and Binary Numbers
Based on book by Mano & Ciletti
Chapter 1
Adapted from slides by Suleyman TOSUN

## Slide 2: Outline
Digital Systems
Binary Numbers
Number-Base Conversions
Octal and Hexadecimal Numbers
Complements
Signed Binary Numbers
Binary Codes
Binary Storage and Registers
Binary Logic

## Slide 3: Digital Systems
Digital computer is the best-known example of a digital system
Others are telephone switching exchanges, digital voltmeters, digital calculators, etc.
A digital system manipulates discrete elements of information
Discrete elements: electric impulses, decimal digits, letters of an alphabet, any other set of meaningful symbols

## Slide 4: Digital Systems
In a digital system, discrete elements of information are represented by signals
Electrical signals (voltages & currents) are the most common
Present day systems have only two discrete values (binary)
Alternative, many-valued circuits are less reliable
A lot of information is already discrete and continuous values can be quantized (sampled)

## Slide 5: Binary Numbers
7392 represents a quantity that is equal to
Decimal number system is of base (or radix) 10
In binary system, possible values are 0 and 1 and each digit is multiplied by
E.g. 11010.11 is

## Slide 6: Binary Numbers
Hexadecimal (base 16) numbers use digits 0-9 and letters A, B, C, D, E, F to represent values 10-15
Operations work similarly in all bases

## Slide 7: Number-Base Conversions
Converting a number from base x to decimal is simple (as shown before)
Decimal to base x is easier if number is separated into integer and fraction parts
Convert 41 to binary
  Divide 41 by 2, quotient is 20 and remainder is 1. Continue dividing the quotient until it becomes 0. Remainders give us the binary number as follows:

## Slide 8: Number-Base Conversions
Conversion of a fraction is similar but the number is multiplied by to instead of dividing

## Slide 9: Octal and Hexadecimal Numbers
Conversions between binary, octal and hexadecimal numbers are easier
Each octal digit corresponds to 3 binary digits and each hexadecimal digit corresponds to 4 binary digits

## Slide 10: Complements
Simplifies
  the subtraction operation
  Logical operations
Two types exist
  The radix complement (r’s complement)
    10’s complement, 2’s complement
  The diminished radix complement ((r-1)’s complement)
    9’s complement, 1’s complement

## Slide 11: 1’s complement
For binary numbers, r=2 and r-1=1.
1’s complement of N is (2n-1)-N
If n=4, 2n=10000. So, 2n-1=1111.
To determine the 1’s complement of a number, subtract each digit from 1.
Or, bit flip!!! Replace 0’s with 1’s, 1’s with 0’s!!!
Example:
  If N= 1011000, 1’s comp.= 0100111
  If N= 010110, 1’s comp.= 101001

## Slide 12: 2’s complement
For binary numbers, r=2, 2’s complement of N is 2n-N
To determine the 2’s complement of a number, determine 1’s complement and add 1 to it.
Example:
  If N= 1011001, 1’s comp.= 0100110, 2’s comp.=0100111
  If N= 1101100, 2’s comp.= 0010100
Another way of finding 2’s comp.: Leave all least significant 0’s and the first 1 unchanged, bit flip the remaning digits.

## Slide 13: Subtraction with Complements
Minuend: 101101
Subtrahend: 100111
Difference: 000110
Add the minuend M to r’s complement of the subtrahend N.
M + (rn-N) = M - N+rn
If M>=N, the sum will produce an end carry. Discard it and what is left is the result M-N.
If M<N, the sum does not produce an end carry and is equal to rn-(N-M) . To obtain the answer in a familiar form, take the r’s complement of the sum and place a negative sign in front.

## Slide 14: Signed Binary Numbers
Negative numbers is shown with a minus sign in math.
In digital systems, the first bit decides the sign of the number.
  If the first bit 0, the number is positive.
  If the first bit 1, the number is negative.
This is called signed magnitude convention.

## Slide 15: Signed complement systems
To represent negative number, 1’s complement and 2’s complements are also used.
Represent +9 and -9 in eight bit system
  +9 is same for all systems: 00001001
  -9

## Slide 16: Arithmetic Addition

## Slide 17: Other Decimal Codes

## Slide 18: Gray Codes
Only one bit changes when going from one number to the next.
How to determine the gray code equivalent of a number:
  Add 0 to the left of number.
  XOR every two neigboring pair in order.
  The result is the gray code.
Example: 1 1 0 0 0 0 -> 0 1 1 0 0 0 0
1 0 1 0 0 0

## Slide 20: Truth tables

## Slide 21: Gate sysbols