## Slide 1: Food processing operations
In the food industry, various operations are used to produce high quality and safety food products and extend their shelf life.
These operations can be grouped into different categories according to their usage principles or purposes.
These operations are also called unit operations.

## Slide 2: Classification of unit operations
Unit operations, which are commonly used in the food industry from farm to fork, are classified into one of six groups as follow:
    Ambient temperature processing
    Heat processing using steam, hot water or oil
    Processing using hot air or heated surfaces
    Processing by direct and radiated energy
    Processing by removal of heat
    Post processing operations

## Slide 3: Unit operations in food industry
Ambient temperature processing
Raw material preparation
Size reduction
Mixing, forming, and coating
Heat process using steam, hot water or oil
Blanching
Industrial cooking
Pasteurization
Separation process
Heat Sterilization
Evaporation and distillation
Processing using hot air or heated surfaces
Dehydration
Smoking
Baking and roasting
Extrusion cooking
Frying

## Slide 4: Unit operations in food industry
Processing by direct and radiated energy
Dielectric heating
Processing by removal of heat
Refrigeration
Chilling
Freezing
Freeze drying and freeze concentration
Infrared heating
Ohmic heating
Post processing operations
Packaging
Filling and sealing of containers
Materials handling, storage and distribution

## Slide 5: AMBIENT TEMPERATURE PROCESSING

## Slide 6: Ambient temperature processing
Processing, which are performed at ambient temperatures, are explained under four main titles.
Separation process
Raw material preparation
Size reduction
Mixing, forming, and coating

## Slide 7: RAW MATERIAL PREPARATION

## Slide 8: Raw material preparation
Preparation of raw materials is one of the important steps for food production to produce high quality products or to offer for sale in the fresh market sector
In order to achieve this goal, application of one or more of unit operations, which are cooling, cleaning, sorting, grading or peeling, is neccessary

## Slide 9: Cleaning of foods
Cleaning removes contaminating materials such as soil, stones, bone, metal fragments, microorganisms, fertilizers, pesticide etc…
Cleaning is one of the significant steps of food processing since it prevents spread of these contaminants to uncontaminated pieces and reduces the risk of spoilage and loss of food.
Cleaning is applied in two different ways:
  Wet cleaning
  Dry cleaning

## Slide 10: Sorting and grading of foods
Sorting means the separation of foods according to their measurable physical properties such as size, shape, weight, color
Grading is the assessment of overall food quality using a number of attributes such as fat distribution for beef, roasting degree for coffee, aroma and flavor intensity for cheese
SORTING
GRADING

## Slide 11: SIZE REDUCTION

## Slide 12: Size reduction
Size reduction is applied to all food process in which the food is needed to cut or broken down into smaller pieces
The main benefits of size reduction are
    an increased surface area which enhance the rate of heat or mass transfer
    reduced particle size facilitate the mixing of ingredients

## Slide 13: MIXING, FORMING AND COATING

## Slide 14: Mixing, forming and coating
Mixing operation is required whenever an ingredient is added to a food
The main purpose of the mixing is obtain a homogenous final mixture by using two or more solid, liquid or gas components
    Addition of water into corn syrup (liquid to liquid)
    Addition of sugar into flour (solid to solid)
    Addition of sugar into fruit juice (solid to liquid)
    Diffusion of air into ice cream dough during ice cream making (gas to liquid)

## Slide 15: Calculation of uniformity of mixing and required mixing time
: standard deviation
n : number of samples
c : concentration of the component in each sample
: the mean concentration of samples
: Standard deviation of a perfectly mixed sample
: Standard deviation of a sample at the start of mixing
: Standard deviation of a sample taken during mixing

## Slide 16: Problem

## Slide 17: Agitation of liquid materials
Agitation is used for liquid foods. For example
  to blend one liquid into another miscible liquid
  to disperse gas in a liquid
  to disperse one liquid into another immiscible liquid
Access link https://www.youtube.com/watch?v=23X1eB5KryQ
Liquid agitator

## Slide 18: Froude number
Froude number is a dimensionless number, which is ratio of the inertial force to gravitational force
  If the vessel has blades, the role of the Froude number is negligible
  If the vessel has no blade, we have to take into consider the role of the Froude number
N: Rotational speed (revolution/s)
Di: Diameter of the impeller (m)
μ: Viscosity of the liquid (kg/ms)
: Accelaration due to gravity (m/s2)

## Slide 19: The curve drawn to find Np

## Slide 20: Problem
A concentrated fruit juice with a viscosity of 0.03 kg/ms and a density of 1100 kg/m3 is being agitated in an agitation system containing a turbine impeller. The impeller has a disk with six blades. The tank diameter is 1.8 m. The height of the liquid in the tank is the same as the tank diameter. The impeller diameter is 0.5 m. The width of the blade is 0.1 m. The tank is equipped with four baffles, each with a width of 0.15 m. If the turbine is operated at 100 rpm, determine the required power.

## Slide 21: SEPARATION PROCESSES

## Slide 22: Separation process
This operation is designed for the separation or physical removal of food components
Centrifugation
Filtration
Extraction using solvents
Expression (pressing)
Membrane separation
Main separation processes

## Slide 23
CENTRIFUGATION

## Slide 24: Centrifugation
Two main applications of centrifugation used in the food industry are separation of immiscible liquids and separation of solids from liquids
The separation factor is centrifugal force, which is generated when materials are rotated.
The size of the force depends on the radius, speed of rotation and the density of the centrifuged materials.

## Slide 25: Working principles of centrifugation
Heavy phase
Light phase
Medium phase
Acceleration force acts towards the centre of the cycle
Centrifugal force acts outwards from the centre
When a material (milk) is exposed to centrifugation, the heavier phase (water in milk) moves to the wall of the centrifuge and the lighter phase (fat in milk) is displaced to an inner annulus of the centrifuge as a result of the effect of these forces

## Slide 26: Animation for centrifugation
Access link : https://www.youtube.com/watch?v=sDhueH3q6Y4

## Slide 27: Basic equations related with centrifugation
The centrifugal force is calculated by using this formula
Fc: centrifugal force
m: mass of the particle (kg)
r: radial distance to the centre of rotation (radius) (m)
ω: angular velocity of the particle (rad/s )
: acceleration due to gravity (9.81 m/s2 )

## Slide 28: Calculation for centrifugal force
Centrifuge speeds are normally expressed as in revolution per minute (rpm)
N: revolution per minute

## Slide 29: Calculation for the rate of seperation
The rate of separation as expressed by velocity is calculated by formula given below
This formula is used to calculate the separation rate between two phases (solid in liquid) with different densities

## Slide 30: Calculation for the rate of seperation
D: Particle diameter (m)
N: Rotation speed (rpm)
r: Radius (m)
ρp: Density of the continous phase (kg/m3)
ρs : Density of the dispersed phase (kg/m3)
μ: Viscosity of the continous phase (kg/ms)
Velocity for separation (m/s)

## Slide 31: What is density and viscosity
Viscosity is defined as resistance to flow of a liquid
Water vs. honey
Density is the amount of material mass in a given volume

## Slide 32: Problems
Beef is clarified from the unwanted compounds by using centrifugate operation at 2600 rpm, with a radius of 15 cm. Calculate the centrifugal force for this operation.

## Slide 33: Problems
The solid particles in a liquid-solid suspension are to be separated by centrifugal force. The particles are 100 microns in diameter with a density of 800 kg/m3. The liquid is water with a density of 993 kg/m3, and the effective radius separation is 7.5 cm. If the required velocity for separation is 0.03 m/s, determine the rotation speed for the centrifuge.

## Slide 34: Liquid-liquid separation
rA: radius for the heavy phase outlet
rB: radius for the light phase outlet
rn: radius for inlet (feeding)

## Slide 35: Calculation of inlet radius
The formula given below is used to determine the position/radius of feed and discharge pipes and to design of the separation cylinder for liquid-liquid systems
ρA: Density of the heavier phasee
ρB : Density of the lighter phase
rA/r1: radius for the heavy phase outlet
rb/r1: radius for the light phase outlet
rn: radius for the inlet

## Slide 36: Problems
Cream is separated from the whole milk by using centrifugation. The density for the skim milk is 1025 kg/m3 and it has a 5 cm outlet radius. Radius of cream outlet is 2.5 cm and the density for cream is 865 kg/m3. Design the separation cylinder and suggest a required radius for the feeding (inlet).

## Slide 37
FILTRATION

## Slide 38: Filtration
Filtration is the removal of insoluble solids from a liquids by passing it through a porous material
Filtration is used to clarify wine, beer, juices, oils and syrups in the food industry
Filter medium

## Slide 39: Formation of filter cake
The solids removed from the liquid accumulate in the filter medium, which is called filter cake.
The formation of filter cake and its thickness affect the filtration rate as shown in the figure
A significant decrease in the rate of filtration process

## Slide 40: Factors that affect the filtration rate
The factors, which affect the filtration rate, are listed below
  The presence and thickness of filter cake (the resistance of the filter cake)
  The pressure drop across the filter medium
  The area of the filtering surface
  The viscosity of the filtrate
  The resistance of the filter medium

## Slide 41: Calculation of filtration rate
The rate of filtration can be described as the ratio of driving force (the pressure required to move the fluid through the filter medium) to resistance
The mathematical equation to calculate rate of filtration is given below
Volumetric flow rate (m3/s)

## Slide 42: Filtration process
The filtration process may occur in two phases
    Constant-rate filtration, which is normally occur during the early stages of the process
    Constant-pressure filtration, which is occur during the final stages of the process

## Slide 43: Constant-rate filtration
Constant-rate filtration is shown by the formula given below, which is used to determine the required pressure drop as a function of the filtration rate
If the thickness of the filter medium (L) is negligible, the equation is corrected
Reorganize the formula

## Slide 44: Constant-rate filtration
The equation given below is used to predict pressure drop requirements for a filter during the early stages of the process
∆P: Pressure drop requirements (Pa)
µ: Viscosity of the fluid (kg/ms)
r’: The spesific resistance of the filter cake
S: Solid content of the fluid
A: Cross-sectional area of the filter (m2)
V: Volume (m3)
t: The filtration time (s)

## Slide 45: Problem
An air filter is used to remove small particles from an air supply to a quality control laboratory. The air (0°C) is supplied at a rate of 0.5 m3/s through an air filter with a 0.5 m2 cross-sectional area. If the pressure drop across the filter is 0.25 cm water after one hour of use, determine the life of the filter if a filter change is required when the pressure drop is 2.5 cm of water.
Assumption: Due to the nature of air filtration, constant-rate filtration can be assumed and the filter medium thickness is negligible.
Use the table (A.4.4) given at next slide to find the viscosity of the air.

## Slide 47: Constant-pressure filtration
The equation used to define the constant-pressure filtration is given below
If the medium thickness (L) is negligible, the equation is corrected
∆P: Pressure drop requirements (Pa)
µ: Viscosity of the fluid (kg/ms)
r’: The spesific resistance of the filter cake
S: Solid content of the fluid
A: Cross-sectional area of the filter (m2)
V: Volume (m3)
t: The filtration time (s)

## Slide 48: Problem
The liquid is filtered at a pressure of 200 kPa through a 0.2 m2 filter. Initial results indicate that 5 min is required to filter 0.3 m3 of liquid. Determine the time that will elapse until the rate of filtration drops to 5x10-5 m3/s.
Assumption: Due to information given in the question, filtration is assumed to be constant-pressure condition and the filter medium thickness (L) is negligible.

## Slide 49: Main factors affecting the filtration process
Formula for the calculation of filtration rate
The rate of filtration is directly dependent on two main factors: filter medium and fluid being filtered
Filter medium is described in terms of filtration area and the spesific resistance of filter medium.
When the area increases, the filtration rate increases.
When the resistance against to filtration increases as a result of filter cake formation, the filtration rate decreases.
Fluid being filtered as described by the viscosity of the fluid. The filtration rate and the fluid viscosity are inversely related.
As the viscosity of the fluid increases, the filtration rate decreases.

## Slide 50: Design of a filtration system
The usage of equations given for constant-rate and constant-pressure filtration systems requires knowlegde of several parameters. However, in most cases, viscosity and spesific resistance values may not be known. Additionally, filter medium thickness (L) is not assumed to be negligible.
A small or pilot-scale operation in the food industry results in determination of filtration rate after given periods of time at a constant-pressure on the small scale filter.

## Slide 51: Design of a filtration system
We can use the formula given below to design the filtration system, which is also used to define the constant-pressure filtration systems.

## Slide 52: Design of a filtration system (an approach)
y = ax + b
If we resemble this equation to another basic equation
y is equal to
b, which is called intercept, is equal to
x is equal to
a, which is called slope, is equal to

## Slide 53: Design of a filtration system (an approach)
If we draw a filtration graph by using the information given in the slide, which is the previous one,
y = ax + b
Y AXIS
X AXIS

## Slide 54: Problem

## Slide 55: Problem (cont.)
  Volume (V): 4 m3
  Time (t): 2 hour
  Pressure (∆P): 400 kPa
  Area (A): 0.1 m2
  Pressure (∆P): 140 kPa
Desired conditions
Designed conditions

## Slide 56: Problem (cont.)
slope
intercept

## Slide 57: Problem (cont.)
  Volume (V): 4 m3
  Time (t): 2 hour
  Pressure (∆P): 400 kPa
  Ouestion:
  Filter area ???
  Area (A): 0.1 m2
  Pressure (∆P): 140 kPa
Desired conditions
Designed conditions
Slope 0.6249
Intercept 29.827

## Slide 58
EXTRACTION USING SOLVENTS
(Solid-liquid extraction)

## Slide 59: Extraction using solvents
Solid-liquid extraction is defined as removal of a desired compound, which is called solute, from a food by using a liquid, which is called solvent
Extraction process has many application areas in the food industry such as
    Extraction of oil from oilseeds and nuts
    Extraction of essential oil and flavor compounds from herbs, spices, fruits and vegetables
    Coffee, tea, and decaffeinated coffee and tea

## Slide 60: Some examples for the solid-liquid extraction process
Oil extraction from nuts
Oil extraction from herbs
Extraction of flavor and color compounds from tea by using hot water

## Slide 61: Theory of the solid-liquid extraction
The solid-liquid extraction involves mixing the food and solvent together, holding for a time and then separating the solvent
During the holding period of time, the mass transfer of solid compounds occur in three stages:
    The solvent enters into the food and dissolve the targeted solute
    The solute trapped in the solvent moves through the surface of the food
    The solute becomes dispersed in the bulk of the solvent

## Slide 62: Extraction using solvents Access link: https://www.youtube.com/watch?v=cF4_RRNIGAc

## Slide 63: Factors affecting the extraction process
1. The solubility properties of a solid compound in the solvent
2. The temperature of the extraction: Higher temperatures cause extraction of undesirable compounds and heat damage; although, it increases the rate of extraction
3. The surface area of the solid: Large surface increases the extraction rate
4. Viscosity of the solvent: As the viscosity decreases, the rate of extraction increases due to easily penetration ability of less viscosious solvents
5. Flowrate of solvent: As the flowrate increases, the rate of extraction increases

## Slide 64: Extraction using solvents
Common types of solvents used for extraction process are water, organic solvents, and supercritical fluids
    Water is the most convenient, cost-effective, and environmentally friendly solvent. It is widely used for the production of sugar, coffee, and tea
    Oils and fats are needed organic solvents (such as acetone, butane, ethanol, hexane, methanol etc.) for extraction since they are water-insoluble
    Among supercritical fluids, supercritical CO2 is generally used for the extraction process

## Slide 65: Supercritical CO2
These fluids has different physical properties from liquids and gases
Supercritical CO2 acts is a liquid but it difuses like a gas
It has low viscosity
It needs low temperature for extraction
It is effectively used in the extraction process due to the advantages of these properties
31.06°C

## Slide 66: References
Singh, R.P. and Heldman D.R. (2009) Introduction to food engineering. Chapter 13: Supplemental processes. Pages 689-720. (4th ed.) Academic Press, California, USA (In the library of our department)
Fellows, P.J. (2017). Food processing technology principles and practice. Part II Ambient Temperature Processing. Pages 201-386. (4th ed.) Woodhead Publishing, Duxford, United Kingdom
Campbell-Platt, G. (2009). Food Science and Technology. Chapter 9: Food processing, Unit operations. Pages 219-234. Blackwell Publishing (In the library of our department)