## Slide 1
FDE 101-Basic Concepts in Food Engineering
Food Processing
Operations

## Slide 2: Unit operations in food industry
Ambient temperature processing
Raw material preparation
Size reduction
Mixing, forming, and coating
Heat process using steam, hot water or oil
Blanching
Industrial cooking
Pasteurization
Separation process
Heat Sterilization
Evaporation and distillation
Processing using hot air or heated surfaces
Dehydration
Smoking
Baking and roasting
Extrusion cooking
Frying

## Slide 3: Unit operations in food industry
Processing by direct and radiated energy
Dielectric heating
Processing by removal of heat
Refrigeration
Chilling
Freezing
Freeze drying and freeze concentration
Infrared heating
Ohmic heating
Post processing operations
Packaging
Filling and sealing of containers
Materials handling, storage and distribution

## Slide 4: HEAT PROCESS USING STEAM, HOT WATER OR OIL

## Slide 5: Heat process using steam, hot water or oil
The unit operations performed by using steam, hot water or oil are listed below
    Blanching
    Industrial cooking
    Pasteurization
    Heat Sterilization
    Evaporation and distillation
    Frying

## Slide 6: BLANCHING

## Slide 7: Blanching
Blanching is a brief exposure of the solid food to hot water or steam
Enzymes results in tissue softening and spoilage during storage of unblanched vegetables and fruits
Therefore, blanching is mainly used to destroy enzymatic activity in vegetables and some fruits
It also reduces the numbers of microorganisms on the surface of the food

## Slide 8: PASTEURIZATION AND HEAT STERILIZATION

## Slide 9: High temperature treatments in foods
In the food industry, heat treatments at high temperatures are used in order to
  destroy enzymes
  kill spoilage and pathogenic microorganisms
As a result of heat treatments,
  The quality and safety of a food product preserves
  The shelf-life of a food product extends

## Slide 10: Spoilage vs pathogenic microorganisms
They cause food deterioration
The food has bas taste, bad look and bad odor
The appearance, taste and odor of food change as a results of microbial growth
The consumption of food are rejected by humans; therefore spoilage microorganisms are not harmful for humans
They can grow on the food and produce toxins
The appearance, taste and odor of food do not change
Humans can ill or death when they consume the food contaminated by pathogenic microorganism and their toxins
Spoilage microorganisms
Pathogenic microorganisms

## Slide 11: Problems….
The number of pathogenic microorganisms in raw milk is 1012. If the D-value is 1.25 sec at 72°C to kill all pathogenic microorganisms, calculate the pasteurization time.
1012 is equal to 12 log
1.25 sec x 12 log = 15 sec
The number of spoilage microorganisms in fruit juice is 8.5x105. If the D-value is 10 sec at 77°C to kill the spoilage microorganisms, calculate the pasteurization time.
8.5x105 is equal to 5.93 log
6 log reduction is required to pasteurize the fruit juice
10 sec x 6 log = 60 sec = 1 min

## Slide 12: HEAT STERILIZATION

## Slide 13: Sterilization
Sterilization is a heat treatment in which foods are heated at a sufficiently high temperature for a sufficiently time to destroy all alive microbial cells, their spores and to inactive enzymes
The temperature used for these process exceeds the boiling point of water, which means high temperatures above 100°C are used to sterilize the food products
As a result , packaged sterilised foods have shelf life more than 6 months at ambient temperature

## Slide 14: Determination of sterilization time
The number of Brucella abortis in raw milk is 1012. If the D-value is 0.21 min at 121.1°C to kill microorganisms, calculate the sterilization time.
1012 is equal to 12 log
12 log x 0.21 min = 2.52 min
The number of Clostridium botulinum in soup can is 7.9x104. If the D-value is 0.79 min at 121.1°C to kill the microorganisms, calculate the sterilization time.
7.9x104 is equal to 4.90 log
5 log reduction is required to sterilize the soup
0.79 min x 5 log = 3.95 min

## Slide 15: UHT or aseptic packaging
For aseptic packaging, or in other words, aseptic processing once the product is sterilized and then the sterilized product is placed into aseptic (sterile) package or container under an aseptic enviroment
UHT processing involves heating foods to 130-150°C for a few seconds

## Slide 16: EVAPORATION

## Slide 17: Evaporation
Evaporation is an important unit operation commonly used to remove water from dilute liquid foods to obtain concentrated liquid products under vacuum condition
This process increases the solid content of foods

## Slide 18: Theory of evaporation
The basic example of evaporation is boiling of water
When the external pressure is equal to vapour pressure of water, boiling starts at 100°C
This process is called evaporation at atmospheric condition

## Slide 19: DISTILLATION

## Slide 20: Distillation
Distillation is the application of heat to separate the components or substances from a liquid mixture depending on their boiling points
It is also defined as purification process

## Slide 21: ProcessIng usIng hot aIr or heated surfaces

## Slide 22: Processing using hot air or heated surfaces
The unit operations performed by using hot air or heated surfaces are listed below
  Dehydration
  Smoking
  Baking and roasting
  Extrusion cooking

## Slide 23: DEHYDRATION

## Slide 24: Dehydration (drying)
Dehydration is the application of heat under controlled conditions to remove the major amount of water normally present in the food
The main purpose of dehydration is to extend shelf-life of foods by reducing water activity
Dried foods are characterized as having a water acitivity below 0.6
Heated air or heated surfaces are used to remove the water from foods during drying process

## Slide 25: Advantages of dehydration
The microbial deterioration is eliminated due to low water content (low aw values)
The rate of other deteriorative reactions are reduced due to low water content (low aw values)
However, the processing temperature is not enough to provide completely inactivation of enzyme, spoilage or pathogenic microorganisms and their spores. Therefore, any increase in moisture content in dried food during storage causes rapid deterioration. Spores of pathogenic microorganisms can cause foodborne illness if the food is not cooked before consumption
Dehydration reduces product mass and volume, which improves efficiency of transportation and storage

## Slide 26: References
Singh, R.P. and Heldman D.R. (2009) Introduction to food engineering. Chapter 5: Preservation process, Chapter 8: Evaporation, Chapter 12: Dehydration (4th ed.) Academic Press, California, USA (In the library of our department)
Fellows, P.J. (2017). Food processing technology principles and practice. (4th ed.) Woodhead Publishing, Duxford, United Kingdom
Campbell-Platt, G. (2009). Food Science and Technology. Chapter 9: Food processing, Unit operations. Pages 234-240. Blackwell Publishing (In the library of our department)