## Slide 1
FDE 101-Basic Concepts in Food Engineering
Food Processing
Operations

## Slide 2: Unit operations in food industry
Ambient temperature processing
Raw material preparation
Size reduction
Mixing, forming, and coating
Heat process using steam, hot water or oil
Blanching
Industrial cooking
Pasteurization
Separation process
Heat Sterilization
Evaporation and distillation
Processing using hot air or heated surfaces
Dehydration
Smoking
Baking and roasting
Extrusion cooking
Frying

## Slide 3: Unit operations in food industry
Processing by direct and radiated energy
Dielectric heating
Processing by removal of heat
Refrigeration
Chilling
Freezing
Freeze drying and freeze concentration
Infrared heating
Ohmic heating
Post processing operations
Packaging
Filling and sealing of containers
Materials handling, storage and distribution

## Slide 4: PROCESSING BY DIRECT AND RADIATED ENERGY

## Slide 5: Processing by direct and radiated energy
The unit operations which are applied by direct or radiated energy are listed below
  Dielectric heating
    Microwave heating
    Radiofrequency heating
  Ohmic heating
  Infrared heating

## Slide 6: MICROWAVE, RADIOFREQUENCY and INFRARED HEATING

## Slide 7: Electromagnetic spectrum
Dielectric (radiofrequency and microwave) and infrared energy are two forms of electromagnetic energy
IR: Infrared heating
RF: Radiofrequency heating

## Slide 9: Working principles of microwaves

## Slide 10: PROCESSING BY REMOVAL OF HEAT

## Slide 11: Processing by removal of heat
The unit operations which are processed by removal of heat from food are listed below
  Refrigeration
    Chilling
    Freezing
  Freeze drying and freeze concentration

## Slide 12: REFRIGERATION (CHILLING AND FREEZING)

## Slide 13: Refrigeration
Removal of heat from foods slows the biochemical and microbiological changes during storage
This process is called refrigeration
Refrigeration is defined as lowering the temperature of a food product and storage it at low temperatures
Refrigeration is performed with two different ways which are chilling and freezing

## Slide 14: Two ways of refrigeration
The temperature of a food is reduced to between -1°C and 8°C
The temperature of a food is reduced to below its freezing point
Freezing causes a great proportion of water undergo a change in state to form ice crystals
Chilling
Freezing

## Slide 15: CHILLING OF FOODS

## Slide 16: Chilling
Chilling is an important unit operation in food industry in which the temperature of a food is reduced to between -1°C and 8°C
The theory of chilling is removal of sensible heat and heat generated by respiratory activity

## Slide 17: Factors that affect chilling effectiveness
The factors that affect the success of chillling process and shelf life of a food product
    Initial microbial load and chemical properties of raw material
    Water activity of food
    Acidity value of food
    Processing and storage conditions
    Hygiene during processing and storage
    Presence of oxygen
    Temperature control
    Properties of packaging material

## Slide 18: Effects of chilling on microorganisms
The growth of psychrotrophic and psychrophilic microorganisms results in color change, slime, off-flavor and off-odor formation
The main safety concern with chilled foods is growth of some pathogenic bacteria below 5°C during extended chilled storage or as a conclusion of any temperature fluctuations
Yeast and molds are also able to grow at chilled temperatures. However, their growth is slow comparing with bacteria

## Slide 19: FREEZING OF FOODS

## Slide 20: Freezing
Freezing is basically defined as reduction in the food temperature to below its freezing point in order to preserve foods without causing significant changes to their sensory qualities and nutritional value
As a result of freezing;
  The form of water changes from liquid to solid to form ice crystals
  The solid concentration increases
  Water activity of the food decreases
  Biochemical, enzymatic and microbial acitivity reduces

## Slide 21: Commercially frozen foods
Main groups of commercially frozen food products are listed below
    Baked products such as bread, cakes, pies
    Fish fillets and seafoods
    Fruits and their concentrates
    Meats and meat products
    Prepared foods such as pizza, dessert, ice cream, ready to eat meals
    Vegetables such as peas, green beas, sweetcorn, potato, spinach

## Slide 22: The effect of freezing on foods
The freezing involves three different steps which are
    Freezing process
    Frozen storage
    Thawing
The effects of each stage on foods and microorganisms are different and they can be explained individually

## Slide 23: Thawing
Thawing is defined as conversion of ice crystalls, which is present in frozen food, into water
Air or water is used to thaw the frozen products
Thawing starts from the surface of a food, which means water occurs on the food surface at first

## Slide 24: Effect of freezing process
During freezing process, two physical situation occurs in especially slow freezing, which are
  Mechanical damage of cell
  Dehydration and thaw loss, or in other words drip loss

## Slide 25: Effect of frozen storage
In foods, some loss of quality due to both chemical changes and enzymatic activity can be occured during storage at normal frozen temperatures (nearly -18°C)
The effect of frozen storage on food quality can be summarized with 6 points as follow
  Degradation of pigments and color change in foods
  Loss of water-soluble vitamins due to oxidation or drip loss
  If the intracellular enzymes are not inactivated, the enzymes can easily react with lipids and proteins as a result of cell damage. This situation results in off-flavor and off-odor formation, changes in texture and color, loss of protein functionality and degradation of lipids

## Slide 26: References
Singh, R.P. and Heldman D.R. (2009) Introduction to food engineering. Chapter 6: Refrigeration, Chapter 7: Food freezing (4th ed.) Academic Press, California, USA (In the library of our department)
Fellows, P.J. (2017). Food processing technology principles and practice. Chapter 20: Heat removal by refrigeration, Chapter 21: Chilling, Chapter 22: Freezing (4th ed.) Woodhead Publishing, Duxford, United Kingdom