## Slide 1: Packaged product qualıty and shelf lıfe
Instructor
Assist. Prof. Dr. Eda Demirok Soncu
E-mail: edemirok@eng.ankara.edu.tr
Phone: +90312 203 3300 (3639 ext.)
Office: 2nd floor #212

## Slide 2: What is food quality?
Quality can be defined as a sum of nutritional content, sensory attributes, safety, physical and chemical properties of a product that have significance in determining the degree of acceptability of that product to the consumer

## Slide 3: Conditions affecting quality of packaged food
The major quality attributes of foods are texture, flavor, color, appearance, and nutritive value
These attributes can all undergo undesirable changes during processing and storage
With the exception of nutritive value, the changes that can occur in these attributes are readily apparent to the consumer, either before or during consumption
Undesirable reactions, such as oxidation, flavor absorption by plastic polymers or moisture absorption of dried foods, can affect food quality under improper packaging conditions
Migration of some components, which are not harmful for human health, from packaging materials to food may adversely affect the quality of the product

## Slide 4: What is food safety?
Food is accepted as safe if it does not contain harmful organisms or compounds in concentrations above the limits
Food safety is defined as protection of consumer from adverse health effects of food under the responsibility and control of legislation

## Slide 5: Conditions affecting safety of packaged food
If the packaging material does not provide a suitable barrier around the food, microorganisms can contaminate the food and make it unsafe
On the other side, microbial contamination can also arise if the packaging material permits the transfer of, for example, moisture or O2 from the atmosphere into the package
Migration of potentially toxic compounds from some packaging materials to the food is another factor that affect food safety

## Slide 6: What is shelf life?
For the majority of foods and beverages, quality decreases over time
Therefore it follows that there will be a finite length of time before the product becomes unacceptable
This time from production to unacceptability is referred to as shelf life

## Slide 7: What can we do for the protection of quality and safety?
In order to maintain the quality and safety of a food product during shelf life;
  We have to know the kind of changes that influence food quality and safety
  We have to know the factors that trigger or control the rate of these reactions
  We have to minimize undesirable changes and maximize the development and maintenance of desirable properties
  We have to use the right packaging option

## Slide 8: DETERIORATIVE REACTIONS IN FOODS

## Slide 9: Deteriorative reactions in foods
Knowledge of the kinds of deteriorative reactions that influence food quality is the first step in developing food packaging that will minimize undesirable changes in quality and maximize the development and maintenance of desirable properties
Once the nature of the reactions is understood, knowledge of the factors that control the rates of these reactions is necessary in the second stage in order to minimize the changes occurring in packaged foods during storage

## Slide 10: Deteriorative reactions in foods
Enzymatic reactions
Chemical reactions
Lipid oxidation
Nonenzymatic browning
Color changes
Flavor changes
Nutritional changes
Microbiological changes
Physical changes
Physical damage
Insect damage
Moisture changes
Barrier to odor-pick up
Flavor scalping

## Slide 11: FACTORS AFFECTING DETERIORATIVE REACTIONS

## Slide 12: Factors affecting deteriorative reactions
Factors that influence deteriorative reactions and their rates are classified one of two groups
  Water activity
  Oxidation-reduction potential
Intrinsic parameters
  Temperature
  Relative humidity
  Gas atmosphere
  Light
Extrinsic parameters

## Slide 13: INTRINSIC PARAMETERS

## Slide 14: 1) Water activity
It is defined as the ratio of the water vapor pressure of food (P) to that of vapor pressure of pure water (Po) at the same temperature
aw: water activity
P: partial pressure of water in a food
Po: vapor pressure of water at the same temperature

## Slide 15: 1) Water activity
Water can influence chemical reactivity in different ways
  It may act as a reactant (e.g. hydrolysis reactions)
  It may act as a solvent, where it may exert a dilution effect on the substrates, thus decreasing the reaction rate
  Water may also change the mobility of the reactants by affecting the viscosity of the food systems (honey vs fruit juice)

## Slide 16: Rates of reactions as a function of water activity

## Slide 17: 2) Oxidation-reduction potential
Redox reactions include electron transfer between two molecules or atoms
The loss of electron is called as “oxidation”. An atom or a molecule which loses electrons is known as “reducing agent”
The gain of electron is called as “reduction”. An atom or molecule which accepts the electrons is known as “oxidising agent”

## Slide 18: 2) Oxidation-reduction potential

## Slide 19: 2) Oxidation-reduction potential
Eh is the symbol of oxidation-reduction potential (ORP)
Eh plays an important role in the cellular physiology of microorganisms, such as growth capacity, enzyme expression, and thermal resistance
Reducing the Eh of orange juice using gas (N2 and H2) immediately after heat treatment maximized microbial destruction during pasteurization and prevented the development of microorganisms during shelf life
Higher level of ORP in milk are mainly responsible for the oxidation of unsaturated fatty acids. Decreasing the Eh in milk could allow an improvement in the quality of these products

## Slide 20: EXTRINSIC PARAMETERS

## Slide 21: 1) Temperature
Temperature is a key factor in determining the rates of deteriorative reactions
In some cases, packaging material can affect the temperature of the food
  Packaging materials that have insulating properties, should be used for chilled and frozen foods
  Regarding foods, which are stored in refrigerated display cabinets, heat transfer is important. Therefore, packaging material should have heat permeability

## Slide 22: 2) Relative humidity
The RH of the ambient environment is important and can influence the aw of the food unless the package provides an excellent barrier to water vapor
Many flexible plastic packaging materials provide good moisture barriers
But packaging materials, which have low barrier properties against to moisture, limit the shelf life of low aw foods

## Slide 23: 3) Gas atmosphere
The presence and concentration of gases in the environment surrounding the food have a considerable influence on the growth of microorganisms
Atmospheric O2 generally has a detrimental effect on the nutritive quality of foods such as
  Microbial growth
  Lipid oxidation, which results in formation of secondary oxidation products or interaction between primary oxidation products and vitamins

## Slide 24: 3) Gas atmosphere
In order to maintain food quality, different packaging techniques are used
  Vacuum packaging, defined as removal of air (O2) from a package prior to sealing, have a beneficial effect by preventing the growth of aerobic microorganisms
  Filling the inside of the package with a gas such as CO2 or N2 before sealing is the basis of modified atmosphere packaging (MAP). Increased concentrations of gases such as CO2 are used to retard microbial growth and thus extend the shelf life of foods

## Slide 25: 4) Light
Many deteriorative changes in the nutritional quality of
foods are initiated or accelerated by light
The catalytic effects of light are most pronounced in the lower wavelengths of the visible spectrum and in the UV spectrum
The intensity of light and the length of exposure are significant factors in the production of discoloration and flavor defects in packaged foods

## Slide 26: 4) Light
How is improved the light properties of packaging materials?
  Plastic materials can be incorporated with dyes or coatings that absorb light at specific wavelengths
  Titanium dioxide have been incorporated into plastic films to absorb UVA and UVB rays
  Glass is frequently modified by inclusion of color-producing agents or by application of coatings

## Slide 27: DETERIORATIVE REACTIONS IN FOODS

## Slide 28: Deteriorative reactions in foods
Enzymatic reactions
Physical changes
Lipid oxidation
Nonenzymatic browning
Color changes
Flavor changes
Nutritional changes
Microbiological changes
Chemical reactions
Physical damage
Insect damage
Moisture changes
Barrier to odor-pick up
Flavor scalping

## Slide 29: 1) Enzymatic reactions
Foods have various types of enzymes, which react with food compounds
Control of enzymatic activity during food processing and storage is essential to maintain food quality
The major factors useful in controlling enzyme activity are temperature, aw, pH, chemicals that can inhibit enzyme action, alteration of substrates, alteration of products, and preprocessing control

## Slide 30: 1) Enzymatic reactions
Three of these factors are particularly relevant in a packaging context
The first is temperature: the ability of a package to maintain a low product temperature and thus retard enzyme action will often increase product shelf life
The second important factor is aw, because the rate of enzyme activity is dependent on the amount of water available; low levels of water (below aw value of 0.3) can severely restrict enzymic activities
Finally, alteration of substrate (in particular, the replacement of O2 with inert gas) is important in many O2-dependent reactions that are catalyzed by enzymes, for example, enzymic browning due to oxidation of phenols in fruits and vegetables

## Slide 31: 2) Physical changes
Physical changes affecting shelf life can be brought about directly by physical damage
The first function of packaging is protection from environmental factors and contamination such as dust and dirt, dehydration and rehydration, insect and rodents, leakage and spillage during storage and distribution
However, in some cases, careless or intentional strike, press or irritation may negatively affect pysical quality of foods during distribution and storage

## Slide 32: 2.1) Physical damage
During product life, particularly in storage, distribution and consumer handling, products are subjected to vibration on vehicles, compressive loads during stacking in warehouses and sudden strike, shake and overturn
The formulation of the product must be sufficient to tolerate these pysical hazards and packaging must be able to withstand and protect the food
For example, emulsions must be stable enough to withstand vibration

## Slide 33: 2.1) Physical damage
**Heat seals and screw caps are vulnerable areas against to damage, resulting in leakage and loss of protection due to air intake
**Fragile products, that are susceptible to crushing are sensitive to physical damage
Fruit and vegetables that are susceptible to bruising require protection from rough handling and the outer packaging must be used for distribution purposes to protect the food from physical damage. The most important thing is that airflow that required by fruits or vegetables for respiration must be allowed.

## Slide 34: 2.2.) Insect damage
Infestation of foods with insects can be extremely unpleasant for the consumer because it is often not detected until the opening of the product
Insect infestation can occur at any point after manufacture, but is most likely during extended storage periods or during shipment
Insect infestation results in loss of materials and damage the name of brands

## Slide 35: 2.2.) Insect damage
Package pests are classified in two groups – penetrators and invaders
Penetrators are capable of entry into package through one or more layers of flexible packaging materials. It is possible to reduce their infestation by preventing the escape of odours from the package through the use of high odor barrier materials
Invaders are more common and enter packages through existing openings, usually created from poor seals, openings made by other insects or mechanical damage. Therefore, seals should be durable against to insects. Additionally, the corners of square packages can also be potential points of entry for insects

## Slide 36: 2.3) Moisture changes
Moisture changes leading to loss or gain of moisture is a significant physical cause of the loss of shelf life of foods
Hygroscopic foods require protection from moisture take up which in dry products such as breakfast cereals and biscuits causes loss of texture, particularly crispness

## Slide 37: 2.3) Moisture changes
Protection or prevention of moisture loss (by dehydration or evaporation) in chilled and frozen foods, cheese, fresh meats is best achieved by maintaining the correct temperature and humidity in storage
Moisture loss in chilled and frozen foods, cheese, fresh meats causes weight loss, financial loss for producers, change in color and appearance
Moisture loss in fresh fruits and vegetables results in wiltness. To prevent moisture loss the recommended range for storage humidity is 80–100%

## Slide 38: 2.3) Moisture changes
Severe dehydration in frozen foods leads to freezer burn
Freezer burn is defined as the formation of greyish zones at the surface due to cavities forming in the surface layer of the food
Freezer burn causes the lean surfaces of meat to become rancid, discoloured and physically changed

## Slide 39: 2.3) Moisture changes
One of the most widely experienced quality changes involving the transfer of moisture is sogginess in sandwiches
Moisture transfer from the filling to the bread can be reduced by the use of fat-based spreads to provide a moisture barrier at the interface
In pastry-based and crust-based products such as pies and pizzas, movement of moisture from fillings and toppings to the pastry and crust causes similar problems

## Slide 40: 2.3) Moisture changes
The movement of moisture or oils may be accompanied by soluble colours; for example, in pizza toppings where cheese and salami come into contact, red streaking of the cheese is seen
Transfer of enzymes from one component to another, for example when sliced unblanched vegetables are placed in contact with dairy products, can lead to flavour, colour or texture problems depending on the enzymes and substrates available
Preparation of these type of foods at the point of consumption, edible films, gelatin films or oily layer between the components are alternative solutions to such problems

## Slide 41: 2.3) Moisture changes
The factors that affect rate of moisture loss;
  the difference between the water vapour pressure exerted by the product and the water vapour pressure in the air
  air speed over the product
Packaging materials, which have low WVTR, should be used to minimize moisture changes

## Slide 42: 2.4) Barrier to odor pick-up
In some cases, food commodities are stored or distributed foods in the same container or trailer
Dairy products, eggs and fresh meat are highly susceptible to picking up strong odours
Chocolate, flavoured sweets, mints have strong flavors
If these type of foods are carelessly stored or transfered together, odors can penetrate under low permeability packaging condition (e.g. some plastic materials allow volatile penetration)

## Slide 43: 2.5) Flavour scalping
If a chemical compound present in the food has a high affinity for the packaging material, it will tend to be absorbed into or adsorbed onto the packaging until equilibrium concentrations have been established in food and packaging
This loss of food constituents to packaging is known as scalping
Scalping does not result in a direct risk to the safety of the food; however, the loss of volatile compounds which contribute to a food’s characteristic flavour affect sensory quality

## Slide 44: 2.5) Flavour scalping
Researches showed that polypropylene are able to absorb the highest quantities of volatiles from apple juice, resulting in loss of aroma compounds
Therefore, particular food-packaging combinations or an effective barrier layer should be designed to reduce the scalping problem

## Slide 45: 3) Microbiological changes
Microorganisms can make both desirable and undesirable changes to the quality of foods

## Slide 46: 3) Microbiological changes
The two major groups of microorganisms found in foods are bacteria and fungi
Bacteria are generally the fastest growing, so in conditions favorable to both, bacteria will usually outgrow fungi
The species of microorganisms that cause the spoilage of particular foods are influenced by two factors: the nature of the foods and their surroundings

## Slide 47: 3) Microbiological changes
Every microorganism has a limiting aw value below which it will not grow, form spores, or produce toxic metabolites
Reducing the aw value of a given food is a good solution to inhibit microbial growth
The temperature of storage is particularly important, and several food preservation techniques (e.g., chilling) rely on reducing the temperature of the food to extend its shelf life. Molds are able to grow at refrigerated temperatures more quickly when compared to bacteria
The presence and concentration of gases (CO2) in the environment has a considerable influence on the growth of microorganisms

## Slide 48: Special aw values for microorganisms
Special limit of aw values for the growth of microorganisms are given below
Mold growth starts at aw value of 0.70
Yeast growth starts at aw value of 0.75
Bacteria growth starts at aw value of 0.80

## Slide 49: CHEMICAL REACTIONS

## Slide 50: Chemical reactions
Many important chemical changes can occur as a result of reactions between components within the food, or between components of the food and the environment
Chemical reactions will proceed if reactants are available and if the activation energy threshold of the reaction is exceeded

## Slide 51: Chemical reactions
The rate of reaction is dependent on
  the concentration of reactants
  the temperature (e.g. every 10°C rise in temperature, the rate of reaction doubles)
  other energy (e.g. light induced reactions)

## Slide 52: Chemical reactions
Specialised proteins called enzymes catalyse biochemical reactions. They can be highly specific catalysts, lowering the activation threshold so that the rate of reaction is dramatically increased
The specificity of enzymes for a particular substrate is indicated in the name, usually by attachment of the suffix -ase to the name of the substrate on which it acts. For example;
    lipase acts on lipids
    protease on proteins

## Slide 53: Chemical changes in lipids
Lipolysis (Hydrolysis in lipids)
Enzymatic hydrolysis
Lipid oxidation
Chemical oxidation
Enzymatic oxidation
Thermic oxidation
Chemical hydrolysis

## Slide 54: Lipolysis (Hydrolysis in lipids)

## Slide 55: Enzymatic lipid hydrolysis
The ester bond is hydrolysed by lipase enzyme
Monogliseride, diglyseride and free fatty acids are degradation products of lipid hydrolysis

## Slide 56: Enzymatic lipid hydrolysis
The factors that affect the rate of enzymatic lipid hydrolysis
  The hydrolysis rate of enzyme is inversely related to lenght of fatty acid. For example, short chain fatty acids are hydrolysed by lipase faster as compared to long chain fatty acids
  When the surface area increases in fat-water emulsions, the rate of enzyme activity increases
  If the water content and aw value of a food product is higher than 10% and 0.3, respectively, the rate of enzyme activity increases

## Slide 57: Chemical lipid hydrolysis
This reaction is catalysed by free fatty acids, which are naturally found in the reaction medium

## Slide 58: Chemical lipid hydrolysis
The factors that increase the rate of chemical lipid hyrolysis are given below;
    Temperature of reaction medium
    The amount of free fatty acids
    Solubility of water in lipids

## Slide 59: What is the importance of free fatty acids in food industry?
Free fatty acids, which have carbon atom less than 16, give characteristic taste, odor and flavor to some food types (for example: cheese and chocolate)
In some cases, free fatty acids, which have carbon atom less than 16, give undesirable taste and odor
Free fatty acids, which are naturally found or formed as a conclusion of lypolysis reactions, are the substrate of lipid oxidation

## Slide 60: Lipid oxidation

## Slide 61: Lipid oxidation
Lipid oxidation results in desirable and undesirable changes in food products
  Desirable changes: For example, lipid oxidation gives characteristic odor, taste and flavor to fermented meat products such as sucuk (dry-fermented sausage)
  Undesirable changes: A number of chemical components of food react with oxygen affecting the colour, flavour, nutritional status and physical characteristics. The results are deleterious and limit shelf life

## Slide 62: Lipid oxidation
We can control oxygen requirement of foods by packaging materials
In some cases, a certain amount of oxygen is needed in order to maintain respiration (e.g. fresh fruits and vegetables) or maintain desired brigt-red color (e.g. fresh meats in modified atmosphere packages)
On the other side, oxygen permeability of the packaging material is crucial, if the food product is prone to undesirable oxidation reactions

## Slide 63: The estimated maximum oxygen tolerance of various foods

## Slide 64: Lipid oxidation
Foods containing a high percentage of fats, particularly unsaturated fats, are susceptible to oxidative reactions
Saturated fatty acids oxidise slowly compared to unsaturated fatty acids
The number of unsaturated bonds is negatively affect the rate of lipid oxidation. When the number of unsaturated bonds increases, rate of oxidation increases

## Slide 65: Lipid oxidation
Three different chemical routes can initiate the oxidation of fatty acids
  The classical free radical route: the formation of free radicals in the presence of metal ion catalysts such as iron, or heat, or light, or oxygen
  Photooxidation in which photo-sensitisers such as chlorophyll or myoglobin affect the energetic state of oxygen
  An enzymic route catalysed by lipoxygenase

## Slide 66: 1) The stages of lipid oxidation
Lipid oxidation is a otocatalytic** reaction
Lipid oxidation has three important stage (1) initiation, (2) propagation and (3) termination
  In the first and second stage, oxygen has been introduced into the unsaturated fatty acids to form peroxides and hydroperoxides, which are primary oxidation products
  In the third stage, secondary oxidation products are formed (aldehydes, ketones, hydrocarbons, alcohols)

## Slide 67: The stages of lipid oxidation
RH : Free fatty acids ROO : Peroxides ROOH : Hydroperoxides ROOR : Secondary
oxidation products

## Slide 68: Formation of free radicals
Removal of H+ atom, which is placed on the left or right side of double bond
As a result of H+ atom removal, double bond is replaced through left or right side
Free radicals are activated by two different ways

## Slide 69: Degradation products and undesirable results of lipid oxidation

## Slide 70: The factors that affect lipid oxidation rate
The factors that affect lipid oxidation rate are given below
    Medium temperature
    Light
    Presence of metal ions (for example Fe+2)
    Surface area of oxygen contact
    Number of double bond in fatty acid

## Slide 71: Important results of lipid oxidation
Undesirable taste and odor compounds occur
Rancid (bitter) taste and odor form
For example, aldehydes, alcohols and ketones that are responsible for the characteristic stale, rancid and cardboard odours associated with lipid oxidation
Some of secondary oxidation products have carcinogenic properties (for example malondialdehyde)
Oxidised lipids react with proteins, vitamins and carbohydrates; thus, nutritional quality of a food product decreases
Food safety is affected

## Slide 72: How we can stop or retard lipid oxidation?
Antioxidants that occur naturally or are added, are able to slow the rate of lipid oxidation or increase the lag time of reactions
Reduction of the concentration of oxygen (both dissolved and in the headspace) to below 1%
Removal of factors that initiate oxidation
Lowering the storage temperature does not stop oxidative rancidity because both the first and second steps in the reaction have low activation energies

## Slide 73: Precautions and packaging options to retard/prevent lipid oxidation
Presence of natural antioxidant compound (e.g. in milk chocolate, the presence of tocopherol (vitamin E), a natural antioxidant in cocoa liquor provides a high degree of protection against rancidity)
Utilization of packaging material which has low light barrier permeability or low oxygen permeability
Replacement of oxygen with nitrogen (e.g. cips, snack foods
Vacuum packaging (in especially meat products)
Utilization of oxygen scavengers

## Slide 74: Nonenzymatic browning reactions

## Slide 75: Nonenzymatic browning reactions
Nonenzymatic browning, or in other words Maillard reaction, is one of the major deteriorative chemical reactions
It occur during storage of dried and concentrated foods

## Slide 76: Nonenzymatic browning reactions
Nonenzymatic browning reaction can be divided into three stages:
  (1) early Maillard reactions involving a simple condensation between a reducing sugar and an amine (usually a protein or amino acid) without browning
  (2) advanced Maillard reactions that lead to the formation of volatile or soluble substances
  (3) final Maillard reactions leading to insoluble brown polymers

## Slide 77: Color changes

## Slide 78: Color changes in tomatoes
Oxidation of lycopene, a red/orange carotenoid pigment in tomatoes, causes an adverse colour change from red to brown and affects flavour
In canned tomato products this can be minimised by using plain unlacquered can
Residual oxygen is consumed by tin dissolution into the product, minimising product oxidation that would otherwise lead to quality loss
However, the extent of dissolution of tin into the product needs to be taken into account in the assigned shelf life of the product as the maximum permitted level of tin in canned foods in the UK is 200mg kg−1

## Slide 79: Color changes in fresh meats
Oxygenated myoglobin, oxymyoglobin, is the pigment in raw meat that is responsible for the bright attractive red colour, which consumers associate with freshness and good eating quality
In conventionally packed fresh beef, meat on a plastic tray is overwrapped with a highly gas permeable plastic material which allows an almost unrestricted supply of oxygen to the myoglobin, favouring the red colour

## Slide 80: Color changes in fresh meats
By vacuum packaging fresh beef, the reduced oxygen level in the pack results in a considerable increase in shelf life, however, the meat colour becomes purple, due to myoglobin being converted to the reduced form, which most consumers are not familiar with
By using MAP, with a gas mixture of about 80% oxygen, the bright red colour maintains. 20% life can be extended to approximately 2–3 times that of conventionally packed fresh beef.

## Slide 82: Color changes in cured meat products
Nitrosohemochrome is the pigment responsible for the pink colouration of cooked cured meats.
This pigment fades rapidly on exposure to air (oxygen) and light
Therefore vacuum packaging or MAP is generally used to achieve the desired shelf life of cooked cured meats
The oxygen content must be less than 0.3%
In MAP, a commonly used mixture is 60% nitrogen and 40% carbon dioxide

## Slide 83: Flavor changes

## Slide 84: Flavor changes
In fruits and vegetables, enzymatically generated compounds derived from long-chain fatty acids play an extremely important role in the formation of characteristic flavors
In addition, these types of reactions can lead to important off-flavors
Enzyme-induced oxidative breakdown of unsaturated fatty acids occurs extensively in plant tissues. This reaction results in two important phonomenons
  Formation of characteristic aromas associated with some ripening fruits
  Distruption of tissues (e.g. enzymatic browning reaction results in tissue softening as well as formation of brown color complex)

## Slide 85: Flavor changes
As is well-known that fats and oils are crucial compounds in the development of off-flavors through autoxidation
Particularly, aldehydes and ketones are the main volatiles from autoxidation, and these compounds can cause painty, fatty, metallic, papery, and candlelike flavors in foods when their concentrations are sufficiently high
On the other side, many of the desirable flavors of cooked and processed foods derive from modest concentrations of these compounds

## Slide 86: Flavor changes
What is the importance of packaging in terms of flavor changes?
The permeability of packaging materials plays a crucial role in terms of two conditions:
  Preservation of desirable volatile components within packages
  Prevention of undesirable components, which can enter through the package from the ambient atmosphere

## Slide 87: Nutritional changes

## Slide 88: Nutritional changes
Chemical reactions have harmful effect on nutritive value of foods
The undesirable changes in nutritional compounds of foods negatively affect sensory and textural quality
There are four important factors that influence nutrient degradation: light, O2 concentration, temperature, and water activity

## Slide 89: Nutritional changes
Light
O2 concentration
Temperature
Water activity
It is important to note that these factors can be controlled by correct packaging conditions

## Slide 90: References
Coles R. et al. (2003). Food Packaging Technology. Blackwell Publishing and CRC Press. 368 pages
Robertson, G.L. (2010). Food Packaging and Shelf Life: A Practical Guide. CRC Press Taylor&Francis Group. 408 pages