## Slide 1: ELECTROTHERAPY
Dr. Pınar Can
pcan@ankara.edu.tr

## Slide 2: Definition
There are many different terminology in electrical stimulation
Examples; galvanic current, faradic current, diadynamic current, high voltage, low voltage, low frequency, medium frequency, transcutaneous electrical nerve stimulation (TENS), electrical muscle stimulation (EMS), functional electrical stimulation (FES), Russian stimulation, and interferential stimulation.
https://www.researchgate.net/profile/Maijke-Van-Bloemendaal/publication/308796211/figure/fig2/AS:413198353223683@1475525572182/The-functional-electrical-stimulation-device-including-two-cuffs-a-foot-switch-and-a.png

## Slide 3
TENS has been widely used to identify stimulators that modify pain,
NMES or EMS has been identified with muscle reeducation, prevention of muscle atrophy, and enhanced joint movement.
If the muscle is innervated by a motor nerve > NMES
when a muscle is denervated and requires direct muscle fiber activation through electrical stimulation > EMS

## Slide 4
NMES is the administration of an electrical current generated by a stimulator that travels through leads to electrodes placed on the skin to depolarize the motor nerve and produce a skeletal muscle contraction.
Stimulation of motor end plates with electrical current causes nerve depolarization and subsequent activation of muscle fibers.

## Slide 5: Basic Principles of Electrical Stimulation
The emergence of a number of biological events in cells, which are the building blocks of the organism, is partially or completely dependent on the membrane potential.
Intracellular (-), extracellular (+)
Electrical currents change this membrane potentials and lead to an action potential
By means of this action potentials, muscles contract

## Slide 6
Three types of currents are commonly used:
  Continuous direct current (DC) > A
  Continuous alternating current (AC) > B
  Pulsed current (either AC or DC) > C
Electrical Current/Waveforms
Levine and Bockstahler, 2014

## Slide 7
Continuous direct current is a unidirectional electrical current that flows for 1 second or longer
Alternating current changes the direction of flow at least once every second.
Continuous direct current (galvanic current) is used only for iontophoresis in clinical practice.
Pulsed current consists of a unidirectional or bidirectional flow of charges (DC or AC) that periodically stops for a limited time period.
All NMES devices are pulsed current stimulators.

## Slide 8: Aims
To increase muscle strength,
muscle retraining,
To increase range of motion (ROM),
correction of structural abnormalities,
To improve muscle tone,
To enhance function,
https://www.globusvet.it/wp-content/uploads/2018/12/Tens01-LOW.jpg

## Slide 9
pain control,
To accelerate wound healing,
edema reduction,
muscle spasm reduction,
enhancing transdermal administration of medication (iontophoresis)
https://www.pawsitivestepsrehab.com/blog/wp-content/uploads/2016/12/TENS-Herc-800x600.jpg
https://international.chattgroup.com/sites/default/files/styles/product_detail/public/chatt_products/id_2756_detail3_4.jpg?itok=h-rh3tyV

## Slide 10
https://horse-canada.com/wp-content/uploads/2015/07/2996.jpg
Effects of electrical stimulation
At the beginning and as a result of each application, the electrical potential of the cell membranes changes.
It causes a muscle contraction by depolarizing the motor nerve with an electrical current delivered via electrodes placed on the skin.

## Slide 11
They provide analgesic effects through sensory blockade that caused by stimulating the nerves.
Some currents have trophic (growth stimulating) effects. This effect occurs with vasodilation and an increase in blood supply.
Application of electrical stimulation for cocontraction of the cranial and caudal thigh muscles (Levine and Bockstaler, 2014) .

## Slide 12
It decreases muscle spasm.
It has edema-reducing effects.
Muscles that are not disconnected from the nerve can be stimulated with low levels of low frequency currents.
It can be used to increase the strength of a normal muscle, but is not as effective as active exercise.
Application electrodes for chronic pain using flexible E-pads because of elbow dysplasia (Levine and Bockstaler, 2014)

## Slide 13
To prevent muscle atrophy in patients with neurological damage,
to stimulate motor recovery and strengthening,
to provide retraining of muscles
to diminish joint contractures
Application of electrodes for lumbar pain utilizing flexible E-pads (Levine and Bockstaler, 2014)

## Slide 14: Iontophoresis
Iontophoresis is a process of transdermal drug delivery by use of a voltage gradient on the skin.
Molecules are transported across the stratum corneum by electrophoresis and electroosmosis, and the electric field can also increase the permeability of the skin.
https://images-na.ssl-images-amazon.com/images/I/819IyswjhSL._SL1500_.jpg

## Slide 15
Positive ions
Cefazolin
Dexamethasone
Hyaluronate
Idoxirudin
Lidocaine
Magnesium
Zinc
Negative ions
Chloride
Ciproflaxacin
Gentamicin
Iodine
Ketocanazole
Salicylate
Tobramycin

## Slide 16: Indications and Contraindications for NMES
Indications;
  fracture repair, ACL reconstruction, and meniscal debridement or repair
  patients with neurologic conditions, such as cerebrovascular accidents, closed head injuries, spinal cord injuries, or other neurologic disease involving paralysis or paresis
Niebaum et al., 2018

## Slide 17
Contraindications;
  High-intensity stimulation directly over the heart
  In animals with pacemakers
  In animals with seizure disorders
  Over areas of thrombosis or thrombophlebitis
  Over infected areas or neoplasms
  Over the carotid sinus
  Any time active motion is contraindicated
  Over the trunk during pregnancy

## Slide 18
Be careful;
  In areas with impaired sensation
  In areas of skin irritation or damage
  Near electronic sensing devices such as ECG monitors (possible interference)
Niebaum et al., 2018

## Slide 19: References
Niebaum K, McCauley L, Medina C (2018) Rehabilitation physical modalities, In; Canine Sports Medicine and Rehabilitation, editors; Chris Zink and Janet B. Van Dyke, 2nd edition, Wiley Blackwell
Levine D, Bockstaler B (2014) Electrical stimulation, In; Canine Rehabilitation and Physical Therapy, editors Darryl Millis, David Levine, 2nd Edition, Saunders, Philadelphia, USA.