## Slide 1: Cheese Technology - 1
Res. Asst, DVM Bahar ONARAN
Ankara University, Faculty of Veterinary Medicine
Department of Food Hygiene and Technology

## Slide 2: Cheese Definitions
Cheese comes in many varieties.
The variety determines the ingredients, processing, and characteristics of the cheese.
Cheese can be made using pasteurized or raw milk.
Cheese made from raw milk imparts different flavors and texture characteristics to the final product.
Prior to cheese making to destroy some of the pathogen microorganisms and provide better conditions for the cheese cultures.

## Slide 3: Cheese Definitions
Cheese can be broadly categorized as acid or rennet cheese, and natural or process cheeses.
Acid cheeses are made by adding organic acids to the milk to cause the proteins to coagulate.
Fresh cheeses, such as cream cheese or queso fresco, are made by direct acidification.
Most types of cheese, such as cheddar or Swiss, use rennet (an enzyme) in addition to the starter cultures to coagulate the milk.
The term “natural cheese” is an industry term referring to cheese that is made directly from milk.
Process cheese is made using natural cheese plus other ingredients that are cooked together to change the textural and/or melting properties and increase shelf life.

## Slide 4: Ingredients
The main ingredient in cheese is milk.
 cow, goat, sheep, water buffalo or a blend of these milks.
The type of coagulant used depends on the type of cheese desired.
 For acid cheeses, an acid source such as acetic acid (the acid in vinegar) or gluconodelta-lactone (a mild food acid) is used.
 For rennet cheeses, calf rennet or, more commonly, a rennet produced through microbial bioprocessing is used.
Calcium chloride is added to the cheese to improve the coagulation properties of the milk.

## Slide 5: Ingredients
Flavorings may be added depending on the cheese. Some common ingredients include herbs, spices, hot and sweet peppers, horseradish, and port wine.

## Slide 6: Starter Cultures
Cultures for cheese making are called lactic acid bacteria (LAB) because their primary source of energy is the lactose in milk and their primary metabolic product is lactic acid.
There is a wide variety of bacterial cultures available that provide distinct flavor and textural characteristics to cheeses.
Starter cultures are used early in the cheese making process to assist with coagulation by lowering the pH prior to rennet addition.
The metabolism of the starter cultures contribute desirable flavor compounds, and help prevent the growth of spoilage organisms and pathogens.
Typical starter bacteria include Lactococcus lactis subsp. lactis or cremoris, Streptococcus salivarius subsp. thermophilus, Lactobacillus delbruckii subsp. bulgaricus, and Lactobacillus helveticus.

## Slide 7
Lactococcus lactis spp. lactis
Lactococcus lactis spp. cremoris
Streptococcus salivarius spp. thermophilus
Lactobacillus delbrueckii spp. bulgaricus
White cheese
Kaşar cheese

## Slide 8
Lactococcus lactis spp. lactis
Lactococcus lactis spp. cremoris
Leuconostoc citrovorum
Cottage cheese
Brie, Camambert
Lactococcus lactis spp. lactis
Lactococcus lactis spp. cremoris
Lactococcus lactis spp. diacetylactis
Leuconostoc citrovorum
Penicillum camamberti

## Slide 9
Cheddar
Lactococcus lactis spp. lactis
Lactococcus lactis spp. cremoris
Leuconostoc spp.
Lactococcus lactis spp. lactis
Streptococcus salivarius spp. thermophilus
or
Lactobacillus delbrueckii spp. bulgaricus
and
Enterococcus faecalis
Mozzarella

## Slide 10
Adjunct cultures are used to provide or enhance the characteristic flavors and textures of cheese.
Common adjunct cultures added during manufacture include;
Lactobacillus casei and Lactobacillus plantarum for flavor in Cheddar cheese,
Propionibacterium freudenreichii for eye formation in Swiss.
Brevibacterium linens of gruyere, brick and limburger cheeses.
Yeasts and molds are used in some cheeses to provide the characteristic colors and flavors of some cheese varieties;
Torula yeast is used in the smear for the ripening of brick and limburger cheese.
Penicillium camemberti in camembert and brie, and Penicillium roqueforti in blue cheeses.

## Slide 11: General Manufacturing Procedure
The temperatures, times, and target pH for different steps, the sequence of processing steps, the use of salting or brining, block formation, and aging vary considerably between cheese types.
The following flow chart provides a very general outline of cheese making steps:

## Slide 12: General Cheese Processing Steps
Standardization of the Milk
Pasteurization of the Milk
Cool Milk
Inoculate with Starter Bacteria and Ripen
Add Rennet and Form Curd
Cut Curd and Heat
Drain Whey
Texture Curd special cloth
Dry Salt or Brine
Form Cheese into Blocks
Store and Age
Package

## Slide 13
1. Standardize Milk
Milk is often standardized before cheese making to optimize the protein to fat ratio to make a good quality cheese with a high yield.
2. Pasteurize/Heat Treat Milk
Depending on the desired cheese, the milk may be pasteurized or mildly heat-treated to reduce the number of pathogen organisms and improve the environment for the starter cultures to grow. Some varieties of milk are made from raw milk so they are not pasteurized or heat-treated. Raw milk cheeses must be aged for at least 60 days to reduce the possibility of exposure to disease causing microorganisms (pathogens) that may be present in the milk.
3. Cool Milk
After pasteurization, milk is cooled to 30-35 °C to bring it to the temperature needed for the starter bacteria to grow.
If raw milk is used the milk must be heated to 30-35 °C.

## Slide 14
4. Inoculate with Starter Bacteria and Ripen
The starter cultures are added to the milk and held at 30-35 °C for 30 minutes to ripen. The ripening step allows the bacteria to grow and begin fermentation, which lowers the pH and develops the flavor of the cheese.
5. Add Rennet and Form Curd
The rennet is the enzyme that acts on the milk proteins to form the curd. After the rennet is added, the curd is not disturbed for approximately 30 minutes so a firm coagulum forms.
6. Cut Curd and Heat
The curd is allowed to ferment until it reaches pH 4.6. The curd is then cut with cheese knives into small pieces and heated to 100°F (38°C). The heating step helps to separate the whey from the curd.

## Slide 15
7. Drain whey
The whey is drained from the vat and the curd forms a mat.
8. Texture curd
The curd mats are cut into sections and piled on top of each other and flipped periodically. This step is called cheddaring. Cheddaring helps to expel more whey, allows the fermentation to continue until a pH of 5.1 to 5.5 is reached, and allows the mats to "knit" together and form a tighter matted structure. The curd mats are then milled (cut) into smaller pieces.
9. Dry Salt or Brine
For cheddar cheese, the smaller, milled curd pieces are put back in the vat and salted by sprinkling dry salt on the curd and mixing in the salt. In some cheese varieties, such as mozzarella, the curd is formed into loaves and then the loaves are placed in a brine (salt water solution).

## Slide 16
10. Form Cheese into Blocks
The salted curd pieces are placed in cheese hoops and pressed into blocks to form the cheese.
11. Store and Age
The cheese is stored in coolers until the desired age is reached. Depending on the variety, cheese can be aged from several months to several years.
12. Package
Cheese may be cut and packaged into blocks or it may be waxed.

## Slide 17: Coagulation Methods for Making Cheese
Up to 80% of all the protein in cow’s milk is associated with the casein micelles.
The molecules of casein are negatively charged, which keeps the very hydrophobic micelles happy and floating around in the water.
Our goal is to get the micelles interacting with each other so that they will coagulate and form a gel (the curds).
We can do this using one of the following methods.

## Slide 18: Coagulation Methods for Making Cheese
Enzyme-Mediated Coagulation (White and Kaşar cheese)
Acid-Mediated Coagulation (Cottage, Quark, cream cheese)
Temperature-Mediated Coagulation (Lor cheese)
The method that you choose determines what type of cheese you will be making.
For instance, using heat to coagulate will kill off all the microorganisms in your milk. This is bad news for cheeses such as swiss and camembert, which rely on additional microorganisms munching away at the cheese during the ripening process. However, temperature-coagulated cheeses are ready in under a few hours whereas the rennet-coagulated cheeses usually require months of aging time.
No matter the method, though, coagulation of milk micelles is an excellent example of how pH, temperature, and proteases can affect protein-protein interactions.

## Slide 19: 1. Enzyme-Mediated Coagulation
This process involves the use of rennet, which is used to make most cheeses.
The pH of the milk drops to the acidic range 5.8-6.6
Rennet can be composed of one or more proteases, including pepsin, chymosin, and proteses.

## Slide 20: Mechanism for the coagulation of the casein by rennin:
is a two-stage process.
In the first stage;
Rennin splits a specific bond in the amino acid chain of the kappa-casein macromolecule converting into a para-kappa-casein and glyco-macropeptide.
This causes an imbalance in the intermolecular forces in the milk system, and the hydrophilic (water-loving) macropeptides are released into the whey.
Unlike kappa-casein, the para-kappa-casein does not have the ability to stabilize the micellular structure to prevent the calcium-insoluble caseins from coagulation.

## Slide 21
In the second stage;
Colloidal calcium phophate bridges within the casein micellular structure are formed in the presence of the soluble calcium, resulting in the three-dimensional curd structure.
Kappa-casein
para-kappa-casein
(colloidal)
glyco-macropeptide
(soluble)
Para-kappa-casein
dicalcium-para-casein
(curd)
Ca+2
rennin
+

## Slide 22: 2. Acid-Mediated Coagulation
In this process, the pH of the milk drops to the acidic range (pH < 4.6).
This alters the interaction of the calcium phosphate molecules with the micelles, and they begin to leak out of the globs.
Once this happens, the micelles become destabilized and begin to interact with each other, forming a gel matrix.
The source of the acid can be exogenous (directly adding acid such as citric acid to the milk) or endogenous (from the lactic acid produced by bacteria).

## Slide 23: Mechanism for the coagulation of the casein by organic acids:
Milk, in its natural state, is negatively charged.
The negative charge permits the dispersion of casein in the milk.
When an acid is added to milk, the H+ concentration neutralizes the negatively charged casein micelles.
When milk is acidified to pH 4.6, the isoelectric point (the point at which all charges are neutral) of casein, an isoelectric precipitate known as acid casein is formed.

## Slide 24: 3. Temperature-Mediated Coagulation
Simply heat up a vat of milk to boiling and get precipitated curds.
Heating whey  lor cheese
Heating whole milk  çökelek
Heating whey and getting precipitated curds.

## Slide 25
When the heat gets turned up, the balance of insoluble and soluble calcium begins to shift toward more insoluble calcium.
In addition, the proteins that are floating around in the whey begin to unfold – at which point they will start interacting with the proteins that are on the surface of the micelles.
This reduces the reactivity of the micelles, and makes it so the micelle proteins will no longer interact with each other.
Temperature

## Slide 26: Rennet
is a complex of enzymes produced in the stomachs of ruminant mammals.
Chymosin, its key component, is a protease enzyme that curdles the casein in milk.
This helps young mammals digest their mothers' milk. Rennet can also be used to separate milk into solid curds for cheese making and liquid whey.
In addition to chymosin, rennet contains other important enzymes such as pepsin and a lipase.
Rennet is used in the production of most cheeses. The mammal's digestive system must be accessed to obtain its rennet.
Non-animal alternatives for rennet are also available.

## Slide 27: Alternative sources
Because of the limited availability of mammalian stomachs for rennet production, cheese makers have sought other ways to coagulate milk since at least Roman times.
The many sources of enzymes that can be a substitute for animal rennet range from plants and fungi to microbial sources.
Cheeses produced from any of these varieties of rennet are suitable for lactovegetarians.
Fermentation-produced chymosin is used more often in industrial cheese making in North America and Europe today because it is less expensive than animal rennet.

## Slide 28: Extraction of calf rennet
Calf rennet is extracted from the inner mucosa of the fourth stomach chamber (the abomasum) of young, unweaned calves as part of livestock butchering.
If rennet is extracted from older calves (grass-fed or grain-fed), the rennet contains less or no chymosin, but a high level of pepsin and can only be used for special types of milk and cheeses.
Traditional method
Dried and cleaned stomachs of young calves are sliced into small pieces and then put into salt water or whey, together with some vinegar or wine to lower the pH of the solution. After some time (overnight or several days), the solution is filtered. The crude rennet that remains in the filtered solution can then be used to coagulate milk. About 1 g of this solution can normally coagulate 2 to 4 L of milk.
Modern method
Deep-frozen stomachs are milled and put into an enzyme-extracting solution. The crude rennet extract is then activated by adding acid; the enzymes in the stomach are produced in an inactive form and are activated by the stomach acid. The acid is then neutralized and the rennet extract is filtered in several stages and concentrated until reaching a typical potency of about 1:15,000; meaning 1 g of extract can coagulate 15 kg of milk.
One kg of rennet extract has about 0.7 g of active enzymes – the rest is water and salt and sometimes sodium benzoate (E211), 0.5% - 1.0% for preservation. Typically, 1 kg of cheese contains about 0.0003 g of rennet enzymes.

## Slide 29: Rennet from Vegetable sources
Many plants have coagulating properties.
In the Iliad that the Greeks used an extract of fig juice to coagulate milk.
Galium, dried caper leaves, nettles, thistles, mallow, and ground ivy can be used as a rennet.
Enzymes from thistle or Cynara are used in some traditional cheese production in the Mediterranean.
Phytic acid, derived from unfermented soybeans, or fermentation-produced chymosin (FPC) may also be used.

## Slide 30: Rennet from Microbial sources
Kluyveromyces lactis (formerly Saccharomyces lactis) is a yeast which has the ability to assimilate lactose and convert it into lactic acid.
is used for genetic studies and industrial applications.
Escherichia coli K-12 is grown in fermenters to produce chymosin (rennet) on a commercial scale.
Aspergillus niger var awamori and Rhizomucor miehei are the species of fungus. They are commercially used to produce enzymes which can be used to produce a microbial rennet to curd milk and produce cheese.
Cheeses produced this way are suitable for vegetarians, provided no animal-based alimentation was used during the production.

## Slide 31: Calcium Chloride
When the casein micelles are disrupted in the pasteurization process, the calcium that was previously held in the gel matrix gets leached out into the whey and we get crappy curd formation.
We fix this problem by adding calcium chloride to the milk when we pour it in the cheese vat.

## Slide 32: Calcium Chloride
Pasteurization thus makes for a looser curd network. When we add calcium chloride, the calcium balance begins to shift back toward the soluble forms of calcium, which makes the casein micelles very happy.
This increases their surface reactivity, so we can get stronger curd formation.
Better Milk = Better Cheese
If you want to make cheese you need good milk.
Just make sure that you’re not using ultra-pasteurized milk!
Supplement it with calcium chloride to stabilize the curd if you want (it’s not completely necessary), and you’ll be good to go 

## Slide 33: Why we add calcium chloride?
Improving the coagulation properties of the milk.
Formation of tight and elastic curd.
Improving the cheese yield
because of the losses with the whey will decreases.
Draining whey will be more easier.
Improving sticking to the cloth.

## Slide 34: Cutting time selection
It depends on rheological and microstructural properties of gels, such as coagulum ﬁrmness and rearrangement capability that, inturn, depend on coagulation factors, milk composition, and milk pretreatment.
For this reason, CT selection greatly affects moisture, yield, and quality of cheese and whey fat losses.
Cutting time is a range between 45 - 60 min.