## Slide 1: Cheese Technology 2
Res. Asst, DVM Bahar ONARAN
Ankara University, Faculty of Veterinary Medicine
Department of Food Hygiene and Technology

## Slide 3: White Cheese Processing Steps
Standardization of the Milk
Pasteurization of the Milk (2 min. at 72 °C)
Cool Milk (until 35-37 °C)
Calcium cloride (20 g to 100 kg milk mix)
Inoculate with starter bacteria (% 2)

## Slide 4
6. Add Rennet
Rennet strenght is usually between 1/10.000 – 1/15.000
1/15.000: means 1 unit of rennet will set 15,000 units of milk at a standard time and temp.
 20 ml to 100 kg milk mix

## Slide 5
7. Cut Curd
Proper cutting is extremely important to both quality and yield.
Improper cutting and handling the curd results in the loss of fines, that is, small curd particles which are not recovered in the cheese.
Therefore, both fat and protein losses occur when shattered curd results in fines too small to be recovered in the cheese.
The freshly cut curd is left for 10 - 15 min to expel little whey.
15 min X 4 = 60 min

## Slide 6
7. Cut Curd
Curd size  bigger than in Kaşar cheese.
Curd size has a great influence on moisture retention.
Hence, there is an obvious relationship between cheese moisture and the prescribed curd size:
High temperature and low moisture varieties such as Italian hard cheese require the smallest curd.
Cutting continues until the curd cutting is the size of rice grains.
Medium moisture cheeses like most washed varieties and Cheddar are cut to Omega cm cubes.
High moisture varieties like soft ripened cheese are cut with 2 cm knives or the curd is simply broken sufficiently to be dipped into forms.
Small curd size will result in greater fat and SNF recovery because large curds tend to get crushed resulting in the loss of 'fines'. Smaller curds will also dry out faster and, therefore, other factors such as cooking temperature and stirring out may have to be adjusted according to curd size.

## Slide 7
8. Drain Whey (sineresis) acidity increases 12-13 SH
9. Texture Curd special cloth
10. Brine (% 16 salted water)
11. Form Cheese into Blocks
12. Store
13. Packaging

## Slide 8: Kaşar Cheese Processing Steps
Standardization of the Milk
Heating Milk (until 40-45 °C)
Calcium cloride (30 g to 100 kg milk mix)
Inoculate with starter bacteria (% 2)
Add Rennet (30 ml to 100 kg milk mix)
Cut Curd (15 min X 4 = 60 min)

## Slide 9
7. Drain Whey (sineresis) acidity increases 12-13 SH
8. Heating curd (5 min. at 85 °C)
9. Boiling the curd (5 min. at 85 °C) in % 5 brine solution
10. Working the curd dough
11. Form cheese into blocks
12. Store
13. Package

## Slide 10: Fermentation types in milk products
Lactic acid fermentation: Lactic Acid Bacteria (LAB)
Alcohol (ethanol) fermentation: Yeasts
Propionic acid fermentation: Propionic Acid Bacteria (PAB).

## Slide 11: Lactic acid fermentation:
Lactic Acid Bacteria (LAB)
is a metabolic process by which glucose and other six-carbon sugars (e.g. sucrose or lactose) are converted into cellular energy and the metabolite lactate.
It is an anaerobic fermentation reaction that occurs in some bacteria.
Yoghurt and fresh cheeses

## Slide 12: Alcohol (ethanol) fermentation:
Yeasts
is a biological process which converts sugars such as glucose, fructose, and sucrose into cellular energy, producing ethanol and carbon dioxide as by-products.
Because yeasts perform this conversion in the absence of oxygen, alcoholic fermentation is considered an anaerobic process.
Kefir, kımız

## Slide 13: Propionic acid fermentation:
Propionic Acid Bacteria (PAB)
 Propionibacterium freudenreichii spp. shermanii
Emmental cheese and Swiss-type cheese

## Slide 14: Kefir
Kefir is an acidic-alcoholic fermented milk product with little acidic taste and creamy consistency that was originated in the Balkans, in Eastern Europe, and in the Caucasus.
Kefir can be produced by fermenting milk with commercial freeze-dried kefir starter cultures, traditional kefir grains, and the product that remains after the removal of kefir grains.

## Slide 15
Kefir grains are a kind of yogurt starter, which are white to yellow – white, gelatinous, and variable in size (varying from 0.3–3.5 cm in diameter) and are composed by a microbial symbiotic mixture of;
Lactic Acid Bacteria – LAB (108 cfu/g),
Yeast (106-107 cfu/g),
Acetic Acid Bacteria – AAB (105 cfu/g) that stick to a polysaccharide matrix.
After successive fermentations, kefir grains can break up to new generation grains, which have the same characteristics as the old ones.

## Slide 16
More than 23 different yeast species have been isolated from kefir grains and from fermented beverages of different origins.
However, the predominant species are;
Saccharomyces cerevisiae,
S. unisporus,
Candida kefyr,
Kluyveromyces marxianus ssp. marxianus.