## Slide 2: 2. Additional provisions for transport by road or rail
2.1. Vehicles in which animals are transported shall be clearly and visibly marked indicating the presence of live animals, except when the animals are transported in containers
2.2. Road vehicles shall carry suitable equipment for loading and unloading.
2.3. When assembling trains and during all other movement of rail wagons every precaution shall be taken to avoid jolting of a rail wagon containing animals.

## Slide 3
3. Additional provisions for transport on roll-on-roll-off vessels
3.1. Before loading onto a vessel the master shall verify that when vehicles are loaded:
(a) on enclosed decks, the vessel is equipped with an appropriate forced ventilation system and it is fitted with an alarm system and an adequate secondary source of power in case of failure;
(b) on open decks, adequate protection from sea water is provided.
3.2. Road vehicles and rail wagons shall be equipped with a sufficient number of adequately designed, positioned and maintained securing points enabling them to be securely fastened to the vessel. Road vehicles and rail wagons shall be secured to the vessel before the start of the sea journey to prevent them being displaced by the motion of the vessel.

## Slide 4
4. Additional provisions for transport by air
4.1. Animals shall be transported in containers, pens or stalls appropriate for the species, which comply with International Air Transport Association (IATA) live animals Regulations, in its version referred to in Annex VI.
4.2. Animals shall be transported only in conditions where air quality, temperature and pressure can be maintained within an appropriate range during the entire journey, having regard to the species of animals.

## Slide 5
5. Additional provisions for transport in containers
5.1. Containers in which animals are transported shall be clearly and visibly marked, indicating the presence of live animals and with a sign indicating the top of the container.
5.2. During transport and handling, containers shall always be kept upright and severe jolts or shaking shall be minimised. Containers shall be secured so as to prevent displacement due to the movement of the means of transport.
5.3. Containers of more that 50 kg shall be equipped with a sufficient number of adequately designed, positioned and maintained securing points enabling them to be securely fastened to the means of transport where they are to be loaded. Containers shall be secured to the means of transport before the start of the journey to prevent displacement due to the motion of the means of transport.

## Slide 6: TRANSPORT PRACTICES
1. Loading, unloading and handling
1.1. Due regard shall be paid to the need of certain categories of animals, such as wild animals, to become acclimatised to the mode of transport prior to the proposed journey.
1.2. Where loading or unloading operations last for more than four hours, except for poultry:
(a) appropriate facilities shall be available in order to keep, feed and water the animals outside the means of transport without being tied;
(b) operations shall be supervised by an authorised veterinarian and particular precautions shall be taken to ensure that the welfare of the animals is properly maintained during these operations.

## Slide 7: Facilities and procedures
1.3. Facilities for loading and unloading, including the flooring, shall be designed, constructed, maintained and operated so as to:
(a) prevent injury and suffering and minimise excitement and distress during animal movements as well as to ensure the safety of the animals. In particular, surfaces shall not be slippery and lateral protections shall be provided so as to prevent animals from escaping;
(b) be cleaned and disinfected.

## Slide 8
1.4. (a) Ramps shall not be steeper than an angle of 20 degrees, that is 36,4 % to the horizontal for pigs, calves and horses and an angle of 26 degrees 34 minutes, that is 50 % to the horizontal for sheep and cattle other than calves. Where the slope is steeper than 10 degrees, that is 17,6 % to the horizontal, ramps shall be fitted with a system, such as provided by foot battens, which ensure that the animals climb or go down without risks or difficulties;
(b) lifting platforms and upper floors shall have safety barriers so as to prevent animals falling or escaping during loading and unloading operations.

## Slide 9
1.5. Goods which are being transported in the same means of transport as animals shall be positioned so that they do not cause injury, suffering or distress to the animals.
1.6. Appropriate lighting shall be provided during loading and unloading.
1.7. When containers loaded with animals are placed one on top of the other on the means of transport, the necessary precautions shall be taken:
(a) to avoid, or in the case of poultry, rabbits and fur animals, to limit urine and faeces falling on the animals placed underneath;
(b) to ensure stability of the containers;
(c) to ensure that ventilation is not impeded.