## Slide 1: INTERPRETING ECG
Dr. Etkin ŞAFAK

## Slide 2: LEADS
To understand electrocardiography, leads need to be understood
Electrodes placed on the skin measure the direction of electrical current discharged by the heart
That current is then transformed into waveforms
An ECG records information about those waveforms from different views or perspectives.
Those perspectives are called leads

## Slide 3: LEADS
A lead provides a view of the heart’s electrical activity between one positive pole and one negative pole.
Between the two poles lies an imaginary line representing the lead’s axis, a term that refers to the direction of the current moving through the heart.
The direction of the current affects the direction in which the waveform points on an ECG.
When no electrical activity occurs or the activity is too weak to measure, the waveform looks like a straight line, called an isoelectric waveform.

## Slide 4: All about leads
Electrode placement is different for each lead, and different leads provide different views of the heart.
A lead may be chosen to highlight a particular part of the ECG complex or the electrical events of a specific cardiac cycle.
Leads II, V1, and V6 are among the most commonly used leads for monitoring,
It is necessary to adjust the leads according to the patient’s condition.

## Slide 5: The 12-lead ECG
A 12-lead ECG records information from 12 different views of the heart and provides a complete picture of electrical activity.
These 12 views are obtained by placing electrodes on the patient’s limbs and chest.
The limb leads and the chest, or precordial, leads reflect information from the different planes of the heart

## Slide 6: LIMB LEADS
The six limb leads—I, II, III, augmented vector right (aVR), augmented vector left (aVL), and augmented vector foot (aVF)—provide information about the heart’s frontal (vertical) plane.
Leads I, II, and III require a negative and positive electrode for monitoring, which makes those leads bipolar.
The augmented leads record information from one lead and are called unipolar.

## Slide 7: Bipolar Leads
All bipolar leads have a third electrode, known as the ground, to prevent electrical interference from appearing on the ECG recording
Lead I provides a view of the heart that shows current moving from right to left.
Because current flows from negative to positive, the positive electrode for this lead is placed on the left arm; the negative electrode is placed on the right arm

## Slide 8: Bipolar Leads
Lead II produces a positive deflection.
Place the positive electrode on the patient’s left leg and the negative electrode on the right arm.
Lead II tends to produce a positive, highvoltage deflection, resulting in tall P, R, and T waves.
This lead is commonly used for routine monitoring
Lead III produces a positive deflection. The positive electrode is placed on the left leg; the negative electrode, on the left arm.
The axes of the three bipolar limb leads—I, II, and III—form a triangle around the heart and provide a frontal plane view of the heart.

## Slide 9: The «a» leads
aVR, aVL, and aVF are called augmented leads because the small waveforms that normally would appear from these unipolar leads are enhanced by the ECG.
They measure electrical activity between one limb and a single electrode.
In lead aVR, the positive electrode is placed on the right arm and produces a negative deflection because the heart’s electrical activity moves away from the lead.
In lead aVL, the positive electrode is on the left arm and produces a positive deflection on the ECG.
In lead aVF, the positive electrode is on the left leg and produces a positive deflection.

## Slide 10: The «a» leads
These three limb leads also provide a view of the heart’s frontal plane.
Lead aVR provides no specific view of the heart.
Lead aVL shows electrical activity coming from the heart’s lateral wall.
Lead aVF shows electrical activity coming from the heart’s inferior wall.

## Slide 11: PRECORDIAL LEADS
The six precordial or V leads—V1, V2, V3, V4, V5, and V6—provide information about the heart’s horizontal plane.
The precordial leads are also unipolar, requiring only a single electrode.
The opposing pole of those leads is the center of the heart as calculated by the ECG.

## Slide 12: Precordial Limbs
Lead V1 electrode is placed on the right side of the sternum at the fourth intercostal rib space.
Lead V2 is placed at the left of the sternum at the fourth intercostal rib space.
Lead V3 goes between V2 and V4.
Lead V4 is placed at the fifth intercostal space at the midclavicular line and produces a biphasic waveform.
Lead V5 is placed at the fifth intercostal space at the anterior axillary line.
Lead V6, the last of the precordial leads, is placed level with V4 at the midaxillary line

## Slide 13: Recording ECG
Place the patient in right lateral recumbency.
Part the hair.
Attach the electrodes to the skin just proximal (above) to the elbows and stifles.
Wet the electrodes with alcohol (do not soak). If panting or excessive motion, move the front limb leads further distal on the limb.
Check the speed, amplitude, and other settings.

## Slide 14: Interpreting ECG
Waveforms produced by the heart’s electrical current are recorded on graphed ECG paper by a stylus.
ECG paper consists of horizontal and vertical lines forming a grid.
A piece of ECG paper is called an ECG strip or tracing

## Slide 15: Interpreting ECG

## Slide 16: Standart deflection
Standard calibration of the ECG is 10mm/mV
At this calibration, 1 miliVolt calibration signal is expected to produce a rectangle of 10 mm height and 5 mm width.

## Slide 17: Standart deflection
When ECG waves are tall, the R or S waves may extend into the QRS complexes above or below them.
To prevent this superimposition, the whole ECG may be calibrated at 5mm/mV .

## Slide 18: PAPER SPEED-measurement of time
The horizontal axis of the ECG strip represents time.
If recording at 50 mm/sec: 0.02 sec= 1 little box
If recording at 25 mm/sec: 0.04 sec=1 little box_

## Slide 19: Methodical Approach to the ECG
Start at the left and go through each complex, identifying known waves.
HR -- fast or slow
Rhythm -- regular or irregular
Identify P waves
– normal or abnormal configuration
– is there a P for every QRS
Measurements
– P-R interval, Q-T interval, S-T segment, etc

## Slide 20: ANY QUESTION?