## Slide 1: INTERPRETING ECG
Dr. Etkin ŞAFAK

## Slide 2: ECG WAVES

## Slide 3: The P Wave
The P wave is the first component of a normal ECG waveform.
It represents atrial depolarization—conduction of an electrical impulse through the atria.

## Slide 4: The PR interval
The PR interval tracks the atrial impulse from the atria through the AV node, bundle of His, and right and left bundle branches.
The PR interval is measured from the beginning of the P wave to the beginning of the QRS complex.
Paper speed: 25 mm/sec
0.04 sec / sq x 3 squares = 0.12 sec

## Slide 5: The QRS Complex
The QRS complex is the average of the depolarization waves of the inner (endocardial) and outer (epicardial) cardiomyocytes. As the endocardial cardiomyocytes depolarize slightly earlier than the outer layers, a typical QRS pattern occurs
The letters "Q", "R" and "S" are used to describe the QRS complex
Q: the first negative deflection after the p-wave. If the first deflection is not negative, the Q is absent.
R: the positive deflection
S: the negative deflection after the R-wave
The QRS duration:

## Slide 6: The QT interval
This segment tells the total duration of the ventricular event, from when the first cell depolarizes to the repolarization of the last cell
Between the beginning of the QRS complex and the end of the T wave

## Slide 7: The T Wave
The T wave represents the repolarization of the ventricles.
There is no cardiac muscle activity during the T wave.

## Slide 8: Calculation
Speed: 50 mm/sec
Standardized deflection: 1 mV
P = 0,02 x 2 = 0,04 sec
P = 0,1 x 1 = 0,1 mV
PQ = 0,02 x 4,5 = 0,09 sec
R = 0,1 x 9 = 0,9 mV
QRS = 0,02 x 2 = 0,04 sec
T = 0,02 x 5 = 0,10 sec
T = 0,1 x 2 = 0,2 mV
QT = 0,02 x 10 = 0,20 sec

## Slide 9: Calculating the HR:
The horizontal axis of the ECG strip represents time.
If recording at 50 mm/sec:
Heart rate = 3000 / number of 1 mm boxes between 2 beats ex: 3000 / 25 = 120 bpm (Why 3000: 3000 one mm boxes = 3000 X 0.02 sec = 60 sec = 1 min)
If recording at 25 mm/sec:
Heart rate = 1500 / number of 1 mm boxes between 2 beats

## Slide 10: Calculating the HR:
Paper speed is 25 mm/sec = 1500 mm/min
Calculate the R-R interval: 18 mm
HR: 1500/18 = 83/min

## Slide 11: Mean Electrical Axis
The Mean Electrical Axis (MEA) is a simple clinical assessment that assesses the ventricular depolarization pattern, that is, the net direction of the electrical current as the heart beats.
It’s described as an angle from -180° to 180°, and is calculated using a 3-leads electrocardiogram (ECG).

## Slide 12: Mean Electrical Axis
Upon depolarization each myocardial fiber in the heart produces its own tiny vector.
The sum of all those vectors across the heart is measured by the ECG leads, which are comprised of a negative and positive pole.
These record a deflection greater than zero if the vector is moving towards the positive pole of the lead, and less than zero if moving towards the negative pole.
A vector moving perpendicular to the lead axis produces no deflection.
Using multiple leads we can develop a “picture” of the electrical activity of the heart.

## Slide 13: Mean Electrical Axis
Because ventricular depolarization accounts for the majority of the electrical activity of the heart, we need only concern ourselves with the magnitude of ventricular vectors when evaluating the MEA.
Thus we can ignore the P and T waves, and use only the QRS complex.
The sum of the complex’s positive component (R) and negative components (Q and S) give the net deflection for that complex.
If this is 0, the complex is said to be isoelectric.
This could be seen as an ECG tracing with no QRS wave or one where the magnitude of R equals the sum of the magnitudes of Q and S.

## Slide 14: Einthoven Method
Lead II = the sum of lead I and lead II.
II = III + I
Example: Lead I: R=1,2 mV, Q=0,8 mV
Lead III: R=0,6 mV, Q=0,2 mV’
What is the magnitude of the resultant vector in lead II?
II = 0,4 + 0,4  II = 0,8 mV

## Slide 15: Einthoven Method
EXMAPLE:
LI 4-0=4
LIII 10-2 =8
0
0
0
+
-
+
-
+
-
I
III
II
±0
+90
±180
+30
+60
+70

## Slide 16: Example 2

## Slide 17: Baileys Axis System
The three bipolar leads (leads I, II and III) can be shown on Einthoven’s Triangle as three arrows, each with a positive and negative pole at one limb of the dog or cat.
There are also 3 unipolar leads in ECG recordings. These are called the augmented vector leads
Adding these to the Bailey axis, we now have a complete picture of all 6 leads and their corresponding angles.
Remember that POSITIVE net deflections of a lead point towards the arrowhead, and NEGATIVE net deflections go away from the arrowhead

## Slide 18: ANY QUESTION?