## Slide 1: Chapter 3 Addressing Modes
Asst. Prof. Dr. Gazi Erkan BOSTANCI
Slides are mainly based on The Intel Microprocessors by Barry B. Brey, 2008

## Slide 2
Efficient software development for the MP requires a complete familiarity with the addressing modes employed by each instruction.
MOV (move data) instruction will be used to describe the data addressing modes.
CALL and JUMP instructions will be used to describe program memory addressing modes.
PUSH and POP instructions will be used to describe the operation of the stack memory.

## Slide 3: Data Addressing Modes
Because the MOV instruction is a very common and flexible instruction, it provides a basis for the explanation of the data-addressing modes.
Figure below illustrates the MOV instruction and defines the direction of data flow.

## Slide 4
The source is to the right and the destination is to the left, next to the opcode MOV. (An opcode, or operation code, tells the microprocessor which operation to perform.)
This direction of flow, which is applied to all instructions, is awkward at first.
  We naturally assume that things move from left to right, whereas here they move from right to left.

## Slide 5
The MOV AX, BX instruction transfers the word contents of the source register (BX) into the destination register (AX). The source never changes, but the destination always changes.
It is crucial to remember that a MOV instruction always copies the source data into the destination. The MOV never actually picks up the data and moves it.
Also, note the flag register remains unaffected by most data transfer instructions. The source and destination are often called operands.
Figure below shows all possible variations of the data-addressing modes using the MOV instruction. This illustration helps to show how each data-addressing mode is formulated with the MOV instruction and also serves as a reference on data-addressing modes.

## Slide 7
Register addressing: Register addressing transfers a copy of a byte or word from the source register or contents of a memory location to the destination register or memory location.
  Example: The MOV CX, DX instruction copies the word-sized contents of register DX into register CX.

## Slide 8
Immediate addressing: Immediate addressing transfers the source, an immediate byte, word, doubleword, or quadword of data, into the destination register or memory location.
  Example: The MOV AL, 22H instruction copies a byte-sized 22H into register AL

## Slide 9
Direct addressing: Direct addressing moves a byte or word between a memory location and a register. The instruction set does not support a memory-to memory transfer, except with the MOVS instruction.
  Example: The MOV CX, LIST instruction copies the word-sized contents of memory location LIST into register CX.

## Slide 10
Register indirect addressing: Register indirect addressing transfers a byte or word between a register and a memory location addressed by an index or base register. The index and base registers are BP, BX, DI, and SI.
  Example: The MOV AX, [BX] instruction copies the word-sized data from the data segment offset address indexed by BX into register AX.

## Slide 11
Base-plus-index addressing: Base-plus-index addressing transfers a byte or word between a register and the memory location addressed by a base register (BP or BX) plus an index register (DI or SI).
  Example: The MOV [BX+DI], CL instruction copies the byte-sized contents of register CL into the data segment memory location addressed by BX plus DI.

## Slide 12
Register relative addressing: Register relative addressing moves a byte or word between a register and the memory location addressed by an index or base register plus a displacement.
  Example: MOV AX,[BX+4] or MOV AX, ARRAY[BX].
  The first instruction loads AX from the data segment address formed by BX plus 4. The second instruction loads AX from the data segment memory location in ARRAY plus the contents of BX.

## Slide 13
Base relative-plus-index addressing Base relative-plus-index addressing transfers a byte or word between a register and the memory location addressed by a base and an index register plus a displacement.
  Example: MOV AX, ARRAY[BX+DI] or MOV AX, [BX+DI+4].
  These instructions load AX from a data segment memory location. The first instruction uses an address formed by adding ARRAY, BX, and DI and the second by adding BX, DI, and 4.

## Slide 14: Program Memory Addressing Modes
Program memory-addressing modes, used with the JMP (jump) and CALL instructions, consist of three distinct forms:
  direct,
  relative,
  and indirect.
This section introduces these three addressing forms, using the JMP instruction to illustrate their operation.

## Slide 15: Direct Program Memory Addressing
Direct program memory addressing is what many early microprocessors used for all jumps and calls.
Direct program memory addressing is also used in high-level languages, such as the GOTO instruction.
The microprocessor uses this form of addressing, but not as often as relative and indirect program memory addressing are used.

## Slide 16
The instructions for direct program memory addressing store the address with the opcode. For example, if a program jumps to memory location 10000H for the next instruction, the address (10000H) is stored following the opcode in the memory.
  Figure shows the direct intersegment JMP instruction and the 4 bytes required to store the address 10000H.
  This JMP instruction loads CS with 1000H and IP with 0000H to jump to memory location 10000H for the next instruction.
An intersegment jump is a jump to any memory location within the entire memory system.) The direct jump is often called a far jump because it can jump to any memory location for the next instruction.

## Slide 17: Relative Program Memory Addressing
Relative program memory addressing is not available in all early microprocessors, but it is available to this family of microprocessors. The term relative means “relative to the instruction pointer (IP)”.
For example, if a JMP instruction skips the next 2 bytes of memory, the address in relation to the instruction pointer is a 2 that adds to the instruction pointer. This develops the address of the next program instruction.

## Slide 18
An example of the relative JMP instruction is shown below.
Note that the JMP instruction is a 1-byte instruction, with a 1-byte or a 2-byte displacement that adds to the instruction pointer. A 1-byte displacement is used in short jumps, and a 2-byte displacement is used with near jumps and calls. Both types are considered to be intrasegment jumps.
An intrasegment jump is a jump anywhere within the current code segment.

## Slide 19: Indirect Program Memory Addressing
The microprocessor allows several forms of program indirect memory addressing for the JMP and CALL instructions.

## Slide 20: Stack Memory Addressing Modes
The stack plays an important role in all microprocessors. It holds data temporarily and stores the return addresses used by procedures. The stack memory is an LIFO (last-in, first-out) memory, which describes the way that data are stored and removed from the stack.
Data are placed onto the stack with a PUSH instruction and removed with a POP instruction.
The CALL instruction also uses the stack to hold the return address for procedures and a RET (return) instruction to remove the return address from the stack.

## Slide 21
The stack memory is maintained by two registers: the stack pointer (SP) and the stack segment register (SS). Whenever a word of data is pushed onto the stack, the high-order 8 bits are placed in the location addressed by SP – 1. The low-order 8 bits are placed in the location addressed by SP – 2. The SP is then decremented by 2 so that the next word of data is stored in the next available stack memory location.
The SP register always points to an area of memory located within the stack segment. The SP register adds to SS x 10h to form the stack memory address in the real mode.

## Slide 22
Whenever data are popped from the stack, the low-order 8 bits are removed from the location addressed by SP. The high-order 8 bits are removed from the location addressed by SP+1. The SP register is then incremented by 2.
Note that PUSH and POP store or retrieve words of data—never bytes—in the 8086 microprocessors.

## Slide 24
Data may be popped off the stack into any register or any segment register except CS. The reason that data may not be popped from the stack into CS is that this only changes part of the address of the next instruction.

## Slide 25
Example Swap operation using stack
mov ax, 1000h
mov bx, 2000h
push ax; 1000h to stack
push bx; 2000h to stack
pop ax; 2000h to ax
pop bx; 1000h to bx