## Slide 1: Chapter 4 Data Movement Instructions
Asst. Prof. Dr. Gazi Erkan BOSTANCI
Slides are mainly based on The Intel Microprocessors by Barry B. Brey, 2008

## Slide 2
mov, push, pop sample

## Slide 3
LEA: Loads a 16 or 32 bit register with the offset address of the data specified by the operand.
  LEA BX, [DI]; loads the offset address specified by [DI], contents of DI into BX register.
  MOV BX, [DI]; loads the data stored at the memory location addressed by [DI] into register BX
  MOV BX, OFFSET DATA1; the same as LEA BX, DATA1

## Slide 4
LDS: Loads any 16 or 32 bit register with an offset address and the DS segment register with a segment address.
  LDS BX, [DI]; Transfers the 32 bit number addressed by DI in the data segment into BX and DS registers

## Slide 5
LODS: Loads AL or AX with data stored at the data segment offset address indexed by the SI register
  LODSB -> AL = DS:[SI]
        SI = SI ± 1
  LODSW -> AX = DS:[SI]
        SI = SI ± 2
Note that the increment or decrement operation on the SI is decided by the value of the D (direction) flag.
  STD for setting (D=1 -> decrement)
  CLD for clearing (D=0 -> increment)

## Slide 6
STOS: Stores AL or AX at the extra segment memory location addressed by the DI register.
  STOSB ->ES:[DI] = AL
        DI = DI ± 1
  STOSW -> ES:[DI] = AX
        DI = DI ± 2
Same applies to DI for this instruction.

## Slide 7
MOVS: Transfers a byte, word or doubleword from the data segment location addressed by SI to the extra segment location addressed by DI.
  MOVSB -> ES:[DI] = DS:[SI] ;(byte transfer)
  DI = DI ± 1
        SI = SI ± 1
  MOVSW -> ES:[DI] = DS:[SI] ;(word transfer)
  DI = DI ± 2
        SI = SI ± 2
  MOVSD -> ES:[DI] = DS:[SI] ;(double word transfer)
  DI = DI ± 4
        SI = SI ± 4

## Slide 8
XCHG: Exchanges the contents of a register with the contents of any other register or memory location.
  It cannot Exchange segment registers or memory-to-memory data.
  XCHG AL, CL; Exchanges the contents of AL and CL
  XCHG AL, DATA2; Exchanges the contents of AL with the data segment memory location DATA2

## Slide 9
XLAT: Converts the contents of the AL register into a number stored in a memory table.
  This is used to convert a BCD number into 7-segment code.
 |  |  |  | -gfe | dcba |  | 
0 | -> | 3FH | -> | 0011 | 1111 | -> | 
1 | -> | 06H | -> | 0000 | 0110 | -> | 
2 | -> | 5BH | -> | 0101 | 1011 | -> | 

## Slide 10
IN and OUT: Perform I/O operations.
  In instruction transfers data from an external I/O device into AL or AX.
  Out instruction transfers data from AL or AX to an external I/O device.
  IN AL, p8; 8bits are input to AL from I/O port p8.
  IN AX, p8; 16 bits are input to AX from I/O port p8.
  OUT p8, AL, 8 bits are output to I/O port p8.
  OUT DX, AX; 16 bits are output to I/O port DX from AX.
Fixed port addressing
Variable port addressing: The port number is stored in DX, and can be changed during the program execution.