## Slide 1: Chapter 5 Arithmetic and Logic Instructions
Asst. Prof. Dr. Gazi Erkan BOSTANCI
Slides are mainly based on The Intel Microprocessors by Barry B. Brey, 2008

## Slide 2
ADD: Addition instruction for 8, 16 and 32 bit binary addition.
  ADD AL, BL ; AL = AL + BL
  ADD CL, 44H; CL = CL + 44H
  ADD [BX], AL ; AL adds to the byte contents of the data segment memory location addressed by BX with the sum stored in the same location
Register Addition
  ADD AX, BX
  ADD AX, CX
  ADD AX, DX
Whenever artihmetic and logic instructions execute, the contents of the flag register change (only the rightmost 8 bits and the overflow change, interrupt, trap and other flags donot change with these instructions.)
16 bit addition

## Slide 3
Immediate Addition
  MOV DL, 12H
  ADD DL, 33H
After the addition, the sum (45h) moves into register DL and flags change as
  Z=0 (result is not zero)
  C=0 (no carry)
  A=0 (no half-carry) Half carry is only for the least significant 4 bits.
  S=0 (result positive)
  P=0 (odd parity)
  O=0 (no overflow)

## Slide 4
Memory to register addition
  MOV DI, OFFSET NUMB; address NUMB
  MOV AL, 0; clear sum
  ADD AL, [DI]; add NUMB
  ADD AL, [DI+1]; add NUMB+1
Addition of two consecutive bytes stored at data segment offset locations NUMB, NUMB+1.
Add Sample

## Slide 5
Increment Addition (INC): Adds 1 to a register or memory location.
  INC BL; BL = BL+1
  INC BYTE PTR[BX]; Adds 1 to the byte contents of the data segment memory location addressed by BX
  INC DATA1; Adds 1 to the contents of data segment memory location DATA1
INC does not affect the carry flag bit
Further to the example in the previous slide
  MOV DI, OFFSET NUMB; address NUMB
  MOV AL, 0; clear sum
  ADD AL, [DI]; add NUMB
  INC DI; increment DI
  ADD AL, [DI]; add NUMB+1
INC Sample

## Slide 6
ADC: Addition-with-carry adds the bit in the carry flag (C) to the operand data.
  This operation is used to add numbers wider than 16 bits in 8086.
  ADC AL, AH; AL = AL + AH+ carry
  ADC CX, BX; CX = CX + BX + carry
ADC is used to perform 32 bit addition from two 16 bit additions using the carry flag.
  ADD AX, CX
  ADC BX, DX
ADC Sample

## Slide 7
SUB: Subtraction instruction for 8, 16 or 32 bit data.
  SUB CL, BL; CL = CL – BL
  SUB [DI], CH; Subtracts CH from tge byte contents of the data segment addressed by DI and stores the difference in the same memory location.
  SUB DH, 6FH; DH = DH- 6FH
Register Subtraction
  SUB BX, CX
  SUB BX, DX

## Slide 8
Immediate Subtraction
  MOV CH, 22H
  SUB CH, 44H
After the subtraction (DEH) moves into CH register and the flags are as follows:
  Z=0 (result is not zero)
  C=1 (borrow)
  A=1 (half-borrow)
  S=1 (result negative)
  P=1 (even parity)
  O=0 (no overflow)

## Slide 9
Decrement Subtraction (DEC): Subtracts 1 from a register or contents of a memory location.
  DEC BH; BH = BH – 1

## Slide 10
SBB: Subtraction with borrow functions as a regular subtraction, except that the carry flag (C), which holds the borrow, also subtracts from the difference.
  SBB AH, AL; AH = AH - AL – carry
  SUB AX, DI
  SBB BX, SI

## Slide 11
Comparison (CMP): This is a subraction tha changesonly the flag bits; the destination operand is never changed. It is normally followed by a conditional jump, which tests the condition of the flag bits.
  JA (Jump above), JB (Jump below),
  JAE (Jump above or equal), JBE (Jump below or equal)
  CMP CL, BL; CL-BL
  Ex.
  CMP AL, 10H; compare AL against 10H
  JAE FUNC; if AL is 10H or above, jump to FUNC.

## Slide 12
Multiplication: This operation can be performed on bytes, words or double words and can be signed integer (IMUL) or unsigned integer (MUL).
Flag bits change after a multiplication, but we only use C and O bits.
  The rest of the bits are unpredictable.
In 8 bit multiplication , if the most significant 8 bits of the result are zero, both C and O flag bits equal to zero.
  These bits show that the result is 8 bits wide (C=0) or 16 bits wide (C=1)

## Slide 13
8 bit multiplication
  MUL CL; AL is multiplied by CL, the unsigned product is in AX
  IMUL DH; AL is multiplied by DH, the signed product is in AX
Ex.
  MOV BL, 5; load data
  MOV CL, 10
  MOV AL, CL; position data
  MUL BL; multiply
  MOV DX, AX; position product

## Slide 14
16 bit multiplication
  This is very similar to 8 bit multiplication. The difference is AX stores the multiplicand instead of AL and the 32 bit product is stored in DX-AX.
    DX stores the most significant 16 bits and AX stores the least significant 16 bits.
  MUL CX; AX is multiplied by CX, the unsigned product is in DX-AX
  IMUL DI; AX is multiplied by DI, the signed product is in DX-AX
  MUL WORD PTR[SI]; AX is multiplied by the word contents of the data segment memory location addressed by SI, the unsigned product is stored in DX-AX
MUL Sample

## Slide 15
Division: This operation can be performed using 8 bit or 16 bit numbers.
None of the flag bits change predictably for a division.
A division can result in different types of errors: divide by zero and divide overflow.
  For example, assume AX = 3000 and this is divided by 2. Since the quotient for an 8 bit division appears in AL, the result of 1500 causes a divide overflow. Because it does not fit in AL.
In most systems, a divide error interrupt display an error message.
8 bit division divides a 16 bit number by an 8 bit number.
16 bit division divides a 32 bit number by a 16 bit number.

## Slide 16
8 bit division: Uses AX for the dividend that is divided by the contents of any 8 bit register or memory location. The quotient moves into AL with AH containing the whole number remainder.
  If AX=0010H (+16) and BL = 0FDH (-3) and IDIV BL executes, then AX=01FBH. This represents the quotient of -5 (AL) and remainder or 1 (AH).
  DIV CL; AX is divided by CL, the unsigned quotient is in AL and the unsigned remainder is in AH.
  With 8 bit division, the numbers are usually 8 bits wide. This means the dividend must be converted to a 16 bit number in AX. CBW (convert byte to word) performs this conversion for signed numbers. For unsigned, we can zero extend the number by clearing AH.
    MOV AL, NUMB; get NUMB
    MOV AH, 0; zero extend
    DIV NUMB1; divide by NUMB1
    MOV ANSQ, AL; save quotient
    MOV ANSR, AH; save remainder

## Slide 17
16 bit division: Similar to 8 bit division, except that instead of dividing into AX, the 16 bit number is divided into DX-AX, a 32 bit dividend. The quotient appears in AX and the remainder in DX:
  DIV CX; DX-AX is divided by CX, the unsigned quotient is in AX and the unsigned remainder is in DX.
If AX is a 16 bit signed number, CWD (convert word to double) sign extends it into a 32 bit number. For unsigned numbers, zero extension is used.
  MOV AX, -100; load -100
  MOV CX, 9; load 9
  CWD; sign extend, AX is extended to DX-AX
  IDIV CX

## Slide 18: Basic Logic Operations
AND: Performs logical multiplication.
It can be used to clear bits of a binary number.
  This process is called masking.
An ASCII-coded number can be converted to BCD by using the AND instruction to mask off the leftmost four binary bit positions. This converts the ASCII range 30H to 39H to range 0–9. Program below converts the ASCII contents of BX into BCD. The AND instruction in this example converts two digits from ASCII to BCD simultaneously.
  MOV BX, 3135H; load ASCII
  AND BX, 0F0FH; mask BX
  AND AL, BL; AL = AL AND BL
  AND CX, DX; CX = CX AND DX
AND Sample

## Slide 19
OR: Performs logical addition.
It can be used to set bits of a binary number.
OR AL, BL; AL = AL OR BL
OR DX, [BX]; DX is ORed with the word contents of data segment memory location addressed by BX.

## Slide 20
XOR: Performs exclusive-OR operation.
It is used to invert some of the bits in a binary number.
  XORing with 1, inverts
  XORing with 0, keeps
  XOR CH, DL; CH = CH XOR DL
  OR CX, 0600H; set bits 9 and 10
  AND CX, 0FFFCH; cler bits 0 and 1
  XOR CX, 1000H; invert bit 12

## Slide 21
TEST: This instruction performs the AND operation, but it does not change the destination operand. It affect the condition of the flag register.
  It is very similar to CMP but it checks a single bit where CMP is used to check a byte, word or doubleword.
Zero flag (Z) is logic 1 if the bit under test is a zero and Z=0 if the bit is not zero.
It is followed by a JZ (jump if zero) or JNZ (jump if not zero) instruction.
  TEST AL, 1; test right bit
  JNZ RIGHT; if set
  TEST AL, 128; test left bit
  JNZ LEFT; if set

## Slide 22
NOT and NEG
  NOT is logical inversion or one’s complement
  NEG is arithmetic sign inversion or two’s complement
  NOT CH; CH is one’s complemented
  NEG AX; AX is two’s complemented

## Slide 23
Shift: Move bit to left or right within a
register or memory location.
Left shift->multiplication by powers of 2+n
Right shift->multiplication by powers of 2-n
  SHL AX, 1; AX is shifted left 1 place
  SHR BX, 12; BX is logically shifted right 12 places
Logical shift is for unsigned data.
Arithmetic shift is for signed data.

## Slide 24
Rotate: Rotates the information in a register or memory location either from one end to another or through carry flag.
  ROL SI, 14; SI rotates left 14 places
  RCL BL, 6; BL rotates left through carry 6 places.
These instructions often used to shift wide numbers to the left or right.
The program below shifts the 48-bit number in registers DX, BX, and AX left one binary place. Notice that the least significant 16 bits (AX) shifted left first. This moves the leftmost bit of AX into the carry flag bit. Next, the rotate BX instruction rotates carry into BX, and its leftmost bit moves into carry. The last instruction rotates carry into DX, and the shift is complete.
  SHL AX, 1
  RCL BX, 1
  RCL DX, 1