## Slide 1: Chapter 6 Program Control Instructions
Asst. Prof. Dr. Gazi Erkan BOSTANCI
Slides are mainly based on The Intel Microprocessors by Barry B. Brey, 2008

## Slide 2
The program control instructions direct the flow of a program and allow the flow to change.
A change in flow often occurs after a decision made with the CMP and TEST instruction followed by a conditional jump instruction.

## Slide 3: The Jump Group
The main program control instruction, jump (JMP), allows the programmer to skip sections of a program and branch to any part of memory for next instruction.
A conditional jump instruction allows the programmer to make decisions based upon numerical tests. The results of numerical tests are held in the flag bits, which are then tested by conditional jump instructions.

## Slide 4: Unconditional Jump (JMP)
Whenever a jump instruction references an address, a label normally identifies the address.
  XOR BX, BX
  START: MOV AX,1
  ADD AX, BX
  JMP NEXT
  ...
  NEXT: MOV BX, AX
  JMP START

## Slide 5: Conditional Jumps and Conditional Sets
The conditional jump instructions test the following flag bits: sign (s), zero (z), carry (c), parity (p) and overflow (o).
  If the condition under test is true, a branch to a label associated with the jump instruction occurs.
  If the condition is false, the next sequential step in the program executes.

## Slide 7: LOOP
The LOOP instruction is a combination of a decrement CX and JNZ conditional jump.
  LOOP decrements CX;
    If CX!=0, it jumps to the address indicated by the label.
    If CX becomes 0, the next sequential instruction executes.
The following example shows how data in one block of memory (BLOCK1) add to data in a second block of memory (BLOCK2), using LOOP to control how many numbers add.
  The LODSW and STOSW instructions access the data in BLOCK1 and BLOCK2.
  The ADD AX, ES:[DI] instruction accesses the data in BLOCK2 located in the extra segment. The only reason that BLOCK2 is in the extra segment is that DI addresses extra segment data for the STOSW instruction.
In this example, the extra segment also addresses data in the data segment, so the contents of DS are copied to ES through the accumulator. Unfortunately, there is no direct move from segment register to segment register instruction.

## Slide 8
.DATA ;start data segment
; DUP duplicates ? 100 times,
; ? Means uninitialized
; 4 DUP(2) = 2,2,2,2
BLOCK1 DW 100 DUP(?) ;100 words for BLOCK1
BLOCK2 DW 100 DUP(?) ;100 words for BLOCK2
.CODE ;start code segment
.STARTUP ;start program
MOV AX,DS ;overlap DS and ES
MOV ES,AX
CLD ;select auto-increment
MOV CX,100 ;load counter
MOV SI,OFFSET BLOCK1 ;address BLOCK1
MOV DI,OFFSET BLOCK2 ;address BLOCK2
L1: LODSW ;load AX with BLOCK1
ADD AX,ES:[DI] ;add BLOCK2
STOSW ;save answer
LOOP L1 ;repeat 100 times

## Slide 9: Procedures
The procedure (subroutine, function or method) is an important part of any computer system’s architecture.
A procedure is a group of instructions that usually performs one task.
It is a reusable section of software that is stored in memory once, but used often as necessary.
The CALL instruction links to the procedure, and the RET (return) instruction returns from the procedure.
The stack stores the return address whenever a procedure is called during the execution of a program.
  The CALL instruction pushes the address of the instruction following the CALL (return address) on the stack.
  The RET instruction removes an address from the stack so the program returns to the instruction following the CALL.

## Slide 10
Ex.
  SUMS PROC
  ADD AX, BX
  ADD AX, CX
  ADD AX, DX
  RET
  SUMS ENDP
  CALL SUMS
Procedure Definition
Procedure Call

## Slide 11: Introduction to Interrupts
An interrupt is either a hardware-generated CALL (externally derived from a hardware signal) or a software-generated CALL (internally derived from the execution of an instruction or aby some other internal event.)
At time, an interrupt is called an exception. Either type interrupts the program by calling an interrupt service procedure (ISP) or interrupt handler.
  Interrupts are special types of CALL instructions.

## Slide 12: Interrupt Vectors
An interrupt vector is a 4-byte number stored in the first 1024 bytes of the memory (00000H–003FFH) when the microprocessor operates in the real mode.

## Slide 13
Samples
  Loop
  Call-Ret
  Absolute Difference
  Reverse
  Sort