## Slide 1: PCR
How does PCR work?:
  Separation of two strands
  from each other (94oC)
  Annealing of Primers (55oC)
    Beginning of Replication
  Extension
  (polymerisastion) (72oC)
    = replication
  Repeat for 20-30 times (cycles)
94°
55°
72°
94°

## Slide 2
CYCLE PARAMETRES
Denaturation; 93°C - 95°C
30 sec – 1 min
Annealing; 37°C - 65°C
30 sec – 1 min
Extension; 72°C
1 min (For every 500 bp DNA add + 30 sec)
25-35 cycles
Final exstantion 2-10 min

## Slide 3
Basic PCR conditions
25-50-100 µl final reaction volumes
Template DNA 1-1000ng
Primers 10-20 pmols
10 mM Tris-CL pH 9.0, 50 mM KCl (10xPCR buffer)
MgCl2 0.5-3.0 mM
final concentration of each dnTPs would be 200 µM dNTP’ler: dATP, dGTP, dTTP, dCTP
1 unit Taq polymerase enzyme

## Slide 4
COntents
Volumes
Final Concentration
10 X PCR Buffer
5l
1X
10 X dNTPs (2mM)
5l
200M
Forward primer (10pmols/l)
5l
1M (50pmols/50l)
Reverse primer (10pmols/l)
5l
1M (50pmols/50l)
Genomic DNA template
2l
1g
Taq polymerase (2U/l)
0.5l
1 unit
H2O (to 50l Final volume)
27.5l
REACTION MIXTURE
25 or 50l final volume Eppendorf (0.2 ml) tube

## Slide 5
3. Cycle is the first cycle when the first products
of targeted length
Amplimers synthesized according to equation mentioned below:
After n number of PCR cycles where exponential amplification
No(1+Y)n-1 target copy will be formed!
No starting number of DNA targets
Y Efficiency of PCR reaction
n cycle number
From this cycle on amplication proceeds exponentially

## Slide 6: Lets presume that only 1 DNA target exists
4. cycle 1(1+1)3=8
5. cycle 1(1+1)4=16
6. cycle 1(1+1)5=32
After a definite number of cycles PCR efficiency decreases.
No(1+Y)n-1

## Slide 7
ALWAYS SHOULD BE
REMEMBERED!
PCR is a very sensitive technique– DNA contamination with an unwanted DNA could be significant!
Always add negative controls to the reaction!
Always add positive controls to the reaction!
Use appropriate filtered pipets and pippet tipds
Perform PCR in separate units
Use laminar flows with UV lambs

## Slide 8
Cloning of gene or gene fragments
Genetic diagnosis – Detection mutations
Maternity-Paternity Tests
DNA sequence analysis
Forensic identification
Determination of quality control of industrial products
Determination of appropriate tissue type for tissue transplantation
Determination of polymorphism in between species
Molecular typing
Detection of pathogens
PCR is used for;

## Slide 9: Advantages and Disadvantages of PCR!
High sensitivity and specificity!
Fast detection and identification!
Could detect inanimate (dead) agents!
Could detect acid-fast and environment fragile agents!
Could detect slow growing bacteria
Provide the probability of later sophisticated studies (typing, sequence analysis, clonning) olanak sağlaması
Still cannot replace isolation in definitive diagnosis!
False-positiveness due to cross-contamination!
Requires lab infrastructure!
Requires well trained personnel!
High expendature costs!