## Slide 1: DNA AGAROSE GEL ELECTROPHORESIS

## Slide 2: Definition
“Electro” means electric energy
“Phoresis” is generated from the Greek word “phoros” which means to carry through.
In the electrophoresis, with the help of a constant electric current, molecules are carried through a special matrix called agarose in a defined direction due to their electrical charge.

## Slide 3: What is gel electrophoresis?
It is a technique, used for the separation of charged molecules in the laboratory.
DNA is a negatively charged molecule!
DNA is moved through an agarose and/or polyacyrilamide matrix with the help of a electric current “running”

## Slide 4
Gel electrophoresis separates macromolecules (proteins or nucleic acids) from each other, depending on their molecular sizes, electrical charges or other physical characteristics!

## Slide 5: Electrophoresis;
Separation
İdentification
Purification
Restriction analysis
Genotyping (PFGE)

## Slide 6: The Electrophoresis Technique;
Simple and easy,
Rapid
Separation of DNA those couldnot be separated by techniues such as Density gradient centrifugation
EtBr 1-10 ng, SYBR Gold 20 pg detection sensitivity

## Slide 7: DNA run distances in agarose gels
DNA’s molecular size
Agarose concentration
DNA’s structure
Presence of EtBr in gel and electrophoresis buffer
Applied voltage
Agarose type
Electrophoresis buffer

## Slide 8: Separation (Separation of Molecules)
Gel is solidified, DNA is loaded into the lanes on the gel “loading”
Electric current is applied to the jel
Separation is performed regarding 2 factors:
Molecule type and size
Molecule charge

## Slide 9: Agarose
Agarose is a carbonhydrate molecule chain extracted from sea lichen
Expensive chemical 500 mg 200 $

## Slide 10: Polyacyrilamide
  Material used in skin electrodes and contact lenses
  In both gels pores are formed where the molecules pass through
  Polyacyrilamide is a more synthetic molecule
  With polyacyrilamide number and diameter of pores could be controlled better

## Slide 11: Differences
Agarose is a natural and pure matrix, on the other hand expensive
Agarose have more universal pore diameters
Polyacyrilamide is synthetic, however pore diameter and number could be defined