## Slide 1: EME 201 Materials Science
Failure

## Slide 2: ENE 201 – Material Science - Failure
The failure of materials is an unwanted event, when human lives and economic losses are considered.
Since engineering materials do not reach theoretical strength when they are tested in the laboratory, it is difficult to guarantee that failures will be avoided during the service.
The usual reasons of failure are poor materials selection, design defects and maintenance problems or misuse.
Under the imposed stress, materials can be split into two or three pieces. This called Simple Fructure.
Ductile Fructure; substantial plastic deformation and tearing of materials
Brittle Fructure; there is no or little plastic deformation and crack propagation

## Slide 3: ENE 201 – Material Science - Failure
Calculation of Ductility (permenant strain that is realized before material fructures)
Percent Elongation ; Percent Reduction in Area
Brittle fracture can be in the form of either cleavage (transgranular) or intergranular fracture.
Ductility Transition Temperature; ductile materials may fracture as brittle materials at a lower temperature. This temperature can be predicted by experimental tests for different materials.
Material fracture can be affected by stress concentration, temperature, thermal shock.
Stress Concentration
The presence of a notch, flaws or cracks either in the material or at the surface, can change the stress where fracture occurs. This is explained by the stress concentration
The fracture starts at some point of these stress concentrations and it decreases the fracture strength.

## Slide 4: ENE 201 – Material Science – Failure
Stress Concentration
Maximum stress can be calculated by where σ0 is applied stress; a is the length of the crack; ρt is the radius of curvature.
The ratio σm /σ0 is called as the stress concentration factor, Kt.
In a brittle material, critical stress σc required for the crack propagation can be calculated by where E is Young’s modulus; γs is specific surface energy.
Fracture toughness can be defined as being a measure of the material’s resistance to brittle fracture when a crack is present and calculated by where Y is the dimensionless parameter

## Slide 5: ENE 201 – Material Science – Failure
At a large thickness, plane strain fracture toughness KIc can be defined
The plane strain fracture toughness depends on temperature, strain rate microstructure.Reduction in grain size increases the KIc.
Impact Fracture Testing
Impact test conditions; a relatively low temperature, high strain rate, triaxial stress state
Impact Testing Techniques; Charpy and Izod are designed for measuring the impact energy, sometimes also called notch toughness.
Impact Energy: the energy required to fracture a test piece under an impact load.

## Slide 6: ENE 201 – Material Science – Failure
Fatigue
Fatigue is caused by repeated dynamic and cyclic stresses.
It is a progressive damage to cause failure.
After a long period of repeated stress or strain cycling, failure occurs
The process of fatigue consists of three stages: Initial crack formation, progressive crack growth, sudden fracture.
Fatigue Cyclic Stresses
reversed stress cycle
repeated stress cycle

## Slide 7: ENE 201 – Material Science – Failure
Cyclic stresses contains maximum (σmax), minimum (σmin) and mean stress (σm), the range of stress (σr), the stress amplitude (σa), and the stress ratio (R).
S-N curves can be used for fatigue calculations.
At Higher N values, the S–N curve becomes horizontal or there is a limiting stress level, called the fatigue limit (also sometimes the endurance limit) for some materials.
Fatigue life is the number of cycles to cause failure at a specified stress level.
Factors That Affect the Fatigue Life
Mean Stress, surface effects, environmental effects (thermal fatigue, corrosion fatigue).

## Slide 8: ENE 201 – Material Science – Failure
Creep
Materials are often placed in service at elevated temperatures (normally above 40 % of absolute melting temperature of the material) and exposed to certain stresses.
This deformation is called creep which is time-dependent and permanent deformation of materials.
Creep limits the lifetime of a part.
t can be seen in all materials; especially amorphous polymers are sensitive to creep deformation.
Boilers, gas turbine engines, and ovens are some of the examples of creep.
There are three stages of the creep deformation, namely; Primary or transient creep, secondary creep or steady-state creep, tertiary creep.

## Slide 9: ENE 201 – Material Science – Failure
Parameters of Creep
The slope of the second part of the creep curve is called the minimum or steady-state creep rate;
Another parameter is time to rupture, or the rupture lifetime.
Creep can be affected by the temperature and applied stress and calculated by

## Slide 10: ENE 201 – Material Science – Failure
References
1) W. D. Callister, Jr., Materials Science and Engineering – an Introduction, 7th Ed., John Wiley & Sons, 2007
2) A. Maleque, M. S. Salit, Material Selection and Desing, Springer, 2013
3) R. M. Christensen, The Theory of Materials Failure, Oxford University Press, 2013
4) L. H. Van Vlack, Elements of Materials Science and Engineering, 6th Ed., Addison-Wesley Publishing, 1989