## Slide 1: Atomic Structure and Interatomic Bonding
Interatomic bonds exist in all solids.
Molecular structure of materials is composed of different bonding pattern.
OBJECTIVE
To be able to interrelate the structure of atoms-bonds and properties of engineering materials.

## Slide 2: Atomic Structure and Interatomic Bonding
Atomic structure– electrons and nuclei
  The structure of atoms affects the type of bonds
  The diameter of atoms is in the angstrom range (10-10 m)
Short and long range atomic arrangements– order of atoms
  Short range: Atoms have order only over short distance (1-10A)
  Crystalline materials: Atoms have 3-D pattern with repetition on a larger distance (10 nm-1cm)
Nanostructure- the structure of materials at a length scale of 1 to 100 nm

## Slide 3: Atomic Structure and Interatomic Bonding
Microstructure–
  Structure of materials at a length scale of 0.1 μm to 100 μm
  Grain size and DEFECTS
Macrostructure--
  Structure of materials at a length scale of > 100 μm
  Porosity, microcracks, surface coatings
  Atomic structure influences how atoms are bonded together.

## Slide 4: The Periodic Table
The first periodic table of elements was published in 1869 by Dmitri Mendeleev.
All elements in the periodic table were classified based on the electron configuration.
Elements in a given column have similar valence electron structures and chemical/physical properties
There are missing elements
http://www.rsc.org/education/teachers/resources/periodictable/pre16/develop/mendeleev.htm

## Slide 5
Atomic Bonding
Metallic bonds
  The metallic bond forms when atoms give up their valence electrons to form an electron sea.
  Are found in metals and their alloys
Covalent bonds
  sharing of electrons between adjacent atoms
  H2, Cl2, CH4, H2O, diamond, SiC………
Ionic bonds
  % ionic character = (1-exp(-0.25 (xA-xB)2))x100
XA, XB are the electronegativities of atoms A and B
NaCl, MgO
van der Waals bonds (London forces, Debye interaction, Keesom interaction)
  physical bonds (secondary bonds)
  Weak in comparison to primary or chemical bonds
Ionic Bond = Metal + Non-metal
Dissimilar Electronegativities

## Slide 6
Atomic Bonding
Bonding Energies and Melting Temperatures
Bonding Type | Substance | Bonding Energy (kJ/mol) | Melting Temperature (oC)
Ionic | NaCl | 640 | 801
 | MgO | 1000 | 1200
Covalent | Si | 450 | 1410
 | C (diamond) | 713 | >3550
Metallic | Hg | 68 | -39
 | W | 849 | 3410
van der Waals | Ar | 7.7 | -189
 | Cl2 | 31 | -101
Hydrogen | NH3 | 35 | -78
 | H2O | 51 | 0
William D. Callister, David G. Rethwisch, Materials Science and Engineering, Eighth Edition, Wiley, 2011.

## Slide 7: References
Donald R. Askeland, Pradeep P. Fulay, Wendelin J. Wright, The Science and Engineering of Materials, Sixth Edition
William D. Callister, David G. Rethwisch, Materials Science and Engineering, Eighth Edition, Wiley, 2011.