## Slide 1: Atomic and Ionic Arrangements
OBJECTIVES
classification of materials based on atomic arrangements
  Crystalline
  Amorphous
arrangements in crystalline solids based on lattice, basis, unit cell and crystal structures

## Slide 2: Order
Short-range order (SRO) - The regular arrangement of the atoms over a short distance (No periodicity in the structure)
  AMORPHOUS MATERIALS
    H2O, silicate glass, polyethylene……….
Long-range order (LRO) - A regular repetitive arrangement of atoms which extends over a very large distance.
  CRYSTALLINE MATERIALS (Metals, Alloys, Most Ceramics)
    Single Crystal (Si, GaAs)
    Polycrystalline
Mixed SRO and LRO -

## Slide 3: Lattice, Basis, Unit Cell and Crystal Structures
A lattice is a collection of lattice points, which are arranged in a periodic pattern.
  3D array of points coinciding with atom positions
Basis + Lattice = Crystal structure
🔴⚫️ + . . . . = 🔴⚫️🔴⚫️🔴⚫️🔴⚫️ . . . . 🔴⚫️🔴⚫️🔴⚫️🔴⚫️ . . . . 🔴⚫️🔴⚫️🔴⚫️🔴⚫️
Basis can be atoms or group of atoms and molecules.
Unit cell is the simplest repeating unit in the crystal
  Opposite faces in the unit cell are parallel
  The edge of the unit cell connects equivalent points

## Slide 4
Crystal Systems
Crystal systems represent the 3D building blocks .
Crystal systems are characterized by a unit cell (UC)
The lattice parameters are the axial lengths and dimensions of UC and represented by lattice constants of a, b, and c .
14 unique case to arrange points in 3D (Bravais Lattices)
14 Bravais lattices are grouped into seven crystal systems of Cubic, Hexagonal, Tetragonal, Rhombohedral, Orthorhombic, Monoclinic, Triclinic.
3 lattice constants, a, b, and c
3 lattice angles, alpha/beta/ gamma

## Slide 5
Crystal Systems, Bravais Lattices
Cubic
Simple cubic
Face centered cubic
Body centered cubic
Tetragonal
Simple tetragonal
Body centerd tetragonal
Hexagonal
Orthorhombic
Simple orthorhombic
Body centered orthorhombic
Base centered orthorhombic
Face centered orthorhombic
Rhombohedral (Trigonal)
Monoclinic
Simple monoclinic
Base centered monoclinic
Triclinic

## Slide 6
http://www.seas.upenn.edu/~chem101/sschem/solidstatechem.html#bravais
Bravais Lattices

## Slide 7
Crystal Systems
Crystal System | Axial Relationships | Interaxial Angles
Cubic | a = b = c | = = = 900
Hexagonal | a = b c | = = 900 = 1200
Tetragonal | a = b c | = = = 900
Rhombohedral | a = b = c | = = 900
Orthorhombic | a b c | = = = 900
Monoclinic | a b c | = = 900
Triclinic | a b c | 900
Crystal System | Axial Relationships | Interaxial Angles
Cubic | a = b = c | 
Hexagonal |  | 
Tetragonal |  | 
Rhombohedral | a = b = c | 
Orthorhombic |  | 
Monoclinic |  | 
Triclinic |  | 
Lattice Parameter Relationships
William D. Callister, David G. Rethwisch, Materials Science and Engineering, Eighth Edition, Wiley, 2011.

## Slide 8: References
Donald R. Askeland, Pradeep P. Fulay, Wendelin J. Wright, The Science and Engineering of Materials, Sixth Edition
William D. Callister, David G. Rethwisch, Materials Science and Engineering, Eighth Edition, Wiley, 2011.