## Slide 1: Imperfections in Solids
Types of imperfections:
  point defects
  line defects (or dislocations)
  surface defects

## Slide 2: Why are Defects Important?
Atomic Bonding
Defects
Material Properties
Crysal Structure
Defects can be created intentionally to alter the properties
(electrical, mechanical, or optical) of the materials.

## Slide 3: Types of Imperfections
POINT DEFECTS
  Vacancy Atoms
  Interstitial Atoms
  Impurities (Substitutional/ Interstitisal)
LINE DEFECTS
  Dislocations
    Edge
    Screw
    Mixed
AREA DEFECTS
  Grain Boundaries
    Tilt
    Twist
The arrangement of the atoms or ions in materials contains imperfections or defects
Crystalline defect is a lattice irregularity

## Slide 4
Point Defects
Vacancy
Self-interstitial
The simplest point defects is vacancy (missing atom)
All crystalline solid contains vacancies
Self-interstitial-Crystal atom occupies an interstitial site in the crystal.
k = Boltzmann Constant
Nv = Equilibrium number of vacancies
N = Total number of atomic sites
Qv = Activation energy
T = Temperature

## Slide 5
Point Defects
Substitutional
impurity atom
Atomic size factor
Crystal structure
Electronegativity
Valences
Interstitial
Impurity atom
The substitutional atoms replace or
substitute for the host atoms.
Copper-Nickel
The interstitial atoms fill the voids
among the host atoms.
Carbon-Iron

## Slide 6
Linear Defects-Dislocations
Dislocations are one-dimensional (linear) defects and can be observed in all crystalline materials.
Misalignment of atoms around a dislocation line
Screw dislocation is produced by skewing a crystal and one atomic plane produces a spiral ramp about the dislocation.
Edge dislocation is defined as the edge of the extra half plane of atoms.
  The upper part is compressed while the region below dislocation experiences tensile stress
  (Positive edge dislocation)
  (Negative edge dislocation)
  Mixed dislocation that contains edge and screw dislocations.

## Slide 7
Linear Defects-Dislocations
Size and the direction of the lattice distortion caused by a dislocation can be defined by Burgers vector b.
b is defined to be closure failure of one atom distance
b is required to complete loop and return to its starting point
b defines magnitude and direction of slip
Dislocation line defect that the boundary between slipped and unslipped region of the crystal.
b is parallel to the screw dislocation and perpendicular to the edge dislocation.

## Slide 8: References
Donald R. Askeland, Pradeep P. Fulay, Wendelin J. Wright, The Science and Engineering of Materials, Sixth Edition
William D. Callister, David G. Rethwisch, Materials Science and Engineering, Eighth Edition, Wiley, 2011.