## Slide 1
Strength of Materials
• Stress and strain
• Elastic behavior/Plastic behavior
• Toughness and ductility
Hardness
Design/Safety Factor

## Slide 2
Engineering Stress and Strain
Stress: Force or load per unit area
  Tension
  Compression
  Shear
F
F
F
F
F
F
Tensile
Compressive
Shear
Shear Stress

## Slide 3
Engineering Stress and Strain
Strain: Elongation change in dimension per unit length.
            (Dimensionless)
Stress and strain are; positive for tension
        negative for compression.
Elastic material
Non-linear material

## Slide 4
Engineering Stress and Strain
Young’s modulus: The slope of the linear part of the stress-strain curve in the elastic region (modulus of elasticity).
Shear modulus (G): The slope of the linear part of the shear stress-shear strain curve.

## Slide 5
Elastic Deformation
Linear Elastic
Non-linear Elastic
Reversible Deformation
Non-permanent deformation where the material completely recovers its original state upon release of applied stress
Notes: The carbon (black) attempting to diffuse into a steel is observed in abundance on the surface; in considerable amounts along grain boundaries; and in little to no concentration within the grains.

## Slide 6
Linear Elastic Deformation Properties
E : Modulus of Elasticity (Young’s Modulus)
E is a measure of material’s resistance to elastic deformation
Stiffness is proportional to it’s Young’s modulus
G : Shear Modulus
Shear stress and shear rate are proportional
Hooke’s Law
E
= E
F
F
Notes: The carbon (black) attempting to diffuse into a steel is observed in abundance on the surface; in considerable amounts along grain boundaries; and in little to no concentration within the grains.

## Slide 7
Linear Elastic Deformation Properties
v relates the lateral and axial strains
Poison’s Ratio
 | v
Max | 0.5
Isotropic materials | 0.25
Metals and alloys | 0.25-0.35
Notes: The carbon (black) attempting to diffuse into a steel is observed in abundance on the surface; in considerable amounts along grain boundaries; and in little to no concentration within the grains.

## Slide 8: References
Donald R. Askeland, Pradeep P. Fulay, Wendelin J. Wright, The Science and Engineering of Materials, Sixth Edition
William D. Callister, David G. Rethwisch, Materials Science and Engineering, Eighth Edition, Wiley, 2011.