## Slide 1: Phase Diagrams

## Slide 2: Phase Equilibria
  Phase: Homogeneous portion of a system that has uniform physical and chemical characteristics.
    A phase boundary is discontinuity in the structure
    Single-phase system is HOMOGENEOUS system
    Two or more phases are MIXTURE or HETEROGENEUS system
  The development of microstructure is related to the characteristics of its phase diagram. Microstructural characteristics that are important for multiphase systems are;
    The number of phases present
    The relative proportions of the phases
    Phases spatial arrangement

## Slide 3: Phase Equilibria
  Equilibrium: A system is at equilibrium if its free energy is at a min. under some combination of T, P and composition.
  Free energy is a function of internal energy and entropy.
  Phase Equilibrium: Equilibrium as it applies to systems in which more than one phase may exists
    Thermodynamically the condition for phase equilibrium is that the free energy of a system is a minimum
    A constancy with time in the phase characteristics
    Metastable system are non-equilibrium ones
    Often, metastable structures are of more significance than equilibrium ones.

## Slide 4: Solubility and Solid Solutions
  A solution is a phase with more than one component
    Sugar melt in water
  Solid solutions in metallic and ceramic materials exist when elements or compounds with similar crystal structures form a single phase that is chemically homogeneous.
    Barium titanate-strontium titanate
    Gallium arsenide-aluminum arsenide
  The composition of solutions can vary because,
    One atom may be substituted for another in the phase structure
    Atoms may be placed in the interstices of the structure

## Slide 5: Solubility and Solid Solutions
  Hume-Rothery rules for unlimited solute solubility;
    Size Factor; The atoms/ions must be of similar size
    Crystal structure: same crystal structure
    Valance; the ions have same valance
    Electronegativity; the atoms must have same electronegativity
  Solid solution strengthening is accomplished by the formation of solid solutions.
    The point defect created restrict dislocation motion and cause strengthening. Restricting dislocation motion leads to material harder or stronger.
    Solid solution strengthening increases the strength and hardness whereas decreases ductility and electrical conductivity of metallic materials.

## Slide 6: Phase Diagrams
A phase diagram shows phases that are in the system under thermodynamic equilibrium conditions.
A phase diagram in which constituents exhibit complete solid solubility is known as isomorphous phase diagram (the copper-nickel system).
One-Component (Unary) Phase Diagram
  Pressure versus Temperature
  Solid, liquid and vapor phases
  On P-T diagram where 3-phases are in equilibrium is called a triple point
Binary Phase Diagram
  Pressure is constant (normally at 101.3 kPa)
  Temperature and compositions are changing
  Many microstructures develop upon phase transformation which occurs when the temperature is altered.

## Slide 7: Interpretation of Phase Diagram
Nomenclature
  For metallic alloys, Greek letters () are used for solid solutions
  Liquidus line; line between L and +L
  Solidus line; line between and +L (below which only exists)
Phases Present
Determination of Phase Compositions
  Tie Line connects the phases in equilibrium with each other and is drawn across the two-phase region at specified T
  The intersections of the tie line and the phase boundaries are recorded for both sites
  Composition of each phases from the horizontal composition axis can be read.

## Slide 8: References
Donald R. Askeland, Pradeep P. Fulay, Wendelin J. Wright, The Science and Engineering of Materials, Sixth Edition
William D. Callister, David G. Rethwisch, Materials Science and Engineering, Eighth Edition, Wiley, 2011.