## Slide 1: H3PO4 (PHOSPHORIC ACID) DETERMINATION
Polyprotic Acid

## Slide 2: Phosphoric acid
Polyprotic acids contain more than one mole ionizable hydronium ions per mole of acids. They ionize to give more than one H+ ions per molecule.
Phosphoric acid is a polyprotic acids. Phosphoric acid containing 3 protons has three acidities different from each other.
Polyprotic acids are ionized to three steps. Each step give one proton and for each step the effect value is 1. Thus, total effect values are three.
It is difficult to tirate 3rd proton of phosphoric acid as it is very weak.

## Slide 3: Reaction Equation:
H3PO4 + NaOH → NaH2PO4 + H2O Ka1 = 7.11x10-3
(End point of bromocresol green )
NaH2PO4 + NaOH → Na2HPO4 + H2O Ka2 = 6.34x10-8
(End point of phenolphthalein)
H3PO4 + 2NaOH → Na2HPO4 + 2H2O Total acidity

## Slide 4
Preparation of Experiments:
Dilute the given sample(20 mL) to 100 mL with distilled water. Transfer 25 mL of sample to an erlenmeyer flask.
Add 2 drops of bromocresol green and phenolphthalein.
Titrate with 0.1 N NaOH until blue-green color and note the volume of titrant used (V1)
Continue titration until violet color and note the volume of titrant used for second part. (V2)

## Slide 5: Calculation:
The concentration of phosphoric acid in the sample is calculated in g / L (Mw: 98)
Determination of 1st proton (1st acidity):
First, the moles of NaOH consumed during titration can be calculated from the following equation using the volume of NaOH that is consumed in the titration and the molarity of the NaOH.
nNaOH = MNaOH × V1

## Slide 6
According to reaction equation:
If 1 mol NaOH reacts with 1 mol H3PO4
nNaOH mol NaOH reacts with x mol H3PO4
From this ratio, the moles of H3PO4 in the diluted sample (𝑥 = nH3PO4 ) is calculated and the molarity of the diluted sample is calculated from x.
MH3PO4 = 𝑥 / VH3PO4
The molarity of the original sample (M𝑠𝑎𝑚𝑝𝑙𝑒) can then be calculated by multiplying the molarity of the diluted sample by the dilution factor.
M𝑠𝑎𝑚𝑝𝑙𝑒 = MH3PO4 × DF
Finally, the molarity is multiplied by the molecular weight to convert the concentration of the original sample to g/L:
C(g⁄L) = M𝑠𝑎𝑚𝑝𝑙𝑒 × 98

## Slide 7
Determination of 2nd proton (2nd acidity):
First, the moles of NaOH consumed during titration can be calculated from the following equation using the volume of NaOH that is consumed in the titration and the molarity of the NaOH.
According to reaction equation:
    nNaOH = MNaOH × V2
If 1 mol NaOH reacts with 1 mol H3PO4
nNaOH mol NaOH reacts with x mol H3PO4
From this ratio, the moles of H3PO4 in the diluted sample (𝑥 = nH3PO4 ) is calculated and the molarity of the diluted sample is calculated from x.
MH3PO4 = 𝑥 / VH3PO4
The molarity of the original sample (M𝑠𝑎𝑚𝑝𝑙𝑒) can then be calculated by multiplying the molarity of the diluted sample by the dilution factor.
    M𝑠𝑎𝑚𝑝𝑙𝑒 = MH3PO4 × DF
Finally, the molarity is multiplied by the molecular weight to convert the concentration of the original sample to g/L:
C(g⁄L) = M𝑠𝑎𝑚𝑝𝑙𝑒 × 98
Reference:
Analitik Kimya Pratikleri-Kantitatif Analiz(Ed. Feyyaz ONUR), A.Ü. Eczacılık Fakültesi Yayınları No. 111, 2014

## Slide 8
Determination of total acidity:
Transfer 25 mL of sample to an erlenmeyer flask.
Add 2 drops of phenphthalein.
Titrate with 0.1 N NaOH until pink color and note the volume of titrant.
nNaOH = MNaOH × VNaOH
According to reaction equation:
If 2 mol NaOH reacts with 1 mol H3PO4
nNaOH mol NaOH reacts with x mol H3PO4
From this ratio, the moles of H3PO4 in the diluted sample (𝑥 = nH3PO4 ) is calculated and the molarity of the diluted sample is calculated from x.
MH3PO4 = 𝑥 / VH3PO4

## Slide 9
The molarity of the original sample (M𝑠𝑎𝑚𝑝𝑙𝑒) can then be calculated by multiplying the molarity of the diluted sample by the dilution factor.
M𝑠𝑎𝑚𝑝𝑙𝑒 = MH3PO4 × DF
Finally, the molarity is multiplied by the molecular weight to convert the concentration of the original sample to g/L: C(g⁄L) = M𝑠𝑎𝑚𝑝𝑙𝑒 × 98