## Slide 1: FIndIng Hazard InformatIon: MaterIal Safety Data Sheets (MSDS) The Globally HarmonIzed System Of ClassIfIcatIon And LabellIng Of ChemIcals (GHS)
PHA297 – LABORATORY SAFETY

## Slide 2: MATERIAL SAFETY DATA SHEET (msds)
This section identifies some good resources with information about hazards of chemicals. It includes a description of these resources and how they might be used.

## Slide 3: MATERIAL SAFETY DATA SHEET (msds)
An Incident: Chemical Sensitivity
Three female students were using 1-fluoro-2,4-dinitrobenzene (FDNB). While working with this reagent over a 2-month to 2-year period, the tips of their fingers and nails exhibited a yellow staining characteristic of FDNB, and blisters developed on their fingers. Testing revealed that the students and their 39-year instructor had developed sensitivity to FDNB—investigation showed that it had been previously reported to be a potent allergen and a strong irritant. The students suggested that their protective gloves were permeable to FDNB, which led to the sensitization. Testing of their gloves revealed that FDNB passed through their protective gloves.
Robert H. Hill, Jr., David C. Finster, Laboratory Safety
for Chemistry Students, 2010, Wiley

## Slide 4: MATERIAL SAFETY DATA SHEET (msds)
>66 million chemicals indexed (December 2016)
Safety information is available for only little amount of chemicals (<1%)
Not all chemicals are tested for toxic properties, and we have relatively little to no information about the hazards of the vast majority of these compounds. In some instances, the information that exists must be sought after by looking for specific information for a specific compound, and even then, it may be hard to find.
Number of CAS (Chemical Abstracts Service) Registered Chemicals. For the current number of CAS chemicals access
Robert H. Hill, Jr., David C. Finster, Laboratory Safety
for Chemistry Students, 2010, Wiley

## Slide 5: MATERIAL SAFETY DATA SHEET (msds)
WHY NOT TEST THE HEALTH EFFECTS OF ALL CHEMICALS?
Money, money, money! It requires lots of money to pay for proper testing! To determine something about the health effects of a chemical requires that it be tested, usually in animals, and rats are the most popular model used for this. A typical toxicity study might cost $50,000 to $100,000 or even more. Unless there is real commercial value in a chemical, it is not likely to be tested for toxicity. Furthermore, this kind of testing is only for immediate effects. Longer term health effects from repeated smaller doses of a chemical are often only recognized by careful observation of people exposed to a chemical for a long period of time. While there are animal toxicity tests for long-term health effects, they are not always predictive of health effects in humans—and they are enormously expensive.
Robert H. Hill, Jr., David C. Finster, Laboratory Safety
for Chemistry Students, 2010, Wiley

## Slide 6: MATERIAL SAFETY DATA SHEET (msds)
1. Identification
2. Hazard(s) Identification
3. Composition/Information on Ingredients
4. First Aid Measures
5. Firefighting Measures
6. Accidental Release Measures
7. Handling and Storage
8. Exposure Controls/Personal Protection
9. Physical and Chemical Properties
10. Stability and Reactivity
11. Toxicological Information
12. Ecological Information
13. Disposal Considerations
14. Transport Information
15. Regulatory Information
16. Other Information
MSDS provides information about hazard of the chemicals
Primary source of information for emergency responders such as firefighters or doctors
Hard copy or soft copy

## Slide 7: MATERIAL SAFETY DATA SHEET (msds)
There might be some little differences between MSDSs in details provided.
Some MSDSs will make the hazards very clear; for example, for acetone the MSDS might indicate “Danger! Extremely Flammable.” Other MSDSs might describe acetone’s hazards somewhat differently, such as “Flammable liquid and vapor. Vapor may cause flash fire.” It may have the ever-popular phrase “Harmful if swallowed or inhaled.”
In other cases, the hazard may not be as clearly explained. For instance, you may find under potential health effects, a section entitled “Inhalation” which explains that the inhalation of vapors irritates the respiratory tract or that exposure can cause respiratory tract and throat irritation. It is easy to deduce that this chemical is an irritant. But it may go further and say that overexposure or high concentrations may cause central nervous system depression, unconsciousness, respiratory failure, and death. These are toxic effects.

## Slide 8: MATERIAL SAFETY DATA SHEET (msds)
Learning From MSDS
After learning about the hazards of the chemical you will want to learn about specific procedures for safe handling. For example, it may state: “Keep away from heat, sparks, flames, or other sources of ignition.” MSDSs often contain special information for firefighters. For example, it may indicate that water is not effective in putting out fires involving this chemical. You will find a section that describes personal protective equipment (PPE) and exposure controls—eye protection, skin protection, and respiratory protection.
A significant problem with many MSDSs is that the PPE is not specific enough to be useful. For example, to protect your skin from exposure, the MSDS may indicate that you should use appropriate protective gloves—but of course you want to know which gloves are appropriate. Each specific chemical requires a specific kind of glove—there is no universal glove!
You will also find procedures that describe how to handle emergency situations, such as spills, but these directions are often not specific enough to be useful. For example, the recommendation to “follow state and local protocols” is accurate, but not helpful.

## Slide 9: THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION AND LABELLING OF CHEMICALS (GHS)
This section presents a brief overview of the United Nations’ Globally Harmonized System of Classification and Labelling of Chemicals (GHS) for defining and communicating hazard information and protective measures related to the physical, health, and environmental risks of chemicals through product labels and safety data sheets (SDSs).

## Slide 10: THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION AND LABELLING OF CHEMICALS (GHS)
An Incident: Isopropanol Explosion
A laboratory worker was preparing some samples using a procedure that involved isopropanol. When he finished he poured the excess isopropanol into a plastic bottle labeled “2-Propanol.” There was an immediate reaction and the container burst and sprayed its contents on the laboratory worker. He was startled, but managed to call for help. Nearby colleagues came to his aid and when he reported that his skin was burning they used an emergency eyewash and emergency shower to wash away the splash. He was taken to the university medical center for an evaluation and later released after being treated for acid burns. Investigators learned that the bottle had been mislabeled and actually contained concentrated nitric acid and some copper waste.

## Slide 11: THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION AND LABELLING OF CHEMICALS (GHS)
What Is the Globally Harmonized System for Classification and Labelling of Chemicals (GHS)?
Today’s marketplace is global and we receive and use foods, goods, and materials from countries all over the world. To improve the interactions of countries in the chemical industry, a consensus of nations under the purview of the United Nations has come together to develop a system for classifying and labelling hazardous chemicals so that all countries classify and label chemicals in the same way. This project is named the Globally Harmonized System for Classification and Labelling of Chemicals, or GHS.
In 1992 the United Nations Conference on Environment and Development in Rio de Janeiro adopted a mandate to develop GHS and by 2000 the initial system was formed. Designing an international system to classify and label chemicals has been a slow and complicated process and implementation of this system is still in progress. The first edition of GHS appeared in 2003. The document describing GHS is known as “The Purple Book” and it underwent revisions in 2005, 2007, 2009, 2013, and 2015.
GHS is an international system that incorporates MSDS-like documents, a standardized labelling system for chemicals, and the protocols for the determination of the hazard ratings.
Compliance with GHS is voluntary. Turkey has implemented GHS since 1 June 2015.

## Slide 12: GHS Hazard RatIngs
Table shows the 28 hazard classes by which chemicals are assessed in the GHS.
Each class has a unique relative rating system (categories) using letters, numbers, or other descriptions. In all cases the most hazardous classes have the lowest numerical rating or “A” and the least hazardous have higher numbers and subsequent letters.
The flammability rating system is deceptively similar to the NFPA (National Fire Protection Association) rating system for flammable liquids except that the rating systems are numerically reversed! The NFPA system ranks the least flammable as “0” and most flammable as “4.” This unfortunate lack of consistency will plague chemists and firefighters since the NFPA system is in widespread use in the United States.

## Slide 13: UsIng GHS
When you work in a laboratory, you can use GHS to help you assess the relative risk of handling hazardous chemicals. GHS will specify the format for MSDS-like documents that will contain the information shown below:
SDS (Safety Data Sheet):
1. Identification
2. Hazard(s) identification
3. Composition/information on ingredients
4. First aid measures
5. Firefighting measures
6. Accident release measures
7. Handling and storage
8. Exposure control/personal protection
9. Physical and chemical properties
10. Stability and reactivity
11. Toxicological information
12. Ecological information
13. Disposal considerations
14. Transport information
15. Regulatory information
16. Other information

## Slide 14: UsIng GHS
The format of labelling of chemicals will be standardized. Each label will contain a product identifier, a pictogram (symbol), a signal word, a hazard statement, and supplier information.
There are nine pictograms and two signal words—“danger” or “warning.” Some examples of hazard statements are
“May cause respiratory irritation,”
“Toxic in contact with skin,” and
“Heating may cause a fire or explosion.”

## Slide 15: UsIng GHS

## Slide 16: UsIng GHS