## Slide 1
Table 1.1. Classification of analytical methods by sample size
Method | Amount of Substance (mg)
Macro Semi-micro Micro Ultra-micro | > 100 10 – 100 1 – 100 < 1
The choice of analysis method can be the result of examining the differences between the classical methods and the instrumental methods, the advantages and limitations of the methods, and the relationship with the amount of matter.
Table 1.2. Characters of classical methods
Advantages | Limitations
The process is simple Accurate Usually based on absolute measurements No need to be very experienced The tools used are simple and inexpensive | It is not specific It takes a lot of time The accuracy decreases as the amount decreases Depends on working environment
Table 1.3. Characters of instrumental methods
Advantages | Limitations
Analysis is quick Few samples are used Complex examples can be used High sensitivity can be achieved Obtain accurate measurement | Initial and continuous calibration is required Sensitivity and accuracy depend on the device and calibration used The cost of processing is quite high Concentration range is limited Experienced analyst is needed
In the majority of analyzes, classical methods are used together with instrumental methods.

## Slide 2
2- Sampling
Substance level is often heterogeneous, sampling is more difficult. In this case, the sampling is done in two steps. First, the large sample is taken, it is picked up from various parts and then the sample is brought to the appropriate dimensions for the laboratory work, which is done by crushing, shredding and grinding.

## Slide 3
In order to reduce the amount of use suitable for use in the laboratory, the sample is spread in a thin layer and divided into four pieces, and two pieces are reciprocated and re-propagated.

## Slide 4
3- Protection of samples
Analysis of water samples should be done immediately, with time is the issue of disruption. Such specimens should be kept in deep freeze and protective additives should be added according to the substance to be determined.

## Slide 5
The time-lapse effect is even more pronounced in biological specimens. For example, proteins and enzymes change structure over time and should be analyzed without delay, otherwise protective precautions should be followed. Most solid samples are stable under normal conditions. More care must be taken when analyzing materials that change over time, such as analysis of radioactive samples.

## Slide 6
4- Preparing the sample for analysis
If the sample decomposes at this temperature, the adsorbed materials are removed by heating under lower pressure. If the solid sample needs to be analyzed by removing the crystal water, it is beneficial to heat the sample at higher temperatures. The solid sample is usually desired to be analyzed for analysis. For this, for example, the solver must be found. Water and strong acids are the most commonly used solvents.

## Slide 7
Some samples are slow to dissolve, which can be slowly heated in a water bath or on a low temperature heating plate after mixing with the sample solvent. Some solutes are insoluble in mineral acids, in which case the substance is heated with dissolving agents such as sodium carbonate, sodium peroxide, potassium bisulfate, potassium pyrosulfate, boric acid, borax, that is, melting is performed.

## Slide 8
It is always necessary to carry out analysis with more than one sample solution with the same characteristics, which is usually called parallel operation. Another sample preparation method practically used is preparing the stock solution. The stock solution is a solution in which the analyte concentration is greater than the analysis solution.

## Slide 9
The material is weighed sensitively and prepared by appropriate methods, obtained in the appropriate volume and stored. When the analysis is to be performed, the desired volume of the solutions is taken and the desired concentration is diluted and used as such.

## Slide 10
5- Analysis and evaluation of results
CA = k. X.
Where k is the proportionality coefficient. Apart from methods such as gravimetric and coulometric methods; concentration is calculated using known chemical standards, the presence of k is an important step in most of the analyzes and is known as the calibration process

## Slide 11
The calculation of the analyte concentration from the analysis results is generally simple. In the calculation, it is useful to consider the dilution steps applied in the analysis, the stoichiometric relationships of the chemical reactions or reactions during the analysis, and the measurement factors required for the device used. In order for the results of the analysis to be meaningful, the error made in the measurement must also be known and the errors are taken into account in the analysis results when given. In other words, we can outline the steps in the quantitative analysis as follows (Figure 1.1).

## Slide 12
Method selection
Sampling
Sample protection
Preparing sample for analysis
Analysis
Evaluation of results
Figure 1.1. Steps in a quantitative analysis