## Slide 1
The reason behind the SST analysis at different time interval is based on the concept that it should not be assumed that the system will behave properly throughout experiment..

## Slide 2
In addition to this, SST studies corresponding to compound of our interest is not enough to check system suitability because the system’s separation capacity is not investigated thoroughly. But, System Suitability Samples (SSSs) or resolution test mixtures of components of interest and expected impurities is required. For this reasons SSTs are analysed before and during testing

## Slide 3
The most important SST parameters which are investigated for different HPLC analysis is
*resolution (R),
*repeatability (RSD— relative standard deviations—of peak
response and retention time),
*column efficiency (N), and
*tailing factor (T).

## Slide 4
These parameters are possessing para amount interest as they indicate system specificity, precision, and column stability. Other parameters include capacity factor (k) and Signal-to-noise ratio (S/N) for impurity peaks.

## Slide 5
All most all HPLC data systems are based on the software dta system which can calculate the measurement and report of these SST parameters.

## Slide 6
Most “official” analytical methods has fixed the acceptance criteria or SST limits which may vary with different tests and are typically less stringent for biologics and trace impurities.

## Slide 7
Table 1: SST limits for HPLC chromatogram according to different guidelines.
SST limits | CDER guidelines | Hsu and Chien recommendation
Repeatability of peak response | ≤1.0% for 5 | ≤1.5% general 5–15% trace <5% biologics
Resolution | >2.0 general | >2.0 general >1.5 quantization
Tailing factor | ≤2.0 | <1.5–2.0
Column efficiency | >2000 (plate count) | Not available
Capacity factor | >2 | 2–8

## Slide 8
Setting limits
SST limits should emphasize the minimum criterion rather than optimal values. Analytical methods simply adopted the general limits from the CDER guidance document [2]. Different guidelines related to SST limits are shown (Table 1)