## Slide 1
Using Mass as a Signal
There are two ways to use mass as an analytical signal. We can, of course, measure an analyte’s mass directly by placing it on a balance and recording its mass. For example, determination of the total suspended solids in water released from a sewage-treatment facility.

## Slide 2
Suspended solids are just that; solid matter that has yet to settle out of its solution matrix. The analysis is easy. A sample collects and passes it through a preweighed filter that retains the suspended solids. After drying to remove any residual moisture, the filter weighs. The difference between the filter’s original mass and final mass gives the mass of suspended solids. It is a direct analysis because the analyte itself is the object being weighed.

## Slide 3
If the analyte is an aqueous ion, such as Pb2+, we cannot isolate the analyte by filtration because the Pb2+ is dissolved in the solution’s matrix. We can still measure the analyte’s mass, however, by chemically converting it to a solid form. If we suspend a pair of Pt electrodes in our solution and apply a sufficiently positive potential between them for a long enough time, we can force the reaction to go to completion.
Pb2+ + 4H2O « PbO2 + H2 + 2H3O+

## Slide 4
The Pb2+ ion in solution oxidizes to PbO2 and deposits on the Pt electrode serving as the anode. If we weigh the Pt anode before and after applying the potential, the difference in the two measurements gives the mass of PbO2 and, from the reaction’s stoichiometry, the mass of Pb2+. This also is a direct analysis because the material being weighed contains the analyte.

## Slide 5
Sometimes it is easier to remove the analyte and use a change in mass as the analytical signal. For example, determine a food’s moisture content by a direct analysis. One possibility is to heat a sample of the food to a temperature at which the water in the sample vaporizes.

## Slide 6
If we capture the vapor in a preweighed absorbent trap, then the change in the absorbent’s mass provides a direct determination of the amount of water in the sample. An easier approach, however, is to weigh the sample of food before and after heating, using the change in its mass as an indication of the amount of water originally present. This technique calls an indirect analysis since we determine the analyte by a signal representing its disappearance.

## Slide 7
The indirect determination of moisture content in foods is done by difference. The sample’s initial mass includes the water, whereas the final mass is measured after removing the water.

## Slide 8
We can also determine an analyte indirectly without its ever being weighed. Again, as with the determination of Pb2+ as PbO2, we take advantage of the analyte’s chemistry. For example, phosphite, PO33–, reduces Hg2+ to Hg22+. In the presence of Cl– a solid precipitate of Hg2Cl2 forms.