## Slide 1: CONDUCTOMETRY

## Slide 2: Conductivity
Conductivity is the measure of A material's ability to transmit electrical current.
C = 1 / R.
Unit of conductivity is S.m-1.

## Slide 3: ConductIvIty of water
Theoretically, pure water does not transmit electric current. Hence it does not contain ions.
But in practice, even pure water has a concutivity value.
Whether or not a water is pure can be understood by looking at the conductivity value.

## Slide 4: ConductIvIty of water
For example, when the conductivity of ultrapure water is 0.055 μS / cm and the conductivity of distilled water is about 0.5 μS / cm, this value is around 56000 μS / cm in seawater.

## Slide 5: Conductometer
The analysis method based on the conductivity changes in the solution is called conductivity measurement (conductometry). The means used to measure conductivity is called a conductometer.

## Slide 6: Conductometer
Conductometer consist of an electrical source, a conductivity cell in which the analysis solution is located, and a resistance meter.
Platinum electrodes coated with platinum black are usually used in the conductivity cell.

## Slide 7: ConductometrIc tItratIon
The concentration of the unknown concentration (analyte) is the type of titration in which the turning point is determined by using the changes in conductivity during the reaction with the known titrant.

## Slide 8: ConductometrIc tItratIon
Conductometric titration is one of the most suitable methods which are widely used in the analysis of dark colored or unclear solutions and in precipitation reactions.