## Slide 1: THERMAL ANALYSIS

## Slide 2
In the pharmaceutical sciences, only a handful of the techniques are commonly employed but the information gained and phenomena that can be explored are countless.

## Slide 3
The primary workhorses in the pharmaceutical sciences include, differential scanning calorimetry (DSC), thermogravimetric analysis (TGA), differential thermal analysis (DTA) and dynamic mechanical analysis (DMA).

## Slide 4
The first will be thermal analytical methods commonly used in the pharmaceutical sciences, primarily DSC (including several specialized techniques) and TGA.

## Slide 5
The second will focus on applications in the pharmaceutical sciences including solid-state characterization of polymorphism, solid dispersions and polymeric dosage forms.

## Slide 6
(DSC)
If any laboratory, ranging from the pharmaceutical industry to academic research, were to purchase only one piece of thermal analysis equipment it would most likely be a DSC. These instruments are available from several manufacturers in a wide range of price and applications. Instruments are available from simple robust DSC’s with robotics and high-throughput capabilities for screening and quality control, to high-end, extremely sensitive instruments for research applications.

## Slide 7
Initially the term heat-flux DSC was used to describe quantitative DTA instruments [4]. Today it is commonly referred to as a DSC method. This development was an improvement over DTA in that it allowed for a measurement in the changes in heat flow as opposed to temperature only.

## Slide 8
By measuring the heat capacity of the heat sensitive plate as a function of temperature during the manufacturing process, an estimate of the enthalpy of transition can be made from the incremental temperature fluctuations [4].