## Slide 1: EEE322 COMMUNICATION THEORY – I
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: EEE322 COMMUNICATION THEORY - I
LECTURE 1
INTRODUCTION TO COMMUNICATION SYSTEMS

## Slide 3: Communication system with input and output transducers (Fig.1.1-1 Carlson, page 3)
Information (message) transfer
  Analog messages: degree of fidelity in analog communication systems
  Digital messages: degree of accuracy in digital communication systems

## Slide 4: Elements of a communication system (Fig.1.1-2 Carlson, page 4)
Transmitter: modulation, source coding, channel coding
Transmission channel: loss (attenuation), noise, interference distortion
Receiver: demodulation, source decoding, channel decoding

## Slide 5: Contamination of a signal transmitting a 1101001 sequence (a) original signal as it leaves the transmitter (b) effects of distortion (c) effects of interference (d) effects of noise (Fig.1.1-3 Carlson, page 5)
Unwanted (corrupting) effects:
  Noise
  Interference
  Distortion

## Slide 6: Fundamental limitations
Technological problems
Fundamental pyhsical limitations:
  Bandwidth
  Noise
  Shannon (1948) stated that the rate of information transmission can not exceed the channel capacity (Hartley-Shannon Law):

## Slide 7: Modulation
Modulation is defined as the process by which some characteristic of a carrier wave is varied in accordance with an information bearing signal (also called message signal) (Haykin, page 100).
Modulation benefits:
  Efficient transmission (reduces antenna dimensions)
  Overcome hardware limitations
  Reduce noise and interference
  Frequency assignment
  Multiplexing

## Slide 8: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.