## Slide 1: EEE322 COMMUNICATION THEORY – I
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: EEE322 COMMUNICATION THEORY - I
LECTURE 13
DIGITAL CONTINUOUS WAVE MODULATION:
AMPLITUDE MODULATION METHODS (ASK, QAM)

## Slide 3
DIGITAL CONTINUOUS WAVE MODULATION
A digital signal can modulate the amplitude, frequency, or phase of a sinusoidal carrier wave.
If the modulating waveform consists of NRZ rectangular pulses, then the modulated parameter will be switched or keyed from one discrete value to another.
Figure 14.1–1 (Carlson, page 649) illustrates binary amplitude-shift keying (ASK), frequency-shift keying (FSK), and phase-shift keying (PSK)

## Slide 4
DIGITAL CONTINUOUS WAVE MODULATION
Spectral Analysis of Bandpass Digital Signals
Any modulated bandpass signal may be expressed in the quadrature-carrier form
The carrier frequency , amplitude , and phase are constant.
The timevarying i (in-phase) and q (quadrature) components contain the message.

## Slide 5
DIGITAL CONTINUOUS WAVE MODULATION
Spectral Analysis of Bandpass Digital Signals
The power spectrum of
where and are the power spectra of the i and q components.

## Slide 6
DIGITAL CONTINUOUS WAVE MODULATION
Spectral Analysis of Bandpass Digital Signals
We define the equivalent lowpass spectrum

## Slide 7
DIGITAL CONTINUOUS WAVE MODULATION
Spectral Analysis of Bandpass Digital Signals
The bandpass spectrum is obtained from the equivalent lowpass spectrum by simple frequency translation.

## Slide 8
DIGITAL CONTINUOUS WAVE MODULATION
Spectral Analysis of Bandpass Digital Signals
The i component is an M-ary digital signal:
where represents a sequence of source digits with rate

## Slide 9
DIGITAL CONTINUOUS WAVE MODULATION
Amplitude Modulation Methods
The binary ASK waveform illustrated in Fig. 14.1–1a (Carlson, page 649) could be generated simply by turning the carrier on and off, a process described as on-off keying (OOK).
In general, an M-ary ASK waveform has M -1 discrete “on’’ amplitudes as well as the “off’’ state.

## Slide 10
DIGITAL CONTINUOUS WAVE MODULATION
Amplitude Modulation Methods
We can set the q component of equal to zero and take the i component to be a unipolar NRZ signal, namely

## Slide 11
DIGITAL CONTINUOUS WAVE MODULATION
Amplitude Modulation Methods
The mean and variance of the digital sequence are

## Slide 12
DIGITAL CONTINUOUS WAVE MODULATION
Amplitude Modulation Methods
The equivalent lowpass spectrum:
Figure 14.1–2 (Carlson, page 651) shows the resulting bandpass spectrum

## Slide 13
DIGITAL CONTINUOUS WAVE MODULATION
Amplitude Modulation Methods
If an M-ary ASK signal represents binary data at rate then
/

## Slide 14
DIGITAL CONTINUOUS WAVE MODULATION
Amplitude Modulation Methods
Quadrature carrier AM (QAM) achieves twice the modulation speed of binary ASK.
Figure 14.1–3a depicts the functional blocks of a binary QAM transmitter with a polar binary input at rate
The serial-to-parallel converter divides the input into two streams consisting of alternate bits at rate /2.

## Slide 15
DIGITAL CONTINUOUS WAVE MODULATION
Amplitude Modulation Methods
The i and q modulating signals:
where and .

## Slide 16
DIGITAL CONTINUOUS WAVE MODULATION
Amplitude Modulation Methods
The i and q components are independent but they have the same pulse shape and the same statistical values, namely Thus,

## Slide 17
DIGITAL CONTINUOUS WAVE MODULATION
Amplitude Modulation Methods
Binary QAM achieves because the dibit rate equals one-half of the input bit rate, reducing the transmission bandwidth to

## Slide 18: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.