## Slide 1: ELE322 COMMUNICATION THEORY – I
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: ELE322 COMMUNICATION THEORY - I
LECTURE 7
CONTINUOUS WAVE MODULATION:
SINGLE SIDE BAND AMPLITUDE MODULATION (SSB AM)
VESTIGIAL SIDE BAND AMPLITUDE MODULATION (VSB AM)

## Slide 3
SUPPRESSED-SIDEBAND AMPLITUDE MODULATION
Conventional amplitude modulation is wasteful of both transmission power and bandwidth. Suppressing the carrier reduces the transmission power.
Suppressing one sideband, in whole or part, reduces transmission bandwidth and leads to single-sideband modulation (SSB) or vestigial sideband modulation (VSB) discussed in this section.

## Slide 4
SUPPRESSED-SIDEBAND AMPLITUDE MODULATION
SSB Signals and Spectra:
The upper and lower sidebands of DSB are uniquely related by symmetry about the carrier frequency, so either one contains all the message information.
Figure 4.4–1a (Carlson, page 186) presents a conceptual approach to single-sideband modulation.

## Slide 5
SUPPRESSED-SIDEBAND AMPLITUDE MODULATION
SSB Signals and Spectra:
The DSB signal from a balanced modulator is applied to a sideband filter that suppresses one sideband.
If the filter removes the lower sideband, the output spectrum consists of the upper sideband alone, as illustrated by Fig. 4.4–1b.

## Slide 6
SUPPRESSED-SIDEBAND AMPLITUDE MODULATION
VSB Signals and Spectra:
Bandwidth conservation argues for the use of SSB, but practical SSB systems have poor low-frequency response.
On the other hand, DSB works quite well for low message frequencies but the transmission bandwidth is twice that of SSB.
Clearly, a compromise modulation scheme is desired; that compromise is VSB.

## Slide 7
SUPPRESSED-SIDEBAND AMPLITUDE MODULATION
VSB Signals and Spectra:
VSB is derived by filtering DSB (or AM) in such a fashion that one sideband is passed almost completely while just a trace, or vestige, of the other sideband is included.
The key to VSB is the sideband filter, a typical transfer function being that of Fig. 4.4–8a (Carlson, page 192).

## Slide 8: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.