## Slide 1: ELE322 COMMUNICATION THEORY – I
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: ELE322 COMMUNICATION THEORY - I
LECTURE 10
PULSE MODULATION:
SAMPLING THEOREM
ANALOG PULSE AMPLITUDE MODULATION

## Slide 3
Sampling Theory
Chopper Sampling:
A simple but highly informative approach to sampling theory comes from the switching operation of Fig. 6.1–1a (Carlson, page 259).
The switch periodically shifts between two contacts at a rate of fs =1/Ts Hz, dwelling on the input signal contact for seconds and on the grounded contact for the remainder of each period.

## Slide 4
Sampling Theory
Chopper Sampling:
The output then consists of short segments for the input x(t), as shown in Fig. 6.1–1b (Carlson, page 259).
Figure 6.1–1c (Carlson, page 259) is an electronic version of Fig. 6.1–1a (Carlson, page 259); the output voltage equals the input voltage except when the clock signal forward-biases the diodes and thereby clamps the output to zero.

## Slide 5
Sampling Theory
Chopper Sampling:
We introduce a switching function s(t) such that
Thus the sampling operation becomes multiplication by s(t), as indicated schematically in Fig. 6.1–2a (Carlson, page 260), where s(t) is nothing more than the periodic pulse train of Fig. 6.1–2b.

## Slide 6
Sampling Theory
Chopper Sampling:
Since s(t) is periodic, it can be written as a Fourier series.
where

## Slide 7
Sampling Theory
Chopper Sampling:
cos
If the input message spectrum is , the output spectrum is

## Slide 8
Sampling Theory
Chopper Sampling:
Two conditions are necessary to prevent overlapping spectral bands:
the message must be bandlimited
the sampling frequency must be sufficiently great that

## Slide 9
Sampling Theory
Chopper Sampling:
The minimum sampling frequency or in the case of sinusoidal signals is called the Nyquist rate.
If sample frequency is fs =2W it is possible for the sine wave to be sampled at its zero crossings; thus, the samples would be equal to zero, and reconstruction would not be possible.

## Slide 10
Sampling Theory
Ideal Sampling and Reconstruction
Ideal sampling is instantaneous sampling.
The sampled wave becomes a train of impulses whose areas equal the instantaneous sample values of the input signal.

## Slide 11
Sampling Theory
Ideal Sampling and Reconstruction
The rectangular pulse train:
Ideal sampling function:

## Slide 12
Sampling Theory
Ideal Sampling and Reconstruction
The ideal sampled wave:
The corresponding spectrum :

## Slide 13
Sampling Theory
Ideal Sampling and Reconstruction
If a signal contains no frequency components for , it is completely described by instantaneous sample values uniformly spaced in time with period 1/2W.
If a signal has been sampled at the Nyquist rate or greater (fs 2W) and the sample values are represented as weighted im-pulses, the signal can be exactly reconstructed from its samples by an ideal LPF of bandwidth B, where

## Slide 14
Analog Pulse Amplitude Modulation
If a message waveform is adequately described by periodic sample values, it can be transmitted using analog pulse modulation wherein the sample values modulate the amplitude of a pulse train.
This process is called pulse-amplitude modulation (PAM).
An example of a message waveform and corresponding PAM signal are shown in Fig. 6.2–1 (Carlson, page 273).

## Slide 15
Analog Pulse Amplitude Modulation
Flat-Top Sampling and PAM:
Although a PAM wave could be obtained from a chopper circuit, a more popular method employs the sample-and-hold (S/H) technique.
This operation produces flat-top pulses, as in Fig. 6.2–1 (Carlson, page 273), rather than curved-top chopper pulses.

## Slide 16
Analog Pulse Amplitude Modulation
Flat-Top Sampling and PAM:
Periodic gating of the sample-and-hold circuit generates the sampled wave:
)
where

## Slide 17
Analog Pulse Amplitude Modulation
Flat-Top Sampling and PAM:
Fourier transformation of this convolution operation yields

## Slide 18
Analog Pulse Amplitude Modulation
Flat-Top Sampling and PAM:
The high-frequency rolloff characteristic of a typical P(f) acts like a lowpass filter and attenuates the upper portion of the message spectrum.
This loss of high frequency content is called aperture effect.

## Slide 19
Analog Pulse Amplitude Modulation
Flat-Top Sampling and PAM:
Required transmission bandwidth:

## Slide 20: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.