## Slide 1: ELE322 COMMUNICATION THEORY – I
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: ELE322 COMMUNICATION THEORY - I
LECTURE 12
PULSE CODE MODULATION,
TIME DIVISION MULTIPLEXING

## Slide 3
Pulse-Code Modulation
PCM is a digital transmission system with an analog-to-digital converter (ADC) at the input and a digital-to-analog converter (DAC) at the output.

## Slide 4
Pulse-Code Modulation
PCM Generation and Reconstruction
Figure 12.1–1a (Carlson, page 545) diagrams the functional blocks of a PCM generation system.
The analog input waveform x(t) is lowpass filtered and sampled to obtain .
A quantizer rounds off the sample values to the nearest discrete value in a set of q quantum levels.
The resulting quantized samples are discrete in time and discrete in amplitude

## Slide 5
Pulse-Code Modulation
PCM Generation and Reconstruction
Let the analog message be a voltage waveform normalized such that
Uniform quantization subdivides the 2-V peak-to-peak range into q equal steps of height V, as shown in Fig. 12.1–1b (Carlson, page 545).
The normalized quantization-level step size can thus be defined as .

## Slide 6
Pulse-Code Modulation
PCM Generation and Reconstruction
Next, an encoder translates the quantized samples into digital code words.
The encoder works with M-ary digits and produces for each sample a codeword consisting of n digits in parallel.
Since there are possible M-ary codewords with n digits per word, unique encoding of the q different quantum levels requires that .

## Slide 7
Pulse-Code Modulation
PCM Generation and Reconstruction
The parameters M, n, and q should be chosen to satisfy the equality, so that
Thus, the number of quantum levels for binary PCM must equal some power of 2, namely .

## Slide 8
Pulse-Code Modulation
PCM Generation and Reconstruction
Finally, successive codewords are read out serially to constitute the PCM waveform, an M-ary digital signal.
The PCM generator acts as an ADC, performing analog-to-digital conversions at the sampling rate

## Slide 9
Pulse-Code Modulation
PCM Generation and Reconstruction
Each encoded sample is represented by a n-digit output word, so the signaling rate becomes
with

## Slide 10
Pulse-Code Modulation
PCM Generation and Reconstruction
The bandwidth needed for PCM baseband transmission:

## Slide 11
Pulse-Code Modulation
PCM Generation and Reconstruction
Fine-grain quantization for accurate reconstruction of the message waveform requires , which increases the transmission bandwidth by the factor times the message bandwidth W.

## Slide 12
Pulse-Code Modulation
PCM Generation and Reconstruction
A PCM receiver with the reconstruction system in Fig. 12.1–2a (Carlson, page 547).
The received signal may be contaminated by noise, but regeneration yields a clean and nearly errorless waveform if is sufficiently large.
The DAC operations of serial-to-parallel conversion, M-ary decoding, and sample-and-hold generate the analog waveform xq(t) drawn in Fig. 12.1–2b (Carlson, page 547).
Lowpass filtering then produces the smoothed output signal.

## Slide 13
Pulse-Code Modulation
Quantization Noise
The ADC operation at the transmitter introduces permanent errors that appear at the receiver as quantization noise in the reconstructed signal.

## Slide 14
Pulse-Code Modulation
Quantization Noise
A pulse converter in place of the sample-and-hold circuit generates the weighted impulse train:
)
where represents the quantization error, namely
=

## Slide 15
Pulse-Code Modulation
Quantization Noise
Lowpass filtering with yields the final output
This expression has the same form as reconstruction of analog pulse modulation with noisy samples

## Slide 16
Pulse-Code Modulation
Quantization Noise
The quantization noise power

## Slide 17
Pulse-Code Modulation
Quantization Noise
The destination signal-tonoise ratio:

## Slide 18
Pulse-Code Modulation
Quantization Noise
A more informative relation for binary PCM is obtained by setting and expressing in decibels.

## Slide 19: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.