## Slide 1: ELE427 COMMUNICATION THEORY – II
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: ELE427 COMMUNICATION THEORY - II
LECTURE 4
NOISE EFFECT ON BASEBAND TRANSMISSION:
ADDITIVE NOISE AND SIGNAL-TO-NOISE RATIO

## Slide 3
Additive Noise and Signal-to-Noise Ratios
Noise often adds to the information-bearing signal at various points between the source and the destination.
For purposes of analysis, all the noise will be lumped into one source added to the signal at the input of the receiver.

## Slide 4
Additive Noise and Signal-to-Noise Ratios
Figure 9.4–1 (Carlson, page 423) diagrams our model of additive noise.
This model emphasizes the fact that the most vulnerable point in a transmission system is the receiver input where the signal level has its weakest value.

## Slide 5
Additive Noise and Signal-to-Noise Ratios
Since the receiver is presumed to be linear, its combined input produces output signal plus noise at the destination.
Accordingly, we write the output waveform as
where and stand for the signal and noise waveforms at the destination.

## Slide 6
Additive Noise and Signal-to-Noise Ratios
The total output power is then found by averaging

## Slide 7
Additive Noise and Signal-to-Noise Ratios
To calculate this average, we’ll treat the signal as a sample function of an ergodic process and we’ll make two reasonable assumptions about additive noise:
The noise comes from an ergodic source with zero mean and power spectral density .
The noise is physically independent of the signal and therefore uncorrelated with it.

## Slide 8
Additive Noise and Signal-to-Noise Ratios
Under these conditions the statistical average of the crossproduct equals zero because and are incoherent.
Thus, the statistical average of yields
which states that we have superposition of signal and noise power at the destination.

## Slide 9
Additive Noise and Signal-to-Noise Ratios
Let’s underscore the distinction between desired signal power and unwanted noise power by introducing the notation
so that

## Slide 10
Additive Noise and Signal-to-Noise Ratios
The signal-to-noise ratio (SNR) will now be defined as the ratio of signal power to noise power, symbolized by
and often expressed in decibels.
This ratio provides an important and handy indication of the degree to which the signal has been contaminated with additive noise.

## Slide 11
Additive Noise and Signal-to-Noise Ratios
For analytic work, we generally take the case of white noise with .
If the receiver has gain and noise bandwidth , the destination noise power becomes

## Slide 12
Additive Noise and Signal-to-Noise Ratios
When the noise has a gaussian distribution, this case is called additive white gaussian noise (AWGN), which is often the assumed model.

## Slide 13: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.