## Slide 1: ELE427 COMMUNICATION THEORY – II
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: ELE427 COMMUNICATION THEORY - II
LECTURE 6
NOISE EFFECT ON BASEBAND TRANSMISSION:
ANALOG REPEATERS
ERROR RATE
REGENERATIVE REPEATERS

## Slide 3
Regenerative Repeaters
Long-haul transmission requires repeaters, be it for analog or digital communication.
But unlike analog-message repeaters, digital repeaters can be regenerative.

## Slide 4
Regenerative Repeaters
If the error probability per repeater is reasonably low and the number of hops m is large, the regeneration advantage turns out to be rather spectacular.
This will be demonstrated for the case of polar binary transmission.

## Slide 5
Regenerative Repeaters
When analog repeaters are used and Eq. (11), Sect. 9.4 applies, the final signal-to- noise ratio is and
Where is the signal-to-noise ratio after one hop.

## Slide 6
Regenerative Repeaters
Therefore, the transmitted power per repeater must be increased linearly with m just to stay even, a factor not to be sneezed at since, for example, it takes 100 or more repeaters to cross the continent.

## Slide 7
Regenerative Repeaters
In contrast, a regenerative repeater station consists of a complete receiver and transmitter back to back in one package.
The receiving portion converts incoming signals to message digits, making a few errors in the process; the digits are then delivered to the transmitting portion, which in turn generates a new signal for transmission to the next station.
The regenerated signal is thereby completely stripped of random noise but does contain some errors.

## Slide 8
Regenerative Repeaters
To analyze the performance, let α be the error probability at each repeater, namely,
assuming identical units.

## Slide 9
Regenerative Repeaters
As a given digit passes from station to station, it may suffer cumulative conversion errors.
If the number of erroneous conversions is even, they cancel out, and a correct digit is delivered to the destination.

## Slide 10
Regenerative Repeaters
The probability of i errors in m successive conversions is given by the binomial frequency function,

## Slide 11
Regenerative Repeaters
Since we have a destination error only when i is odd,

## Slide 12
Error Rate
We can easily account for the signaling-rate difference when the message bits are encoded in blocks of length
To relate the M-ary symbol error probability Pe to the resulting error probability per bit, we’ll assume a Gray code and a reasonably large signal-to-noise ratio.

## Slide 13
Error Rate
Under these conditions a noise excursion seldom goes beyond one amplitude level in the M-ary waveform, which corresponds to just one erroneous bit in the block of bits.
Therefore,
where stands for the equivalent bit error probability, also called the bit error rate (BER).

## Slide 14: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.