## Slide 1: ELE427 COMMUNICATION THEORY – II
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: ELE427 COMMUNICATION THEORY - II
LECTURE 10
PCM AND PREDICTIVE CODING:
LINEAR PREDICTIVE CODING (LPC)

## Slide 3
LPC Speech Synthesis
Linear predictive coding (LPC) is a novel approach to digital representation of analog signals.
The method uses a transversal filter (or its digital-circuit equivalent) plus some auxiliary components to synthesize the waveform in question.

## Slide 4
LPC Speech Synthesis
The parameters of the waveform synthesizer are then encoded for transmission, instead of the actual signal.
Considerable efficiency results if the synthesizer accurately mimics the analog process.
Since there already exists extensive knowledge about speech processes, LPC is particularly well suited to speech synthesis and transmission.

## Slide 5
LPC Speech Synthesis
Figure 12.3–9 (Carlson, page 569) diagrams a speech synthesizer consisting of two input generators, a variable-gain amplifier, and a transversal filter in a feedback loop.
The amplifier gain and filter tap gains are adjusted to model the acoustical properties of the vocal tract.

## Slide 6
LPC Speech Synthesis
Unvoiced speech (such as hissing sound) is produced by connecting the white-noise generator.
Voiced speech is produced by connecting the impulse-train generator set at an appropriate pitch frequency.

## Slide 7
LPC Speech Synthesis
If the filter has about 10 tap gains, and all parameter values are updated every 10 to 25 ms, the synthesized speech is quite intelligible, although it may sound rather artificial, like a robot.
Some talking toys and recorded-message systems generate speech sounds by the synthesis method, drawing upon parameter values stored in a digital memory.

## Slide 8
LPC Speech Synthesis
Systems that generate speech in this manner are called vocoders.
An alternative to vocoders are waveform encoders where a given algorithm such as PCM is employed to replicate a given speech signal.

## Slide 9
LPC Speech Synthesis
Now consider the LPC transmitter of Fig. 12.3–10a.
Sample values of voice input are analyzed to determine the parameters for the synthesizer, whose output is compared with the input.

## Slide 10
LPC Speech Synthesis
The resulting error is encoded along with the parameter values to form the transmitted digital signal.
The receiver in Fig. 12.3–10b (Carlson , page 570) uses the parameter values and quantized error to reconstruct the voice waveform.

## Slide 11
LPC Speech Synthesis
A complete LPC codeword consists of 80 bits—1 bit for the voiced/unvoiced switch, 6 bits for the pitch frequency, 5 for the amplifier gain, 6 for each of the 10 tap gains, and a few bits for the error.
Updating the parameters every 10–25 ms is equivalent to sampling at 40–100 Hz, so LPC requires a very modest bit rate in the vicinity of 3000 to 8000 bps.
Table 12.3–1 (Carlson , page 571) compares LPC with other voice encoding methods.

## Slide 12
LPC Speech Synthesis
The substantial bit-rate reduction made possible by LPC has stimulated efforts to improve the quality of speech synthesis for voice communication.
In fact, as shown in Table 12.3–1 (Carlson , page 571), using LPC we can compress speech from a 56 kbps to 3 kbps rate.

## Slide 13: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.