## Slide 1: ELE427 COMMUNICATION THEORY – II
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: ELE427 COMMUNICATION THEORY - II
LECTURE 11
ERROR CONTROL CODING:
ERROR DETECTION AND CORRECTION (HAMMING DISTANCE, ARQ AND FEC STRATEGIES)

## Slide 3
ERROR DETECTION AND CORRECTION
Coding for error detection, without correction, is simpler than error-correction coding.
When a two-way channel exists between source and destination, the receiver can request retransmission of information containing detected errors.

## Slide 4
ERROR DETECTION AND CORRECTION
This error-control strategy, called automatic-repeat-request (ARQ), particularly suits data communication systems such as computer networks.
However, when retransmission is impossible or impractical, error control must take the form of forward error correction (FEC) using an error-correcting code.

## Slide 5
Repetition and Parity-Check Codes
When we try to talk to someone across a noisy room, we may need to repeat ourselves to be understood.
A brute-force approach to binary communication over a noisy channel likewise employs repetition, so each message bit is represented by a codeword consisting of n identical bits.
Any transmission error in a received codeword alters the repetition pattern by changing a 1 to a 0 or vice versa.

## Slide 6
Repetition and Parity-Check Codes
If transmission errors occur randomly and independently with probability Pe = a, then the binomial frequency function gives the probability of i errors in an nbit codeword as
,

## Slide 7
Repetition and Parity-Check Codes
Consider, for instance, a triple-repetition code with codewords 000 and 111.
All other received words, such as 001 or 101, clearly indicate the presence of errors.
Depending on the decoding scheme, this code can detect or correct erroneous words.

## Slide 8
Repetition and Parity-Check Codes
For error detection without correction, we say that any word other than 000 or 111 is a detected error.
Single and double errors in a word are thereby detected, but triple errors result in an undetected word error with probability

## Slide 9
Repetition and Parity-Check Codes
For error correction, we use majority-rule decoding based on the assumption that at least two of the three bits are correct.
Thus, 001 and 101 are decoded as 000 and 111, respectively.

## Slide 10
Repetition and Parity-Check Codes
This rule corrects words with single errors, but double or triple errors result in a decoding error with probability

## Slide 11
Repetition and Parity-Check Codes
More efficient codes are based on the notion of parity.
The parity of a binary word is said to be even when the word contains an even number of 1s, while odd parity means an odd number of 1s.

## Slide 12
Repetition and Parity-Check Codes
The codewords for an error-detecting parity-check code are constructed with n - 1 message bits and one check bit chosen such that all codewords have the same parity.
With n=3 and even parity, the valid codewords are 000, 011, 101, and 110, the last bit in each word being the parity check.

## Slide 13
Repetition and Parity-Check Codes
When a received word has odd parity, 001 for instance, we immediately know that it contains a transmission error—or three errors or, in general, an odd number of errors.
Error correction is not possible because we don’t know where the errors fall within the word.
Furthermore, an even number of errors preserves valid parity and goes unnoticed.

## Slide 14
Repetition and Parity-Check Codes
As an example of parity checking for error correction, Fig. 13.1–1 (Carlson, page 594) illustrates an error-correcting scheme in which the codeword is formed by arranging k message bits in a square array whose rows and columns are checked by parity bits.
A transmission error in one message bit causes a row and column parity failure with the error at the intersection, so single errors can be corrected.
This code also detects double errors.

## Slide 15
Code Vectors and Hamming Distance
Rather than continuing a piecemeal survey of particular codes, we now introduce a more general approach in terms of code vectors.
An arbitrary n-bit codeword can be visualized in an n-dimensional space as a vector whose elements or coordinates equal the bits in the codeword.

## Slide 16
Code Vectors and Hamming Distance
We thus write the codeword 101 in row-vector notation as X=(1 0 1).
Figure 13.1–3 (Carlson, page 594) portrays all possible 3-bit codewords as dots corresponding to the vector tips in a three-dimensional space.
The solid dots in part (a) represent the triple-repetition code, while those in part (b) represent a parity-check code.

## Slide 17
Code Vectors and Hamming Distance
Notice that the triple-repetition code vectors have greater separation than the parity-check code vectors.
This separation, measured in terms of the Hamming distance, has direct bearing on the error-control power of a code.

## Slide 18
Code Vectors and Hamming Distance
The Hamming distance d(X, Y) between two vectors X and Y is defined to equal the number of different elements.
For instance, if X (1 0 1) and Y (1 1 0) then d(X, Y) 2 because the second and third elements are different.

## Slide 19: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.